## Slide 1: Injection facility for Novosibirsk Super Charm Tau Factory
Dmitriy Berkaev
Budker Institute of Nuclear Physics SB RAS

## Slide 2: Super-CT Project
Thermionic
Gun
Polarized e- Gun
e- Photogun
1 nC, 3 ps
ΔE/E ~ 0.5 %
(total charge)
e- 1 GeV + 1.5 Gev Linacs
AS – 16 + 24
Klystron – 8 + 12
Length – 72 m + 96 m
e- 1.5 GeV Linac
AS – 24
Klystrons – 12
Length – 96 m
e+ 1.5 GeV Linac
AS – 24
Klystrons – 12
Length – 96 m
Damping Ring
e+ 1 – 1.5 GeV
1 GeV Linac
AS – 16
Klystrons – 8
Length – 72 m
Debuncher
Compressor
Damping
Wiggler
IP
RF System
Damping
Wiggler
Damping
Wiggler
Damping
Wiggler
Siberian
Snake
Crab
Sext
Crab
Sext
RF photogun: beam charge is 1 nC, laser length is 266 nm, laser energy is up to 3 mJ, laser pulse length is not more 10 ps, metallic cathode, beam energy is at least 5 MeV, beam energy spread for
total charge is not more 0.5%, rms beam length is about 1 mm (3 ps)
Accelerating structure: TW, constant impedance (geometry), length is 3 m, quasi-constant electric field distribution, energy gain is 22 MeV/m, beam energy per structure is 66 MeV
Klystron: peak power is 50 MW, repetition rate is 50 Hz, pulse length is up to 5 μs
RF module: 1 klystron, 2 accelerating strictures, electric field amplitude is 27 MV/m, gap between structures is 1 m
Thermionic gun: pulse length is up to 10 ns, peak current is about 8 A
Total number of accelerating structures: 104
Klystron number: 52
Total length of the linacs: ~440 m
Drift channel for 1.5 GeV mode

## Slide 3: Location of the new Facility
BINP Main Building
VEPP-2000
Collider
VEPP-4M
Collider
SCT Injector
SCT Factory

## Slide 4: Accelerating Module
Control Module
RF Amplifier
Modulator
Klystron
SLED
RF Load
Acceleration
Structure
23 MeV/m
134 MeV/module

## Slide 5: Accelerating Structure
Accelerating Cell
The Structure at the Testing Stand (2018)
Total number of accelerating structures: 104

## Slide 6: “5045 SLAC” Klystron
Cathode Module
Resonators
Drift Tube with Collector
Focusing Solenoid
Parameters:
50 MW
2856 MHz
5 mks
50 Hz
Klystron number: 52
RF Windows

## Slide 7: Modulator
High Voltage Module
HV Transformer
HV Transformer Tank
Modulator number: 52

## Slide 8: Start of the acceleration…
e- gun
Compressor (buncher)
module with solenoid
First section
with solenoid
SLED
Klystron
Modulator

## Slide 9: Conversion system
Positron
Production
Target
Flux Concentrator

## Slide 10: VEPP-5 Injection Complex at BINP
Number of е- at the conversion system per pulse – 3.5∙1010
Energy of е- at the conversion system – 270 MeV
Energy of e+ at the end of Linac – 400 MeV
Number of e+ per pulse at the end of Linac – 3.5∙109
In operation and since the end of 2015 provides both e+ and e- to VEPP-2000 and VEPP-4M colliders

## Slide 11: Super-CT Project Injector
Thermionic
Gun
Polarized e- Gun
e- Photogun
1 nC, 3 ps
ΔE/E ~ 0.5 %
(total charge)
e- 1 GeV + 1.5 Gev Linacs
AS – 16 + 24
Klystron – 8 + 12
Length – 72 m + 96 m
e- 1.5 GeV Linac
AS – 24
Klystrons – 12
Length – 96 m
e+ 1.5 GeV Linac
AS – 24
Klystrons – 12
Length – 96 m
Damping Ring
e+ 1 – 1.5 GeV
1 GeV Linac
AS – 16
Klystrons – 8
Length – 72 m
Debuncher
Compressor
Damping
Wiggler
IP
RF System
Damping
Wiggler
Damping
Wiggler
Damping
Wiggler
Siberian
Snake
Crab
Sext
Crab
Sext
Total number of accelerating structures: 104
Klystron number: 52
Total length of the linacs: ~440 m
Drift channel for 1.5 GeV mode
2*1011 electrons/positrons per second
@ the energy of 1.5 – 2.5 (3) GeV