## Slide 1: Particle Identification (PID) at HIEPA Experiment
Ming Shao
CPPT/USTC

## Slide 2
MDC
PXD/SSD
PID-barrel
PID-endcap
EMC
Coil
York/Muon
York/Muon
IP
3~6 cm
10 cm
15 cm
85 cm
105 cm
135 cm
185 cm
245 cm
120 cm
140 cm
190 cm
240 cm
300 cm
20
Detector System

## Slide 3: PID detector Key features
Enable /K (and K/p) 3-4 separation up to 2GeV/c
Suitable for high luminosity run – fast detector
Radiation hard, especially in the endcap region
Compact – reduce costs of the outer detectors
Modest material budget – <0.5X0

## Slide 4: PID at low momentum
Specific energy loss (dE/dx) in the gaseous tracking detector (MDC) can be used for low momentum PID
Better dE/dx resolution for longer track length
Example: ~6-7% at BESIII MDC (track length ~0.7m)  /K/p ID for p<0.8/1.1 GeV/c

## Slide 5: Time of Flight?
/= T/T =m2/2p2
T =L/c * m2/2p2 ~ L/c * m2/2p2
For /K/p at p=2GeV/c, T ~ 0.1ns*L(m) = 100/270 ps at L~1m. So for clean /K/p separation an overall TOF time resolution ~30/90ps is needed.
TOF alone can not identify /K to p=2GeV/c

## Slide 6: Cherenkov detector
Cherenkov radiation:
  Radiation if particle velocity
  larger than speed of light in
  medium
Commonly used in HEP experiment to identify particles at high momentum
Various types of Cherenkov detector
  Threshold Cherenkov – simple to build
  Imaging Cherenkov: RICH(large momentum range)/DIRC/TOP(most compact)

## Slide 7: Design - 1
A threshold Cherenkov detector (/K), plus a TOF
Similar to BELLE ACC design
n~1.01-1.03, TOF resolution ~90ps
Technically simple
But need more space to accommodate more materials
Plastic scintillator + PMT or MRPC can be used for TOF
Threshold Cherenkov detector module

## Slide 8: Radiator index choice
Aerogel is the only choice in this index range

## Slide 9: Expected performance - 1
n = 1.030, /K separation 0.8-2.5GeV/c
n = 1.010, /K separation 1.0-3.5GeV/c
BELLE ACC

## Slide 10: Design - 2
No TOF, PID by RICH only
Similar to BELLE-II ARICH design, aerogel + HAPD readout, but with higher refractive index to extend to lower momentum
n~1.1-1.13 (Below threshold for proton at p<2GeV/c)
n~1.06 already proven at the endcap, how about n~1.1-1.13 (close to aerogel limit)? How about the barrel region?
Need further R&D
Proximity focusing

## Slide 11: Expected performance - 2
double aerogel, n0=1.050,1.065
Proximity gap = 200mm
c=336mrad
=15.8mrad
Ndet= 11.4
>5.5 σ /K separation at 4 GeV/c
BELLE-II ARICH
~5mm photon
sensor size

## Slide 12: Design - 3
PID by RICH only
Similar to ALICE HMPID design, with MWPC (CsI coated cathode) readout
n~1.3 (liquid C6F14), UV detection
  or LiF (n~1.46, sawtooth surface) at CLEO-III
Already proven
Immune to B field  same structure can be used at both the endcap and the barrel
MWPC too slow? Aging?
C6F14 must be kept at high purity
LiF

## Slide 13
Expected performance - 3
Cherenkov angle vs. track momentum in p-Pb data
ALICE HMPID
Liquid C6F14 radiator n~1.3 @ 175nm
Proximity gap = 80mm
MWPC readout pad size 8mm8.4mm
>3 σ /K separation at 3 GeV/c

## Slide 14: Expected performance -3

## Slide 15: iTOP
Design - 4
DIRC

## Slide 16: iTOP performance

## Slide 17: Baseline Design
PID by RICH at 0.8<p<2GeV/c, no TOF
Proximity RICH, similar to ALICE HMPID design, but with CsI coated GEM/THGEM readout (PHENIX HBD)
  avoid photon feedback
  less ion backflow to CsI
  Fast (few ns), high rate capacity
  Robust
  Radiation hard
Proximity gap ~10cm
n~1.3 (liquid C6F14), UV detection
HBD GEM readout

## Slide 18
Imaging resolution
Take n=1.13/1.3 and Nphoton=10
~60/40 mrad single photon resolution is needed for clean /K separation at p=2GeV/c
correspond to ~20/14mm photon sensor size (with a proximity gap of 10cm)

## Slide 19
Expected performance
The final performance should be similar to that of ALICE HMPID, fulfilling the requirements imposed to PID at HIEPA experiment

## Slide 20
Thank you for your attention!
Suggestions are Welcome!

## Slide 21: Relevant formula
Threshold:
Emission angle:
Photon yield: