## Slide 1
Véronique Puill
S. Barsuk, D. Breton, L. Burmistrov, V. Chaumat, S. Drouet1, S. Dubos, P. Hallin, O. Lemaire,
L. Leterrier1, P. Loaiza, J. Maalmi, A. Natochii, A. Stocchi, P. Vallerand, S. Wallon
1 LPC Caen
21 March 2018
Cherenkov detectors R&D at
HIEPA 2018

## Slide 2
Experience in Cherenkov detectors development and R&D :
UA9 proton flux measurement
Cherenkov Lab R&D project
Proposal of a FTOF detector for Super -c Factory
Cherenkov detectors R&D at LAL

## Slide 3
The CpFM for UA9
in collaboration with CERN, Imperial College, INFN, PNPI
UA9 mission: Investigate bent crystals as primary collimators in hadron colliders
The halo particles are removed by a cascade of amorphous targets:
1. Primary and secondary collimators intercept the diffusive primary halo.
2. Particles are repeatedly deflected by Multiple Coulomb Scattering also producing hadronic showers
3. Particles are finally stopped in the absorber
Beam collimation
The collimator job is to control and safely dispose of the halo particles that are produced by unavoidable beam losses from the circulating beam core (caused by collisions at the interaction points, the interaction of the beam particles with residual gas, intra-beam scattering, …)
Daniele Mirarchi,
A&T Seminar, CERN
Main roles of the collimation system:
Minimization of possible magnet quench
Protect the machine from fast accidental losses
Avoid high radiation levels displaced all around the accelerator

## Slide 4
Present collimation system designed to handle 360 MJ of stored energy in the machine
Hi-Lumi upgrade an increase up to about 700 MJ is foreseen
The connected increased circulating intensity of about a factor two, calls for:
Improved cleaning performances
Reduction of induced impedance by collimators
Reduction of the beam instabilities
R&D for the upgrade of the LHC collimation system
Crystals collimation which aims are to improve the cleaning and reduce the impedance is one of the R&D projects approved for the LHC collimation
D. Mirarchi, A&T Seminar, CERN
Collimation scheme using a solid state primary collimator scatterer (SC).
(b) Collimation scheme with a bent crystal (BC) as a primary collimator. Halo particles are deflected and directed onto the absorber far from its edge
Yu.M. Ivanov
Notes: En vue de la seconde exploitation du LHC, à haute énergie, il a été décidé d’optimiser divers aspects du système. En effet, dû au doublement de l’énergie emmagasinée dans la machine, l’efficacité du nettoyage du faisceau doit être améliorée et l’impédance induite par les blocs de collimation réduite.
Le CERN a donc mis au point de nouveaux dispositifs pour remplacer 20 % des collimateurs existants et travaille également sur des projets de R&D mettant en œuvre des technologies innovantes, dont la collimation par cristal : un cristal courbé, remplaçant le collimateur primaire, peut dévier le halo pour l’amener sur l’intérieur des collimateurs secondaires, améliorant ainsi leur efficacité d’absorption.

## Slide 5
Investigate bent crystals as primary collimators in hadron colliders
The UA9 Experiment @ CERN
Bent crystals work as a “smart deflectors” on primary halo particles (W. Scandale 10.1103/PhysRevSTAB.11.063501)
If crystalline planes are correctly oriented, particles are subjected to a coherent interaction (channeling):
5
The UA9 Collaboration proved that bent crystals can be used as primary collimators in the SPS and in the LHC
  large angle deflection also at high energy (40 µrad at 7 TeV)
  reduced interaction probability (e.g. diffractive events, ion fragmentation/dissociation)
  reduced impedance (less secondary collimators, larger gaps)
  small angular acceptance
  concentration of the losses on a single absorber
Notes: Depuis environ dix ans, la collaboration UA9 constituée d’experts du CERN, des laboratoires russes PNPI, IHEP et JINR, de l’INFN, du LAL et de l’Imperial College, étudient les avantages d’utiliser des cristaux courbés dans les systèmes de collimation des collisionneurs
Si une particule pénètre tangentiellement aux plans atomiques du cristal de Silicium, elle peut, avec une certaine probabilité, être canalisée. Sinon, elle peut être réfléchie et repeupler le halo.
Les avantages d’une collimation par cristal courbé sont : un grand angle de déflection même à haute énergie (40 µrad à 7 TeV), une probabilité d’interaction des particules du halo avec des éléments massifs réduite et une réduction du budget d’impédance de la machine. Les 2 inconvénients majeurs sont une faible acceptance à l’entrée du cristal et la concentration des pertes dans un même absorbeur.
La collaboration UA9 a installé un système de collimation à l’échelle, utilisant un cristal courbé comme déflecteur primaire, dans la zone de test H8 du hall nord du CERN, dans le SPS (depuis 2008) et au LHC (depuis 2014).

## Slide 6
The CpFM: Cherenkov proton Flux Measurement
In vacuum, radiation hard detector:
interception of the channeled beam by a quartz radiator (retractable finger)
emission of Cherenkov light readout by a PMT placed 1 m from the beam pipe (light brought by silica fibers)
PMT amplified signal readout by the WaveCatcher module (3,2 GHz digitizer)
2 channels (one to measure the background)
Aim of the CpFM: count the number of deflected protons with a precision of about 5% in the SPS environment (mean value over several bunches)

## Slide 7
Radiation levels close to the pipe:  dose = 10 Mrad/year
thermal neutrons fluence = 1014 n/cm²/year
protons fluence = 1013 p/cm²/year
Radiation hardness of the CpFM components
 Irradiation (60Co) with a dose of 11 MGy (1100 Mrad) : stability of the samples Heraeus Suprasil Standard & Infrasil, Spectrosil A and B (Saint-Gobain) and Corning 7940
Quartz radiation hardness
3 fused silica types (Corning 7980, Schott Lithosil Q0, Heraeus Suprasil 1) irradiated with 150MeV proton beam with dose levels: 100krad, 1Mrad and 10Mrad
 No significant radiation damage observed in any fused silica sample
M. Hoek, RICH 2007
Our choice: Corning 7980 & Heraeus Suprasil

## Slide 8
Optical Fiber radiation hardness
Risk: transmittance loss
Good candidate: all silica fiber:
core 600 µm
attenuation @350nm <=0,06dB/m
operational in 200-1200 nm range
18 rad/s (0.3 rad/s LHC worst)
PMT radiation hardness
no deterioration of the quartz window transmittance
increase of the dark current (x 500 with 20 Mrad of )
no important change of the gain and quantum efficiency
coloring of the glass
glass scintillation
protons / neutrons /γ‐rays
Hamamatsu R7378A
Radiation hardness of the CpFM components

## Slide 9
The CpFM: Cherenkov proton Flux Measurement
Fibres bundle
PMTs socket and housing
Quartz bars
Wavecatcher
DAQ electronics
p

## Slide 10
CpFM Calibration Beam Tests in H8
400 GeV/c p , 180 GeV/c +
Calibration coefficient (CpFM with straight bar): 0.63 p.e/proton
40 m cables
PMTs
bundle
WaveCatcher module
Quartz bars end touching the 45 ° viewport
L bars connected to the flange

## Slide 11
The CpFM in the SPS
Installation in the SPS, 58 m downstream the crystal
http://dx.doi.org/10.1088/1748-0221/12/04/P04029
General article about the CpFM R&D and its installation:
alignment of the quartz bars
flange
Quartz bars

## Slide 12
Deflected protons measurements by the CpFM
CpFM1
CpFM2
interception of the channeled beam
interception of the halo
Linear scan: insertion of the bars in the beam pipe
CpFM amplitude distribution in the channeling region in good agreement with the expectations
Number of deflected protons as a function of the position inside the beam pipe
CpFM1
CpFM2
5 mm between the 2 bars
Notes: Nous avons participé à 3 autres prises de données qui n’ont malheureusement pas été très fructueuses pour le CpFM car nous avons eu très peu de temps faisceau dédié à son étude, environ 5 h en tout et pour tout, dû à des problèmes avec le faisceau du SPS.
Ce plot montre l’amplitude du signal des 2 voies lorsque le CpFM est en position de parking. On observe que le CpFM2 a un signal plus élevé que le CpFM1
Sur ce plot, on voit la variation du signal du détecteur en fonction de sa position transverse dans le tube faisceau.

## Slide 13
Deflected protons measurements by the CpFM
Angular scan: counting of the deflected proton when changing the angular orientation of the crystal (from 1800 to 900 µrad)
max signal on CpFM
min losses on the BLM
Channeling angle found at 1432 µrad
 good agreement bewteen the CpFM and the scintillator BLM (Beam Loss Monitors)
Losses measured by the BLM
CpFM count rate
Notes: Nous avons participé à 3 autres prises de données qui n’ont malheureusement pas été très fructueuses pour le CpFM car nous avons eu très peu de temps faisceau dédié à son étude, environ 5 h en tout et pour tout, dû à des problèmes avec le faisceau du SPS.
Ce plot montre l’amplitude du signal des 2 voies lorsque le CpFM est en position de parking. On observe que le CpFM2 a un signal plus élevé que le CpFM1
Sur ce plot, on voit la variation du signal du détecteur en fonction de sa position transverse dans le tube faisceau.

## Slide 14
On-going development: development of an ASIC
Evaluation of both partial and total charge carried by the detector signal, which is proportional to the particle flux.
partial charge
total charge
Design of a new electronics: measurement of the charge, the amplitude and the time at 40 MHz without dead-time
Each channel is composed of 3 preamplifiers ensuring the measurement of partial charge (around the peak of the signal with a programmable width), total charge over the full clock period, and peak detection, associated to a Time to Analog Converter stage ensuring the time measurement between the discriminator signal and the beam clock.
 V1 in October 2018

## Slide 15
Development of a multichannel detection chain for the measurement of an absolute particles flux with an accuracy of 5 % and a timing resolution of 20 ps.
Characteristics :
- 8 to 16 channels/detector
Ultra vacuum compatible
Response to single particle (proton, pion, ion)
Charge measurement from 1 to tens of thousands of incident photons on the photodetector
Timing resolution of 20 ps (rms) for few particles
matrix SiPM, PMT, MCP-PMT
Amplification
Charge and timing measurement
particle
Radiator
(Quartz)
Multichannel integrated electronics
Cherenkov Lab R&D Project
Photodetector
Optimization of the light yield : mechanical integration of the bars in a metallic flange for the uses in vacuum
Multichannel ASIC in TSMC 130 nm for the measurement of the charge over a large dynamic range and with a timing resolution of 20 ps
Technological challenges

## Slide 16
Tests of different quartz polishing qualities
The effect of polishing is very difficult to simulate  we need to perform tests
Our request : roughness = 1 , 10 and 50 nm
Search for companies which produce/polish quartz bars (Fused Silica) : USA, China, Ukraine, Switzerland, Germany, Czech Republic, Japan, Russia  only 2 companies answered positively to our request but the can only ensure the « best effort » but cannot provide intermediate quality of polishing …
We are looking for a way to measure this polishing quality
Ordering of 4 bars with “optical quality”
We use ultra polished Quartz (surface flat to 0.1 mm or better, surface & side polish quality 200 angstroms rms) in order to maximize the total internal reflections but they are :
Very expensive
Difficult to produce
Would it be possible to work with bars with a lower quality of polishing ?

## Slide 17
Distribution of the number of p.e per incoming proton produced at the PMT photocathode
L-shape bar and curved bar (bar not in direct coupling with the PMT)
Bar geometries comparison – GEANT4 simulations
I-bar
Pyramidal-bar
90°

## Slide 18
Bar geometries comparison in tests beam
Test (CERN - end of October 2017) with  of 3 different quartz geometries: straight (I), curved and pyramidal bar
I bar
Banana bar
Pyramidal bar
beam
Best results with the Pyramidal bar (as expected
with the Simulation)

## Slide 19
  New CpFM geometry for UA9
Amplitude distribution
Calibration Coefficient : 60 p.e./proton
 factor 100 in comparison with the previous CpFM version (10 if we compare the system without the fiber bundle)
First application of the Cherenkov Lab work: improvement of the CpFM for UA9
Installation of a pyramidal bar in direct coupling with the PMT inside the SPS

## Slide 20
MCP-PMT HAMAMATSU SL10-M16 : MCP-PMT 64 channels (16 x 4), old generation
  Photodetector studies (MCP-PMT, SiPM)
Mapping of the current response over the 16 channels
39ps | 40ps | 38ps | 39ps
38ps | 38ps | 39ps | 38ps
40ps | 39ps | 39ps | 40ps
40ps | 39ps | 39ps | 40ps
Single Photoelectron Timing Resolution (SPTR)
SPTR () mapping
Internship work of Jiajin Zhang (University of Science and Technology of China)
MCP-PMT BURLE XP85012: MCP-PMT 64 channels (old generation)
SPTRbest () = 55 ps
MCP-PMT PHOTEK to be ordered

## Slide 21
SiPMs : 4 SiPMs HAMAMATSU, 2 KETEK, 2 Sensl
  Photodetector studies
SPTR (FWHM) of HAMAMATSU & KETEK SiPM
Internship work of Tetiana POVAR (Kiev University)
SPTRbest () = 70 ps

## Slide 22
  Readout Electronics development
The ASIC with integrated TDC and two internal gains will simultaneously measure the amplitude and the arrival time of the signal. It will be capable of measuring a signal from a single electron and will cover a large dynamic range
Requirements for the Cherenkov Lab ASIC
8 channels
Single photon response
Dynamic range of tens of kp.e
Timing resolution of 20 ps rms
High counting capability (2 MHz in average, 40 MHz
for a few tens of events)
Challenge:
      the circuit has to work with different kinds of detectors
      wide dynamic range
      very high counting capability
What is ready:
timing measurement
threshold detection
frontend stage
charge measurement
On-going:
Tests of the first proto (timing, partial charge measurement, slow control)

## Slide 23
  Example of quartz bar as a radiator for Cherenkov detection: the CpFM for UA9
Initial design : the bars are brazed to the flange
  Mechanical integration of a Quartz bar in a metallic flange
Even if company ran a very slow thermal cycle to minimize the thermal mismatch between the parts, one of the quartz bar got totally cut
The last bar was not cut and hold on the flange but it was cracked
The issue seems to be the CTE gap (coefficient of thermal expansion) between the metal and the fused silica

## Slide 24
Design of the First prototype for Cherenkov Lab :
Round quartz bar (brazing easier with a circular symmetry)
Stainless steel flange
  Mechanical integration of a Quartz bar in a metallic flange
Asked by the company : shoulder where the flange and the bar will be brazed together
 What consequences on the output signal ?

## Slide 25
Simulation of the geometry proposed by the company (reduced diameter)
  Simulation of a round Quartz bar (1/2)

## Slide 26
No variation of the generated photons with the length of the shoulder
Less reflections with a shoulder over 50% of the surface
85%
80%
Shoulder diameter D (cm)
Shoulder at 50%, 80 %, 85 % of the bar
  Simulation of a round Quartz bar (2/2)
Strong variation of the ratio detected photons/generated photons for D between 8.5 and 10 mm
Shoulder diameter D (cm)
Detected photons/produces photons
Shoulder at 50% (diameter reduction over half the length of the bar)
* Cut : cut of the end of the bar at 47°

## Slide 27
  First proto: round bar + flange
Good surprise : no breaking of the bar
Metallic pipe (7 mm length x 0.5 mm width)
what consequence for the Cherenkov light yield ?
To be measured
Bad surprise: possible photon absorber

## Slide 28
  Next step : brazing of rectangular bar
Rectangular bars 
measurement of the polishing quality
characterization of the light yield (comparison of the bars before and after the brazing)
  Characterization of the bars with a  source  on-going measurements @ CERN

## Slide 29
For a Super -c factory
We propose to participate to the development of a Forward Time-Of-Flight (FTOF) detector for HIEPA endcap PID
FTOF goals:
charged particle identification (/K separation) for particle momenta up to 2 GeV/c
time-stamp for a given bunch-crossing event for all detector signals
Constraints:
the space allocated for the PID system between the main drift chamber and the calorimeter in the endcaps is limited to 20 cm
in order to limit preshower effects   amount of material in front of the electromagnetic calorimeter (< 0.5 X0)
Challenge:
the available flight length is only between 1.3 and 1.6 meters long while the /K/p separation should be efficient up to 2 GeV/c  to fulfill this requirement, the timing measurement must be accurate to better than 30 ps
Design and development of a FTOF sector for charge and timing measurements accurate at the level better than 30 ps composed of a Fused Silica radiator connected to MCP-PMT or SiPMs readout by a dedicated front-end electronics.
Collaboration LAL, USTC, TSNUK (Ukraine)

## Slide 30
30
Layout:
12 thin (15 mm thick) quartz tiles
Cherenkov light detected by fast MCP-PMTs
WaveCatcher electronics
Forward PID requirements: Good K/ separation in 0.8-3.5 GeV/c range
Compact device (thickness < 10 cm) Radiation-hard
LAL solution : « Forward Time-Of-Flight »
Flight length ~ 2 m required timing resolution of 30 ps
At least 10 photons / track timing resolution per photon around 100 ps
Geant4 Simulation
Proposal: SuperB-like FTOF Detector
Quartz tile readout by MCP-PMT (HAMAMATSU or BURLE)
Time of the p.e arrival vs channel for K (3.5 GeV/c)
Notes: 30
Groupe Evaluation AERES 13-14 janvier 2011

## Slide 31
Test of a prototype of one sector at SLAC in the CRT (Cosmic Ray Telescope)
● Good agreement between data and simulation
● 70 ps time resolution per p.e.
● Demonstration of the principle
MCP-PMT characterization measurements
Proposal: SuperB-like FTOF Detector
Notes: 31
Groupe Evaluation AERES 13-14 janvier 2011

## Slide 32
Conclusions
Cherenkov Lab, a generic R&D project with
R&D on mechanical integration
R&D on electronics
Quartz and Photodetectors studies
 Joint proposal LAL-USTC-Kiev U: FTOF detector R&D for the PID at Super -c factory
Expertises @ LAL:
Quartz Cherenkov detectors design (Geant4 simulation) and tests
Test benches for absolute calibration (gain, efficiency, timing) of photodetectors
Readout (ASIC) development
Design and fabrication in Mechanics
WP management (SuperB, UA9)

## Slide 33
BACKUP

## Slide 34
UA9 SPS
Extensive tests with 120-270 GeV protons and Pb ions since 2009
Single bunch and multibunch dedicated beams
Fast and reproducible crystal alignment
Clear loss reduction with respect to an amorphous orientation up to x 20 reduction
Particles well channelled by the crystal don’t approach the planar channel walls closely  no nuclear interactions  beam losses measured by the BLM instrument (Beal Loss Monitor) are strongly reduced
channeling
amorphous orientation
W. Scandale, SPSC 2012
Notes: Le 1er système de collimation a été installé initialement dans le SPS pour évaluer l’efficacité de la technologie. Les taux de pertes étaient mesurés au moyen de Beam Loss monitor.
De nombreux essais ont été menés avec des faisceaux de protons et d’ions Plomb de 120 à 270 GeV/c. Ces plots montrent le nombre de particules détectées dans les BLM situés en amont de l’absorbeur en fonction de l’inclinaison du cristal (protons à gauche, ions à droite). Les particules déviées par le cristal courbé n’interagissent pas dans ces compteurs ce qui se traduit par une importante réduction du taux de comptage lorsque les plans cristallins sont alignés avec la trajectoire des particules.
Ces essais ont démontré la faisabilité de la collimation assistée par cristal et une réduction d’un ordre de grandeur des rayonnements créés par les interactions inélastiques dans le collimateur primaire qui sont susceptibles de créer de graves dommages.
Après de nombreuses années de travail intensif et des résultats importants, UA9 a prouvé que la technologie des cristaux courbés était suffisamment maîtrisée pour qu’on puisse envisager de l’appliquer à une collimation au LHC.

## Slide 35
UA9 LHC
Losses recorded with BLM at goniometer position normalized to beam flux
Crystal test at the LHC supported in 2015 with 3 dedicated MD
Channeling observed for the first time with LHC beams
Protons: 6.5 TeV (record )
Pb ions: 450 GeV (record )
A prototype crystal collimation system was designed and installed in the LHC to validate the feasibility of this concept at the LHC during Run II
protons 6.5 TeV
Notes: Pour l’essai mené récemment au LHC, deux cristaux de silicium, ont été installés dans la zone d’insertion IR7. Ces essais de collimation avec des ions à 450 GeV et des protons à 6.5 TeV ont été couronnés de succès.

## Slide 36
New Experiment : Measurement of the magnetic moment of the Λc
Proposal from A. Stocchi (LAL) et al, “Physics Beyond Colliders Kickoff Workshop”, Geneva, 6 September 2016
The magnetic moment of the long living baryons has been measured by looking at the precessing of the spin along a intense magnetic field (change in the polarisation). It was done for long living particle such as the strange baryons
No measurement of magnetic moments of charm or beauty baryons has been performed so far because the lifetimes of charm/beauty baryons are too short to measure the magnetic moment by standard techniques (Short living particles i.e. c ~100 µm with boost ~100‐200  L=2‐3cm)
The spin precession angle  is proportional to the bending angle of the crystal c through the Lorentz factor  and the magnetic moment (g-2)
Proposal: Exploitation of the intense electromagnetic field between crystal atomic planes of a bent crystal (Thousands Tesla over cm length) which induces the spin precession of c+ to measure its the magnetic moment (c(c+)  60 µm)

## Slide 37
Double crystal setup
• A first bent crystal deflects the halo particles upstream of an interaction region of LHC, in our case the LHCb one, in order to separate them from the circulating beam.
• A target inserted in the pipe intercepting the deflected halo, producing polarized Λc .
• A second bent crystal (= small super strong magnet) able to induce a sizable spin precession angle during the lifetime of the particle and deflect them into the LHCb detector which will measure the final polarization vector by analyzing the angular distribution of the particle decays
• An additional absorber to intercept the halo particles non-interacting with the target, thereby allowing the possibility of fixed-target operation in parasitic mode
Experimental setup needed:
Xtal

## Slide 38
The new CpFM in the SPS
New CpFM requirements
Inside primary vacuum
Transparent for the machine
Dynamic range : 1 to 100/bunch (but the integrated intensity value will be from 107 to 109 p/s)
Measurements to be performed: amplitude (from 5 mV to 2 V) and timing (with a precision on the timing
measurement of 2 ns)
Measurement rate: bunch per bunch every 25 ns
Calibrated detector with on-line monitoring (at least or an in-situ calibration)
Accuracy of the measurement: 5-10 % in absolute
Duration of the measurement: at least 20 days