## Slide 1: Accelerator of HIEPA Facility : Concept, Challenges and Current Status
Luo, Qing Dr. &Associate Professor
National Synchrotron Radiation Lab, Accelerator Division
Jan. 2015

## Slide 2: Outline
Concept of HIEPA with HALS
Key Points
Ideas and Methods
Important Technologies
Conceptual Design Team
Future Plans

## Slide 3: Concept of HIEPA with HALS
Hefei Advanced Light Source Concept
4th Generation Light Source with DLSR
Notes: Hard x ray：0.01nm-0.1nm，10k-100KeV；lower than 0.01nm，super hard X，100KeV+；0.1-10nm，soft x，100-10KeV; vacuum ultra violet, 150~200nm。

## Slide 4: What’s a 4th Generation Light Source with DLSR？
Diffraction Limited Storage Ring
  a.k.a. Ultimate Storage Ring
Most important parameter: brightness
  Determined by beam emittance
  Electron beam emittance reaches diffraction limit of photon beam
    Wavelength/(4π)
Notes: Possibilities for a Diffraction-Limited Upgrade of a Soft X-ray Light Source， R Hettel
DLSR design and plans: an international overview， R Hettel， J. Synchrotron Rad. (2014). 21, 843-855
Main design goal is to decrease the horizontal beam emittance to diffraction limit of soft x and hard x-ray.
For 10^-10m, hard x, 12.4 keV，8 pm.rad；10^-9m, soft X，1.24 keV，80 pm.rad。

## Slide 5: Storage Ring Light Source compared to Linac Based FEL
Peak Brightness
Average Brightness
Pulse Repetition Frequency
Number of beamlines, stable &tunable
DLSR based light source is needed

## Slide 6: Hefei Light Source
National Synchrotron Radiation Lab and Hefei Light Source
Notes: Hard x ray：0.01nm-0.1nm，10k-100KeV；lower than 0.01nm，super hard X，100KeV+；0.1-10nm，soft x，100-10KeV; vacuum ultra violet, 150~200nm。

## Slide 7: Hefei Light Source
National Synchrotron Radiation Lab and Hefei Light Source
  Approved in 1983, First built 1984-1991, 2nd phase 1999-2004, Upgrade to HLS II 2010-2014
  800MeV, 40nm·rad, 300mA,66.13m, 50ps
Notes: Hard x ray：0.01nm-0.1nm，10k-100KeV；lower than 0.01nm，super hard X，100KeV+；0.1-10nm，soft x，100-10KeV; vacuum ultra violet, 150~200nm。

## Slide 8: Hefei Light Source
Notes: Hard x ray：0.01nm-0.1nm，10k-100KeV；lower than 0.01nm，super hard X，100KeV+；0.1-10nm，soft x，100-10KeV; vacuum ultra violet, 150~200nm。

## Slide 9: Concept of The Light Source
Low Energy SR Source(1-3.5GeV)
  Optimized energy 2GeV, 1000m, 0.1nm·rad
  VUV-soft X ray
Unique for VUV to soft X ray
  Mid-energy, i.e. SSRF 3.5GeV, best for 5-25keV high brightness hard x-ray
  Low-energy, best for lower than 1keV, VUV to soft x, 100 times brighter than SSRF
  VUV, 1meV@10eV high energy resolution
Notes: Energy of electron beam determines the best spectrum range for synchrotron radiation.，3.5 GeV is best 适合于提供能量在5～25 keV的高亮度X射线光源，在能量低于1keV的真空紫外和软X射线波段范围，合肥先进光源的亮度将比上海光源高出100倍（如表1和图1所示）。同时只有在VUV光源上，才能获得超高能量分辨1meV@10eV，探测和操控能带较窄的价电子问题。因此北京、上海光源都不利于获得高亮度的真空紫外辐射。
VUＶ：该波段的紫外线在空气中被氧气强烈吸收而只能应用于真空，其长波限粗略在150~200nm。

## Slide 10: Concept of The Light Source
Why VUV to soft X ray
  Both Atom & Electron scale
    Matter science
    Energy science
    Nuclear technology
    .etc
  Supplement for national SR system
Amazing collider and also brilliant light source
Notes: 合肥大科学中心未来体系的一部分
现有的正负电子对撞机主要用于粒子物理实验，同步辐射只是寄生产物，例如BEPC II作为光源有专用与兼用两种模式，兼用模式下优先保证对撞，光源的利用效率很低。而HIEPA作为同步辐射光源供光将不区分专用模式与兼用模式，对撞的同时也正常供光，工作效率互不影响，这将是一个重大的系统集成创新。
HIEPA作为光源，又可称为合肥先进光源（Hefei Advanced Light Source, HALS）。HALS的工作能量为2GeV，水平方向自然发射度0.1nm·rad，束流品质极高，所提供的
同步辐射工作波长可调并覆盖软X射线到真空紫外（Vacuum Ultra Violet, VUV）波段，在相干性和亮度方面可接近于同一波段的激光光源，同时还可与现有激光光源作用和耦合，是探测和操纵物质与能量的理想平台。作为先进的低能光源，其建设指标超过世界上正在运行和正在建设的同类大科学装置，特别是作为衍射限光源提供横向全相干VUV光，将对物质的形成、调控和创造提供良好的研究条件，为我国高水平用户做出世界一流的研究成果创造前所未有的机遇：
解决原子和电子两种尺度的科学问题，迫切需要X射线和VUV两种同步辐射光源。
由于科学研究对光源的要求不同，为了揭开自然界各种现象和生命起源的本质，提高控制宏观和微观物质的能力，同时需要X射线光源研究物质的原子结构信息和真空紫外光源研究与功能和性质相关的材料的电子结构信息。所以世界上从第一代同步辐射光源开始就存在着两类不同波段的光源（VUV和X射线光源），并一直并行发展。
科学将从观测时代迈入控制时代，需要先进的VUV光源。
21世纪科学将进入量子调控世界。2007年12月，美国能源部在科学研究报告中明确提出了未来面临的五个重大挑战，分别为：在电子水平上控制材料形成过程，利用剪裁特性实现原子和能量节约的材料合成，控制原子或电子的复杂相互关系，在纳米尺度上控制能量和信息和表征和控制极端非平衡态材料。在以上五个重大挑战中，第一和第三重大挑战，必须利用先进的VUV光源，才能研究在电子水平上控制材料形成过程和控制材料中电子之间的复杂相互作用关系。VUV光源在其他三项重大挑战中也将发挥重要作用。
在《国家科学和技术中长期发展规划纲要（2006-2020年）》中部署的蛋白质研究、量子调控研究、纳米研究和发育与生殖研究等重大研究计划中均涉及到电子结构-量子态的探测和调控。强关联体系中的高温超导机理和巨磁阻现象、原子分子反应中的电子转移过程、磁记录材料中自旋电子的运动状态、催化剂表面的反应动力学行为、生物细胞中的蛋白质复合体的相互作用等也均涉及电子层面的观测、操纵和控制，亟需先进的同步辐射VUV光源。
先进VUV光源对国家重大战略布局和国防建设有不可替代的作用。
对先进的VUV光源迫切需求主要体现在以下几个重大基础科学领域：
能源与环境：只有高亮度的VUV光源才有可能在飞秒或皮秒的时间尺度内实时检测化学反应过程，认知化学过程的催化反应机理，为提高能源效率、新能源开发以及环境污染治理提供理论指导。
纳米科学：软X射线扫描透射显微和光发射谱以及超高分辨真空紫外散射等实验技术将能够研究单个纳米颗粒的三维空间形貌、电子结构和光谱等性质，VUV时间分辨技术则可用于研究纳米颗粒的生长过程和性质的变化。这些工作将为发展新型功能纳米器件提供理论基础。
凝聚态物质与新奇量子现象：高亮度的VUV-软X射线光源可以实现超高分辨的角分辨光电子能谱、软X射线磁性圆二色显微和非弹性散射等同步辐射新技术，将实现对电子结构、自旋结构和元激发结构的高分辨测量和原位表征，从中发现新奇量子现象，发展基于新量子现象的新材料和新器件，为下一代信息技术的发展提供理论基础。另一方面，由于自旋、轨道间的相互作用可以通过强磁场的作用，改变物质的电子状态，进而改变材料的光、电磁性质，和原子、分子的化学性质。利用同步辐射光源与强磁场联合的实验手段将会开创性地揭示强磁场下各种物理现像的微观机制和机理，有望对一些物理现像做出全新解释。
生命科学：发展高亮度的VUV光源，利用软X射线CT方法更精细的观察细胞内部三维形貌和细胞器结构，获取蛋白质和细胞的功能信息，不仅仅对生命现象会有全新的解读，而且为疾病的形成机理提供全新的信息，有利于研发对疾病的干预手段和研制相应诊断治疗产品。
核技术和核工业:基于同步辐射光源的谱学测量，是研究镧系和锕系稀土族元素等重元素材料电子态和相变的最重要手段之一。重元素中未填满的f壳层，对其物性起着致关重要的影响。由于f价电子的能带很窄（1 －10 meV），为了能从谱学的角度对f价电子进行研究，我们需要超高能量分辨率1meV@10eV，象这样的能量分辨率只能在VUV波段上实现。因此，新的VUV同步辐射光源的建立，对于这方面的研究必将起到重要的推动作用。
国防：国家同步辐射实验室的燃烧研究已达到国际先进水平，如果能利用具有高通量VUV新光源，就可以研究高超声速燃烧所特有的气动热力学及燃烧机理，有助于指导超燃冲压发动机的设计与制造，同时也可用于特殊领域中极端条件（耐高温，耐腐蚀，耐辐射，高强度，高韧度）材料的功能研究，有助于提升我国的国防、航天和海洋开发实力。
国内光源布局远不能满足科学技术快速发展对先进VUV光源的需求。
同步辐射的电子能量直接决定了同步辐射最优的光谱范围，因此，在能量低于1keV的真空紫外和软X射线波段范围，束流能量在1.5-2GeV的低能光源的亮度将比束流能量在3-4GeV左右的中能光源高出两个数量级，相比5GeV左右的高能光源优势则更加明显。因此，已经建成的3.5GeV中能上海光源，与正在建设中的5GeV高能北京先进光源，都不利于获得高亮度的真空紫外辐射。在合肥建设先进的低能光源，恰可以完成我国同步辐射光源在能区分布、地理位置分布两方面的合理化战略布局。
现有的合肥光源（Hefei Light Source, HLS）是我国第一台专用真空紫外光源，它的建设和运行是我国同步辐射事业的开创性成果，为我国基础研究和国防建设做出了重大贡献。然而作为二代机器，HLS束流发射度偏大、亮度较低，与国际先进的真空紫外同步辐射光源相比有很大的差距，完全不能满足未来科学技术发展和科学重大挑战的需求。在国家同步辐射实验室以往的工作基础上，继承技术、人力资源与工作经验等多方面的积累，建设HALS，可以充分利用与整合现有的资源，为合肥地区建设综合科学中心、开展物质科学研究提供极其有力的保障。

## Slide 11: Key Points
Luminosity of super tau-charm factory
  1033->1035
4th generation light source
Performance improvement
  Sharing Mode
  Beam physics @ next generation circular accelerators
    Collider beam physics，storage ring beam physics（beam collective effect）
    Beam-beam effect
    Electron cloud，.etc
Notes: 正电子-负电子束束效应，空间电荷效应，流强相关性
电子云效应：电子环，电子-正电子；

## Slide 12: Large Crossing Angle and Crabbed waist collision scheme
High luminosity requires very short bunches to allow decreased betay at the IP
Hourglass effect; beam-beam effect
Large Piwinski angle and Crabbed waist scheme
Large Piwinski angle collision:
*Super B factory conceptual design report, March, 2007
Notes: In high luminosity colliders, one of the key requirements is very short bunches, since this allows a decreased betay at the IP, thereby increasing the luminosity. However, betay cannot be made much smaller than the bunch length without incurring an hourglass effect.
Moreover, high luminosity requires small vertical emittance, together with large horizontal beam size and horizontal emittance, to minimize the beam-beam effect. It is, unfortunately, very diffcult to shorten the bunch length sigmaz in a ring.
Large piwinski angle : 有效对撞，提高kseiy, 不需要降低束团长度，因为解决了hourglass效应的问题
Small spot size at the IP, i.e., higher luminosity (Eq. 3.3)
Reduction of the vertical tune shift (Eq. 3.4); and Suppression of vertical synchrobetatron resonances
There are additional advantages in such a collision scheme: there is no need to decrease the bunch length to increase the luminosity, as proposed in standard upgrade plans for B and fai Factories. This will certainly ease the problems of HOM heating, coherent synchrotron radiation of short bunches, excessive power consumption, etc.. Moreover the problem of parasitic collisions (PC) is automatically solved by the higher crossing angle and smaller horizontal beam size, which makes the beam separation at the PC large in terms of sigmax.
However, a large Piwinski angle itself introduces new beam-beam resonances and may strongly limit the maximum achievable tune shifts？？？ (see for example [13]). This is where the crabbed waist innovation is required. 引入了新的非线性共振，空间电荷场强，刚好需要crabbed waist创新来解决
Tune shift也是调整kseiy的办法，具体？？？

## Slide 13: Differences between Colliders and Light Sources
Different construction goal
different beam quality requirements
luminosity；brightness;
different design and optimize methods
Notes: r=sigmay/sigmax， ip处束团截面的形状因子，即垂直与水平方向尺寸的比值，ksei为垂直方向束-束作用参量，kb束团数目，ib束团流强
积累、加速及对撞是对撞机的三大机能，所谓积累是设法把高能加速器在不同时间加速出来的脉冲粒子束团积累在对撞机环形真空室（称为储存环）中。一般需要积累几十或上千个束团，才能达到对撞所需的强度。电子同步加速器的束流团的积累是依靠同步辐射来完成的，同步辐射虽然使同步加速器的能量难于进一步提高，但却使得电子束的横向及纵向的尺寸在加速过程中大大收缩，即密度大大提高，利用这一特性就可以积累一股很强的电子束流。质子却没有这种特性，这就需要用动量积累过程来得到强流质子束。
积累以后，对撞机还可以将注入其中的高能粒子进一步加速到更高的能量，对撞机的这一作用与普通的同步加速器完全一样，粒子的能量是由安置在圆环上的高频加速腔供给的，在整个加速过程中，对撞机的磁场逐渐上升，高频腔的频率也被严格控制得与被加速粒子的回旋频率一样或成整数倍，从而使粒子不断地被加速到更高能量。当粒子被加速到预定能量后，对撞机的磁场就被维持在相应的恒定值上，粒子束就在环形真空室中不断地回旋，两束并在对撞区域内某点发生对撞。这时布置在对撞区周围的测量仪器，就可对碰撞时发生的事例不断地进行测量，剩下的没有起反应的粒子将继续在环里回旋运动，等到下一次到达对撞区时再度发生对撞。一直到束流的强度降低到不能再作物理实验为止，这时两股束流的寿命也就中止了。束流的寿命一般可达几小时或几十小时，所以作为注入器的高能加速器只有在积累过程中才把粒子束流提供给对撞机，而在对撞的过程中，还可供轰击静止靶的物理实验用。为了增加对撞的几率（即提高对撞机的亮度），70年代初期，出现了在对撞区中插入一种特殊的称为低包络插入节的聚焦结构，使束流在对撞点的横截面受到强烈的压缩，从而使对撞点的束流密度大大增加。
设计服务对象不同，优化目标不同
对撞亮度是局部参数，优化途径为增加流强、压缩束团尺寸，发射度无关（无sigma ’ 项）；供光亮度与寿命为全局参数，反比于发射度？？，途径为增加流强或优化降低发射度。
±符号的参数对不同能量的束流应该如何？？？
这是忽略hourglass效应的公式；sigmaz<=betay时可忽略hourglass效应，sigmaz很低时允许很小的betay，从而提高亮度，但sigmaz很难降低；betay比sigmaz小很多的时候，无法忽略hourglass效应

## Slide 14: Ideas and Methods
Symmetric two ring collision
Design the storage ring independently, treat IR as insertion device
Modular design for IR and typical periods
Local compensation
Suppress β function at IR to sub-mm
Notes: 装置沿用双环对撞方案，
单独设计储存环，采用模块化设计标准单元和对撞区，
然后对撞区作为插入段设计组成储存环，
在类似直线对撞机的插入段中优化对撞点的beta函数，使其降低到亚毫米量级，从而提高对撞亮度；
Crab sextupole，非线性补偿
Effect of the Sextupole Finite Length on Dynamic Aperture in the Collider Final Focus, A. Bogomyagkov, S. Glukhov, E. Levichev, P. Piminov
In high luminosity colliders, one of the key requirements is very short bunches, since this allows a decreased betay at the IP, thereby increasing the luminosity. However, betay cannot be made much smaller than the bunch length without incurring an hourglass effect.
Moreover, high luminosity requires small vertical emittance, together with large horizontal beam size and horizontal emittance, to minimize the beam-beam effect. It is, unfortunately, very diffcult to shorten the bunch length sigmaz in a ring.
Large piwinski angle : 有效对撞，提高kseiy, 不需要降低束团长度，因为解决了hourglass效应的问题
Small spot size at the IP, i.e., higher luminosity (Eq. 3.3)
Reduction of the vertical tune shift (Eq. 3.4); and Suppression of vertical synchrobetatron resonances
There are additional advantages in such a collision scheme: there is no need to decrease the bunch length to increase the luminosity, as proposed in standard upgrade plans for B and fai Factories. This will certainly ease the problems of HOM heating, coherent synchrotron radiation of short bunches, excessive power consumption, etc.. Moreover the problem of parasitic collisions (PC) is automatically solved by the higher crossing angle and smaller horizontal beam size, which makes the beam separation at the PC large in terms of sigmax.
However, a large Piwinski angle itself introduces new beam-beam resonances and may strongly limit the maximum achievable tune shifts？？？ (see for example [13]). This is where the crabbed waist innovation is required. 引入了新的非线性共振，空间电荷场强，刚好需要crabbed waist创新来解决
Tune shift也是调整kseiy的办法，具体？？？

## Slide 15: Ideas and Methods
Crabbed waist + Large crossing angle
Long drift for insertion device/FEL
Notes: 装置沿用双环对撞方案，
单独设计储存环，采用模块化设计标准单元和对撞区，
然后对撞区作为插入段设计组成储存环，
在类似直线对撞机的插入段中优化对撞点的beta函数，使其降低到亚毫米量级，从而提高对撞亮度；
Crab sextupole，非线性补偿
Effect of the Sextupole Finite Length on Dynamic Aperture in the Collider Final Focus, A. Bogomyagkov, S. Glukhov, E. Levichev, P. Piminov
In high luminosity colliders, one of the key requirements is very short bunches, since this allows a decreased betay at the IP, thereby increasing the luminosity. However, betay cannot be made much smaller than the bunch length without incurring an hourglass effect.
Moreover, high luminosity requires small vertical emittance, together with large horizontal beam size and horizontal emittance, to minimize the beam-beam effect. It is, unfortunately, very diffcult to shorten the bunch length sigmaz in a ring.
Large piwinski angle : 有效对撞，提高kseiy, 不需要降低束团长度，因为解决了hourglass效应的问题
Small spot size at the IP, i.e., higher luminosity (Eq. 3.3)
Reduction of the vertical tune shift (Eq. 3.4); and Suppression of vertical synchrobetatron resonances
There are additional advantages in such a collision scheme: there is no need to decrease the bunch length to increase the luminosity, as proposed in standard upgrade plans for B and fai Factories. This will certainly ease the problems of HOM heating, coherent synchrotron radiation of short bunches, excessive power consumption, etc.. Moreover the problem of parasitic collisions (PC) is automatically solved by the higher crossing angle and smaller horizontal beam size, which makes the beam separation at the PC large in terms of sigmax.
However, a large Piwinski angle itself introduces new beam-beam resonances and may strongly limit the maximum achievable tune shifts？？？ (see for example [13]). This is where the crabbed waist innovation is required. 引入了新的非线性共振，空间电荷场强，刚好需要crabbed waist创新来解决
Tune shift也是调整kseiy的办法，具体？？？

## Slide 16: Ideas and Methods
DLSR，7BA
Notes: 以往的beta函数不能降到亚毫米，因为短于束团长度会有hourglass效应，反而减弱亮度；也使得发射度无法降低。
首先是一个低发射度的储存环，Multi-bend Achromat结构，例如7BA

## Slide 17: Ideas and Methods
Design goal
Design goals | value
Luminosity | 1035/(cm2·s)
Brightness | 1017~1021 Ph./s mm2 mrad2 0.1%BW
Beam Energy（1/2 Collision Energy） | 2GeV，1-3.5GeV tunable
Current | 2A
Electron Beam Emittance | 100pm·rad
Lattice | MBA，7-bend
Collision Method | Large Crossing Angle+Crabbed Waist
Circumstance | 800-1000m
Raw estimate，2GeV，2cm/0.5mm betay@ IP，luminosity 7×1034/(cm2·s)
Suppress βy
Notes: 装置沿用双环对撞方案，
单独设计储存环，采用模块化设计标准单元和对撞区，
然后对撞区作为插入段设计组成储存环，
在类似直线对撞机的插入段中优化对撞点的beta函数，使其降低到亚毫米量级，从而提高对撞亮度；
已经优化到的参数：HALS，1.5GeV

## Slide 18
Notes: 薛镇，北京正负电子对撞机重大改造工程（BEPC II）的亮度监测，2010.5

## Slide 19: Important Technologies
Polarized beam
New inject method
Superconducting
Ring based FEL
Ultrahigh vacuum
High precision beam diagnostics, control and feedback
Power supply，Bracing，etc.

## Slide 20: Important Technologies
Polarized Beam
  Polarized electron beam source
  Siberian Snake curing depolarization
New injection method
  Top-up injection
  Minimizing injection-induced detector background
Notes: The Siberian Snake, a series of magnets wrapped around the beam pipe of a particle accelerator.
For a storage ring collider, magnet cycles for injection and acceleration as well as varying beam currents (leading to variation in the beam pipe temperature) degrade the efficiency of the IP tuning. Latest lepton ring colliders, like PEP-II, KEKB, SuperKEKB as well as the proposed FCC-ee and CepC employ top-up injection, where the collider-ring magnets do not need to cycle, and the beam currents are held almost constant, being continually replenished from a full-energy injector. This “top-up injection” requires an additional high-energy, fast cycling or pulsed, injector(s), as well as an appropriate injection scheme. Longitudinal injection appears particularly well suited for top-up, with regard to minimizing injection-induced detector background (with zero or low dispersion across the
IR) and in view of the faster radiation damping in the longitudinal plane.

## Slide 21: Important Technologies
Numerical tracking, computer simulation
  6 dimension particle tracking
  Add electron spin degree of freedom
    8 dimension
  Lie algebra method, genetic algorithm
  Get the optimum parameters
Notes: 为了完成粒子物理实验的要求，对撞束流必须保持一定的极化度。计划研制高品质的极化电子束源，并且在现有六维粒子跟踪计算原理基础上，增加电子自旋自由度，对电子进行八维相空间的数值跟踪计算，通过研究储存环中各种扰动因素对束流极化度的影响，确定最佳方案维持束流极化度。

## Slide 22: Important Technologies
Superconducting tech
  Superconducting magnets
    Quadrupoles, solenoid coils,.etc
  Superconducting cavities
    Storage ring RF cavities, deflecting cavities, .etc
Ring based X-ray
  Icon of 4th generation source: high quality x-ray
    Echo Enabled Harmonic Generation FEL
Notes: 为了满足高对撞亮度和高同步辐射亮度需求，HIEPA需要广泛运用超导技术，因此需要进行预研。超导技术主要应用于超导磁铁与超导腔两类装置。
超导腔技术的研究内容包括：储存环高频腔，超导腔相比常温腔功率利用效率更高，单腔加速电压也更高，可减少加速腔数和总的高频腔束流阻抗，减小束流不稳定性；偏转腔，用于将束流偏转至对撞区，超导腔相比常温腔阻抗更低、偏转电压更高。
超导磁铁与插入元件技术的研究内容包括：储存环超导波荡器或扭摆器等插入元件，可以提供更好品质的同步辐射光；对撞区超导四极铁与超导螺线管线圈，提供更强的磁场以完成本地补偿、压缩束流包络与束团尺寸的目的；以及其他超导磁铁等。

## Slide 23: Important Technologies
Ultrahigh vacuum tech
  Gettering film
  Synchrotron radiation photon absorber
High precision beam diagnostics
  Digital beam signal processing
  New diagnostics(based on cavities, synchtron radiation, etc.)
Power supply, bracing, etc.
  Stability, ripple; vibration monitoring
Notes: 新装置的流强大、束流品质高，磁铁间隙与孔径小，无论是对撞亮度的需要，还是光源亮度的需要，都对真空系统的设计提出了更高的要求。
传统的真空系统的设计、材料选取及材料的表面处理工艺无法满足物理设计要求。如何设计小截面尺寸储存环真空室、降低储存环气压分布梯度、减小材料表面热出气率、抑制二次电子产额，以及迅速排除同步辐射光解吸气体，成为储存环真空系统设计的关键技术。在储存环真空管道的内表面沉积NEG非蒸发型吸气膜（锆钒钛合金材料）就是解决这一系列问题的一个最为有效的方法。当厚度约1000纳米的NEG非蒸发型吸气膜被高温（200℃左右）激活后，就可以作为分布式的真空泵，在储存环细长型真空系统中非常有效的排出气体，降低气压分布梯度，而不受空间尺寸和管道流阻限制。同时抗多次电子撞击（Multipacting），具有较低的同步辐射解光致解吸PSD系数和高温热出气率。
新装置的高亮度使得真空室光子吸收器上的同步辐射功率密度大大提高，同步辐射光子吸收器的高热负载的吸收、大热量的转移和吸收器材料热应力寿命成为储存环真空部件设计的关键性问题。因此为了保证新光源储存环动态气压小于2 纳托（nTorr）和8小时以上的束流寿命，有必要开展新型光子吸收器的设计、加工工艺和材料的选用研究工作。
新装置束流品质相对HLS的大幅度提高，以及高亮度对撞对于对撞区束流位置等参数的精确要求，对束流诊断系统的时间、空间与能量分辨能力等提出了更严苛的需求。计划采用更先进的电子学技术，提高束流诊断电子学系统的信号分辨能力，降低噪声，从而升级现有的束流测量技术。计划发展基于新方法、新设备的多种新型诊断技术，例如基于谐振腔、条带等的束流诊断技术等。举例说明，经过这些改进以后，可以将束流横向位置的分辨率提高到亚微米甚至纳米量级。
新装置的极高束流品质与极高束流稳定性，对加速器电源的品质提出了更高的要求。
前述的磁铁、高频腔、电子束源等各环节，均需要使用电源。脉冲高压电源和磁铁电源的稳定度、纹波、分辨率等均要求在1ppm。相比现有的合肥光源重大维修改造项目升级后的电源稳定度、纹波和分辨率要求大多在100ppm（储存环四极磁铁在25ppm），这一要求提高了1-2个数量级。
由于新装置的束流横向尺寸非常小，要求束流轨道的稳定性达到亚微米量级，根据以往对撞机与光源的建设经验，必须要求支撑系统提供超高的稳定度。地基和储存环支撑系统的震动研究包括：
地基震动研究。运用大地震动监测仪器建立大地震动监测网络，监测光源所在位置的大地震动规律；分析光源运行的受扰敏感频率区域，通过避让、阻尼的方法减少或者消除该不利影响。开展光源选址所在地的地面振动观测及其测量数据的分析与研究，为光源选址提供实验依据，也为光源土建设计提供实测数据和设计依据。
储存环支撑系统的震动研究。研究储存环支撑系统震动和束流关系，建立一套震动的监测系统，首先可以通过实时监测，确定震动可能给束流带来的影响，从而可以通过计算机软件，实时调整控制系统，使束流更加稳定；其次可以建立震动—束流关系模型，在可能的情况下对影响较大因素的系统进行改造，使束流的稳定性得到提高。

## Slide 24: Nsrl：Accelerator Division
1983-2015
  32yrs synchrotron building and running experience
People
  50 scientists & engineers, 30PhDs
  15 professors & associate professors
Plan
  National multidiscipline center, 2015
  ->recruit 50 people, most of them PhD
Notes: 负责人：王琳（代），罗箐
项目组成员：李为民、李京祎、张善才、徐宏亮、王勇、李和廷、徐卫、刘刚文、何志刚、陈念；根据研究进展情况，增加所需要的研究人员。
任务：合肥先进光源的概念设计研究，第一阶段完成光源的概念、布局、lattice等物理设计。
  12人，正高4人，副高4人，博士9人，专职：2人

## Slide 25: Nsrl：Accelerator Division
Accelerator conceptual design team
  2014.7 prepare，2014.11 establish
People
  Experienced consultant
  Young scientists lead
Plan
  Recruit 2 more scientists
  RMB 300k in two years for CDR only
  Apply for key project of National Nature Science Fund
Notes: 负责人：王琳（代），罗箐
项目组成员：李为民、李京祎、张善才、徐宏亮、王勇、李和廷、徐卫、刘刚文、何志刚、陈念；根据研究进展情况，增加所需要的研究人员。
任务：合肥先进光源的概念设计研究，第一阶段完成光源的概念、布局、lattice等物理设计。
  12人，正高4人，副高4人，博士9人，专职：2人

## Slide 26: Future Plan
2015.1-6
  Scheme Layout
  Prototype Lattice
  CDR Ver.0
2015.7-12
  CDR Ver.1
2016.1-12
  CDR Ver.2
  TDR Ver.1
Notes: 合肥光源重大维修改造项目结束后，将获得更多重视。

## Slide 27: conclusion
HIEPAF feasibility
Great Plan, Long way
Meaningful to future of science and scientists

## Slide 28: References
E. Levichev, The project of a Tau-Charm factory with Crab Waist in Novosibirsk, Physics of Particles and Nuclei Letters, Vol5(7), p554-9, Dec 2008
C. Milardi, Present Status of the DA Phi NE Upgrade and Perspectives, INTERNATIONAL JOURNAL OF MODERN PHYSICS A, Vol24(2-3), p360-368, Jan 2009
Lin Wang，HALS advanced research report，2009
Wei Fan，Lin Wang，et al., Physics issues in Diffraction Limited Storage Ring Design, SIIENCE China, Physics, Mechanics & Astronomy, Vol.42(5):p802-807, May 2012
Qing Qin，Zhe Duan，Review and idea about super tau-charm particle factory
Hettel R, DLSR design and plans: an international overive, Journal of Synchrotron Radiation, 2014, 21: 843-855.
Xiaoming Jiang，Jiuqing Wang, et al.，China High Energy Synchrotron Radiation Light Source and Its Test Facility Project， SIIENCE China, Physics, Mechanics & Astronomy, Vol.44(10):p1075-1094, Aug 2014
Frank Zimmermann, Collider Beam Physics, CERN-ACC-2014-0284，Nov 2014

## Slide 29: Thanks for your attention