## Slide 1: Design of SuperKEKB
Y. Funakoshi
KEK
Jan. 16 2015 Workshop on Physics at Future High Intensity Collider @ 2-7GeV

## Slide 2: Contents
Concept of SuperKEKB
Brief Introduction: Design of SuperKEKB
Future plan

## Slide 3: Concept of SuperKEKB

## Slide 4: KEKB B-Factory
Superconducting cavities (HER)
e-
e+
ARES copper cavities (LER)
8 GeV e- 3.5 GeV e+ Linac
e+ target
ARES copper cavities (HER)
Belle detector
KEKB B-Factory
TRISTAN tunnel
♦World-highest Peak Luminosity
    2.11 x 1034cm-2s-1
    Twice as high as design value
♦World-highest Integrated Luminosity
  Total: 1041fb-1 as of June 30th 2010
Crab cavities
1 for each ring
♦Crab crossing (f = 11 mrad)
♦Skew-sextupole magnets
The KEKB operation was terminated at the end of June 2010 for the upgrade toward SuperKEKB.

## Slide 5: SuperKEKB Luminosity Target
SuperKEKB
8x1035 cm-2s-1
2x1034 cm-2s-1
x40 !!
Target integrated luminosity is 50 ab-1.
(~10 year operation)
Notes: As you can see in this trend plot, the target luminosity of SuperKEKB is about 2 order higher than the current B factories.
But how can it be achieved?

## Slide 6: Luminosity of KEKB and SuperKEKB
 | KEKB Acieved |  | SuperKEKB Nano-Beam | 
 | LER | HER | LER | HER
Ibeam [A] | 1.6 | 1.2 | 3.6 | 2.6
βy* [mm] | 5.9 | 5.9 | 0.27 | 0.30
ξy | 0.09 | 0.12 | 0.088 | 0.081
Luminosity [cm-2 s-1] | 2.1 x 1034 |  | 8.0 x 1035 | 
Factor 2
Factor 20
Almost same
40 times higher

## Slide 7: Collision Scheme
d
Nano-Beam Scheme SuperKEKB
Half crossing angle: f
2 f = 83mrad
interaction region << bunch length
interaction region = bunch length
~ 6 mm
~ 300 μm
5-6 mm
10-12 mm
100-150 mm
6-7 mm
Hourglass requirement
Vertical beta function at IP can be squeezed to ~300μm.
Need small horizontal beam size at IP.
→ low emittance, small horizontal beta function at IP.
KEKB head-on (crab crossing)
No crab waist scheme has been assumed at SuperKEKB
P. Raimondi

## Slide 8: Machine Design Parameters
parameters |  | KEKB |  | SuperKEKB |  | units
 |  | LER | HER | LER | HER | 
Beam energy | Eb | 3.5 | 8 | 4 | 7.007 | GeV
Half crossing angle | φ | 11 |  | 41.5 |  | mrad
# of Bunches | N | 1584 |  | 2500 |  | 
Horizontal emittance | εx | 18 | 24 | 3.2 | 4.6 | nm
Emittance ratio | κ | 0.88 | 0.66 | 0.27 | 0.25 | %
Beta functions at IP | βx*/βy* | 1200/5.9 |  | 32/0.27 | 25/0.30 | mm
Beam currents | Ib | 1.64 | 1.19 | 3.6 | 2.6 | A
beam-beam param. | ξy | 0.129 | 0.090 | 0.088 | 0.081 | 
Bunch Length | sz | 6.0 | 6.0 | 6.0 | 5.0 | mm
Horizontal Beam Size | sx* | 150 | 150 | 10 | 11 | um
Vertical Beam Size | sy* | 0.94 |  | 0.048 | 0.062 | um
Luminosity | L | 2.1 x 1034 |  | 8 x 1035 |  | cm-2s-1

## Slide 9: Design of SuperKEKB

## Slide 10
Taking advantage of existing items
・ the KEKB tunnel,
・ the KEKB components
as much as possible!
Major upgrades towards KEKB×40
Add / modify RF systems for higher beam current
Main ring arc and straight section:
Redesign the lattices of both rings to reduce the emittance
Main ring arc section:
LER: Replace all main dipoles
HER: Preserve the present cells
KEKB
Super
KEKB
New beam pipe& bellows
TiN-coated beam pipe with antechambers
New QCS magnet for Nano-beam scheme
New superconducting
final focusing quads near the IP
New e+ source
Positron damping ring
New low
emittance e gun
New design for Near-IR
New and re-use wiggler magnets are mixed:
Oho section (LER&HER)
Nikko section (LER)

## Slide 11: RF system upgrade
Requirements
  Higher beam current
    Higher beam power (~x2), higher HOM power (~x3)
Basic scheme is the same as that of KEKB
  LER: ARES cavities
  HER: ARES and SCC
  KEKB LER: ~<2.0A, HER: ~1.4A -> LER: 3.6A, HER:2.6A (SuperKEKB)
Issues
  How to supply twice higher power to beams
    ARES: 1 klystron supplies 2 cavities with power(KEKB) -> 1 klystron supplies 1 cavity
    Modifications of input coupler
  Coupled bunch instability
    RF feedback, Longitudinal bunch-by-bunch feedback
  Beam gap transient
    Reduce abort gap: 5%(KEKB) -> 2%
  Handling of HOM power
    ARES: No modifications of HOM dampers will be needed.
    ACC: Some modifications of HOM dampers will be needed.
  Low level RF control system
    Analog(KEKB) -> Digital system based on FPGA
      More accuracy and flexibilities

## Slide 12: KEK RF accelerating system
1.2MW CW
Klystron
Nornalconducting cavity（ARES）
Superconducting cavity（SCC）
・ Invented at KEK as RF system for very high beam current storage
・ Stored world’s highest beam current with superconducting RF cavity
・ Suitable for high Vc
HER：ARES x12 + SCC x8
LER: ARES x20

## Slide 14: SCC (superconducting cavity)
Beam pipe: 150Φ
LBP
SBP
electron
  Measures for handling HOM power for the design current
  - Replacing tapers and gate-valves with larger bore ones to reduce loss factor.
  - Adding dampers to disperse HOM power for each damper.

## Slide 15
B
E
C
A
A
B
C
A
B
C
D
E
E
D
C
B
A
D4
D5
D7
D8
D10
D11
LER
HER
ARES cavity
SC cavity
Klystron, HP&LLRF system
Crab cavity
2
2
2
1
2
2
2
2
2
2
2
2
1
1
2
1
Type “A” power supply (for two klystrons)
Type “B” power supply (for one klystron)
1
OHO
FUJI
NIKKO
F
E
A
B
C
D
C
B
A
D4
D5
D7
D8
D10
D11
2
2
2
2
2
2
2
2
2
2
2
2
2
2
D
C
B
A
2
E
F
D
2
2
F
E
2
F
E
D
C
B
A
H
G
F
E
D
C
B
A
D
C
B
A
D
C
B
A
D
C
B
A
SuperKEKB-RF
(ultimate)
KEKB-RF
remove 4 ARES
convert to LER
add 2 ARES
add 2 SC (option)
add 2 klystrons, HP&LL
add 2 power supplies
add 2 more klystrons, HP&LL,
add 1 more power supply
add 5 klystrons, HP&LL
add 3 power supplies
E
F

## Slide 16: Coupled bunch instability (CBI) with ARES (LER)
radiation damping time: ~ 20ms

## Slide 17: Magnet system upgrade
Basic design concepts for SuperKEKB
  Use the KEKB tunnel
  Use the components of KEKB as much as possible;
    Preserve the present cells in the HER
    Replace dipole magnets, keeping other main magnets in the LER arcs.
Major upgrade plan to achieve new low emittance beam optics for both LER and HER.
  Replace dipoles and change the wiggler layout for LER
  Install wiggler magnets in HER
  Replace IR magnets

## Slide 18: LER wiggler magnets
Main purpose of wiggler magnets is shortning of radiation damping time.
Wigglers are also used for emittance control.
Smaller dispersion (x) makes the emittance smaller.
x at wiggelers will be changed from 10mm(KEKB) to 5mm(SuperKEKB).
Emittance created in the wiggler sections will be about 1/3 with similar damping.
Emittance is determined by a balance between radiation damping and radiation excitation.
Smaller x makes H smaller.
Weaker magnetic field makes excitation weaker.
Longer wigglers make strong damping
<5mm
<10mm
wiggler magnets
wiggler magnets
B2P 0.89m(KEK) -> 4m
ex = ~6nm(KEKB) -> 1.9nm

## Slide 19: Vacuum system upgrade
Beam pipes
  New beam pipe: Beam pipes with antechambers.
    Low beam impedance, Higher strength against intense SR
    Less photoelectron effect to position beam [LER] : Electron-cloud formation is suppressed.
    Most of HER beam pipes will be reused.
  Add more powerful countermeasures against electron cloud (EC) effects [LER].
    Solenoid field, TiN coating
    New technique: Clearing electrode, Grooved surface
Main components
  Bellows chambers, gate valves, movable masks (collimators), stoppers, etc. are designed to fit the beam pipes.
    Higher strength against higher beam currents
Main upgrade is the replacement of beam pipes and other main vacuum components.

## Slide 20: Beam pipes
Beam pipes with antechambers
  Small effect of photoelectrons, low beam impedance, low SR power density
  The cross section should fit to the existing magnets.
  Aluminum alloy is available for LER arc section . Copper is required for wiggler section (and HER).
  TiN coating for suppressing electron cloud density
Beam
SR
NEG strip
Conductance:
~ 88 l/s/m
t6 mm
Aluminum
(A6063)
BPM
Copper
(OFC)
Q magnet
Concept

## Slide 21
 | KEKB (e+/e-) | SuperKEKB (e+/e-)
Charge [nC] | 1/1 | 4/5
Normalized emittance[mm] | 2100/300 | 100/50 (H)
 |  | 20/20 (V)
SuperKEKB requirements (tentative)
Linac upgrade

## Slide 22
Newly introduced Damping Ring !

## Slide 24: Issues
IR design and dynamic aperture
Low emittance tuning
Magnet alignment strategy
Beam-beam related issues
IP orbit control
Beam loss and beam injection
Electron clouds
Detector beam background

## Slide 25: IR design and dynamic aperture
One of the key issues at SuperKEKB
  Success of SuperKEKB largely depends on how low values of IP beta-functions will be achieved with enough dynamic aperture.

## Slide 26: Final Focus Quadrupoles (QCS’s)
KEKB
Full crossing angle：22 mrad
QCS
QCS
QC1
QC1
QC2
QC2
QC2
QC2
QC1
QC1
QC1
QC1
SuperKEKB(Nano Beam Scheme)
Full crossing angle：83 mrad
QC2
QC2
QC2
QC2
e+
e+
e-
e-
QCS’s are common
SR from QCS’s are reduced.
IP
IP
Independent QCS’s
L*= 1.4m (QCS-L)
1.7m (QCS-R)
L*= 1.2m (QC1E)
0.73m (QC1P)

## Slide 27
Y. Ohnishi

## Slide 28: Corrector coils of QCS
Dipole and skew dipole coils make a beam-line geometry and correct dispersions.
Skew quadrupole coils correct x-y couplings.
Sextupole and skew sextuple coils correct error field due to a misalignment of quadrupole coils. This error field affects the dynamic aperture significantly.
Octupole coils at QC1 and QC2 enlarge a transverse aperture.
HER cancel coils correct sextupole, octupole, decapole and dodecapole leakage field from QC1P in LER.

## Slide 29
Y. Ohnishi

## Slide 30
Y. Ohnishi

## Slide 31: Touschek Lifetime
Touschek lifetime depends on dynamic aperture.
Efforts to widen dynamic aperture
  Careful design of QCS magnets to minimize higher multipoles etc.
  Careful IR design: LCC, x-y coupling correction etc.
  Optimization of octupoles, sextupoles, skew-sextupoles
w/o machine errors
Y. Ohnishi

## Slide 32: Beam lifetime
 | KEKB (design) |  | KEKB (operation) |  | SuperKEKB | 
 | LER | HER | LER | HER | LER | HER
Radiative Bhabha | 21.3h | 9.0h | 6.6h | 4.5h | 28min. | 20min.
Beam-gas | 45ha) | 45ha) |  |  | 24.5min.b) | 46min. b)
Touschek | 10h | - |  |  | 10min. | 10min.
Total | 5.9h | 7.4h | ~133min. | ~200min. | 6min. | 6min.
Beam current | 2.6A | 1.1A | 1.6A | 1.1A | 3.6A | 2.6A
Loss Rate | 0.12mA/s | 0.04mA/s | 0.23mA/s | 0.11mA/s | 10mA/s | 7.2mA/s
a) Bremsstrahlung
b) Coulomb scattering, sensitive to collimator setting
As for loss rate, beam loss accompanied with the beam injection should be added.
4nC@25Hz
2.9nC@25Hz

## Slide 33: Low emittance tuning
The design vertical emittance of SuperKEKB is very small compared to those of existing colliders.
The low vertical emittances have been achieved in SR machines. However, low emittance tuning in colliders is much more difficult.
One of the key tuning issues at SuperKEKB will be low emittance tuning.

## Slide 34: SuperKEKB beam-beam simulation
K. Ohmi
Smaller (single beam ) vertical emittance gives higher luminosity.
Much lower vertical emittance than the design (about half) will be needed to achieve the design luminosity.
Strong-strong method (PIC)
For the long-rage force, the gaussian distribution was assumed.
 | LER | HER
ex [nm] | 3.2 | 4.6
ey [pm] | 8.64 | 11.5
k [%] | 0.27 | 0.25
SuperKEKB design
SuperKEKB design luminosity

## Slide 35: Comparison of emittances of colliders
Existing colliders
Future colliders
From Beam Dynamics Newsletter No. 31
Courtesy of F. Zimmermann, H. Burkhardt and Q. Qin
LEP3
TLEP-H

## Slide 36
KEKB method of optics correction
SVD solver

## Slide 37: Simulation for SuperKEKB with machine errors
Simulation was done by H. Sugimoto in case of HER.
Assumed machine errors
Corrections
  Closed orbit, x-y coupling, beta-beat, dispersions (KEKB methods)
 | sx = sy [mm] | sq [mrad] | DK/K
Normal Quad | 100 | 100 | 2.5 x 10-4
Sextu. | 100 | 100 | 2.5 x 10-4
Bend. | 0 | 100 | 0
QC1, QC2 | 100 | 0 | 0
BPM | 0 | 10 x 103 | 2mm (resolution)
Machine errors are created randomly with gaussian distributions.

## Slide 38: Results of simulation (HER)
Dynamic aperture after LET.
Vertical emittance distribution after LET
100 samples
No errors
H. Sugimoto
This simulation shows that the target vertical emittance is achievable.
(This simulation does not include alignment error in LCC section.)
Target

## Slide 39: Dynamic aperture with different types of errors
No errors
Rotation errors of quadruples seems most dangerous.
We may have to rethink tolerance of rotation errors of normal quadrupoles.
H. Sugimoto

## Slide 40: Magnet alignment strategy at SuperKEKB
The target positions of the initial alignment of SuperKEKB is a smoothed curve made from present (2013 )magnet positions (not on a plane).
The tolerance of magnets alignment around the target curve is the same as KEKB.
  Position error: 100 mm (1 s)
  Rotational error: 100 mrad (1 s)
    We have to rethink about this?
We will need special care for the alignment of the magnets around the local chromaticity correction.

## Slide 41: Effects of Tunnel deformation at SuperKEKB HER
Tunnel deformation observed at KEKB
- In the construction period of KEKB (1998), all magnets were aligned on the same plane.
- A large subsidence has been observed:
~ 2mm/year and still in progress.
Target (5.8pm)
Vertical emittance
-If the alignment error around the V-LCC (vertical local chromaticity correction) area is excluded, the vertical emittance can be preserved well below the target value with optics corrections.
- As for the alignment error of V-LCC, we will need a special care. This is a remaining problem.
A. Morita

## Slide 42: Beam-beam related issues
Beam lifetime shortening with beam-beam effects
Luminosity degradation
  The design luminosity was determined based on the strong-strong beam-beam simulation.
  It has been shown that beam-beam + lattice nonlinearity and space charge effect may degrade the luminosity.

## Slide 43: LER Dynamic Aperture
beam-beam
aperture
lost
Y. Ohnishi
If the crab waist scheme is available, the situation will be much improved…
We are still studying this issue. Tune survey….

## Slide 44: HER Dynamic Aperture
beam-beam
aperture
lost
Y. Ohnishi

## Slide 46: Future Plan

## Slide 47: SuperKEKB commissioning phases
Phase 1
w/o QCS and Belle II
vacuum scrubbing
basic machine tuning
Phase 2
w/QCS and Belle II
w/o Vertex detector
BKG study
Luminosity tuning
Target luminosity: 1 x 1034 cm-2 s-1
Phase 3
Physics Run
Luminosity tuning

## Slide 48: Status of SuperKEKB
KEKB operation finished on June 30th 2010
Just after this, the construction works for SuperKEKB started.
The upgrade works for Phase 1 are approaching completion.

## Slide 49
SuperKEKB/Belle II Schedule (possible scenarios)
JFY2018
2018
2014
JFY2014
2015
2016
2017
JFY2015
JFY2016
JFY2017
Japan FY
now
Calendar
Power restriction
in summer
phase 1
phase 2
phase 3
Start-up
QCS, Belle II install
VXD install
w/o QCS
w/o Belle II
w/ QCS
w/ Belle II (no VXD)
w/ full Belle II
phase 1
phase 2
phase 3
Start-up
QCS, Belle II install
VXD install
Current plan ongoing
w/o QCS
w/o Belle II
w/ QCS
w/ Belle II (no VXD)
w/ full Belle II
phase 1
phase 2
phase 3
SuperKEKB Construction
Start-up
QCS, Belle II
VXD install
Original plan
w/o QCS
w/o Belle II
w/ QCS
w/ Belle II (no VXD)
w/ full Belle II
phase 1
phase 2
Start-up
QCS, Belle II install
VXD install
w/o QCS
w/o Belle II
w/ QCS
w/ Belle II (no VXD)
JFY2014 Operation budget cut by 12 Oku-Yen
More realistic estimation of schedule: 11 months for phase 1->2, 6 for phase 2->3.
SuperKEKB Construction
SuperKEKB Construction
SuperKEKB Construction
Power restriction
in summer
Power restriction
in summer
phase 3
w/ full Belle II
Power restriction
in summer
(B) Desirable JFY2015 budget
Possible scenarios discussed in B2EB, B2GM and BPAC on Nov. 2014.
(A) Conceivable JFY2015 budget
Actual scenario depends on the budget.

## Slide 50: Backup slides

## Slide 51
“to do” list:
- off-momentum optics correction
- identify dominant lattice nonlinearities in both rings affecting luminosity
- develop nonlinear optics measurement & correction scheme
optimize nonlinear optics & DA including space charge & beam-beam effect
compensation scheme for space charge
correction scheme with/for crab waist

## Slide 53: Beam background
At SuperKEKB with x40 larger Luminosity, beam background will also increase drastically.
  Touschek scattering
  Beam-gas scattering
  Synchrotron radiation
  Radiative Bhabha event: emitted g
  Radiative Bhabha event: spent e+/e-
  2-photon process event: e+e-e+e-e+e-
  etc…
e-
e+
e-
Beam-origin
Luminosity dependent
Notes: In this slide, I have listed up variety of possible beam background sources at SuperKEKB.
Among these background sources, so-called “Touschek scattering” will be the most difficult one to cope with, which I will explain in more detail in the following slides.

## Slide 54: Impact on detector
Assuming design luminosity, BG impact on detector performance(occupancy, tracking/PID performance etc..) is tolerable.
Assuming 10 years operation at design luminosity, most of our detector components are safe for radiation damage/neutron flux.
  except for TOP PMT photocathode lifetime, which needs further x2 reduction.
Gammas in BGshower reach TOP quartz bar and generate electrons by Compton scattering and etc.. Those electrons emit Cerenkov photons and those photons reach PMT photocathode.

## Slide 55: Collimators
Horizontal collimators are effective to reduce Touschek BG in IR area
To reduce IR loss of beam-gas Coulomb BG, very narrow (~2mm half width) vertical collimator is required
TMC instability is an issue, low-impedance design of collimator head is important
Should withstand ~100GHz loss (tungsten)
Precise control of collimator width is important (otherwise IR loss rapidly increase)
Life time | Touschek | Beam-gas Coulomb | Rad. Bhabha
LER | 10 min. | 25 min | 28 min.
HER | 10 min. | 46 min. | 20 min.
IR loss ¦s¦<4m | Touschek | Beam-gas Coulomb | Rad. Bhabha
LER | 250 MHz | 90 MHz | 0.6GHz*
HER | 30 MHz | <10 MHz | 0.5GHz*
*Effective rate
Vertical collimator

## Slide 56: Status of SuperKEKB/Belle-II project
Hiroyuki Nakayama (KEK) 2013.01.31 Bonn university
KEKB and Belle(-I): successful
Upgrade to SuperKEKB/Belle-II
Beam background estimation
Assumed audience:
masters&PhD students as well as postdocs and staff working on ATLAS, ILC, Ice Cube, and Belle (II)

## Slide 57: Tungsten shield inside QCS cryostat
QC2RP
QC2RE
QC1RP
QC1RE
Put as much tungsten as possible around the beam pipe
to stop showers generated by beam loss

## Slide 58: Schedule around near-IR
Phase 1 (January 2015~)
  Magnet
    Fabrication of new magnets: FY2013
    Installation: June 2014~
  Beam pipe
    Fabrication
      Outer region: FY2013
      Central region: FY2014
    Installation: August 2014~
  Mini shield
    Fabrication: FY2013
    Setting with the shield support stage: May 2014(?)
Phase 2 (Installation: June-December 2015,
Beam: January 2016~)
  IP chamber
    Fabrication in progress
  Bellows and BPM pipe
    Design depends on a installation scenario
    Fabrication: FY2014
  Ta beam pipe
    Model test: 2011-2012
    Design study: FY2013
    Fabrication: FY2014
  QCS moving stage
    QCSL: FY2013
    QCSR: FY2014
  Concrete shield
    Design: FY2013
    Fabrication: FY2014
58
Au coat, 10~20 mm
Be
f 20
f 10
Cu coat, ~10 mm
Cu coat, ~10 mm
IP chamber (part)
go as planned
Phase 1
Kanazawa

## Slide 59: Commissioning phase 0 (2013 Sep. ~ 2014 Dec.)
Machine condition
  SuperKEKB rings: construction
  Linac commissioning in parallel with its construction
Tuning items
  To be covered by the next talk.
Nov. 11 09:50
Injector commissioning and issues 30'
Speaker: Masanori Satoh (KEK)

## Slide 60: Commissioning phase 1 (2015 Jan. ~ June)
Machine condition
  No QCS, No solenoid (no Belle II), No beam collision
Tuning items
  Linac tuning (if necessary)
  Basic commissioning of machine (~ 1.5 month)
    Injection tuning, Hardware check and bug fix, software bug fix
  Vacuum scrubbing (>~3 months)
    Belle II people request enough vacuum scrubbing in this stage (before Belle II roll-in). At least one month with beam currents of 0.5 ~ 1 A.
  Damping ring commissioning (start from May 2015)
    Beam injection with damping ring
  Detector beam background
    Study with Beast detectors, check of collimator system (two new-type collimators in LER)
  Some optics tuning
    With day-1 optics
    Low emittance tuning w/o Belle-II solenoid
  Study of beam instability (FII, e-cloud)
    Tuning on bunch-by-bunch feedback
Nov. 13 09:20
Bunch-by-bunch feedback 20'
Speaker: Makoto Tobiyama (KEK)

## Slide 61: Phase 1 optics (HER)

## Slide 62: Vacuum scrubbing at KEKB （HER/LER）
HER
LER
HER
LER

## Slide 63: Damping ring commissioning
We have no concrete commissioning plan so far. We need to make a plan.
Nov. 12 11:20 DR LTR, RTL 20'
Speaker: Mitsuo Kikuchi (KEK)
Nov. 12 11:40 DR beam monitors 20'
Speaker: Hitomi Ikeda (KEK)

## Slide 64: Commissioning phase 2 (2016 Jan. ~ May)
Machine condition
  w/ QCS, w/ Belle II (w/o VXD),TOP detectors partially installed, full accelerator tuning, no physics experiment
Tuning items
  Optics tuning
    Tentative target values of IP beta’s: βx*: x4, βy*: x8
    Optics tuning with QCS and Belle II solenoid
    Low emittance tuning w/ Belle II solenoid
    Optics tuning w/ beam collision
  Detector beam background
    Study with Belle II detector, test of continuous injection
  Increase of beam currents (instability, RF power, vacuum issues)
    Detector background may possibly give some restriction.
    Continue upgrade for RF system (support ~70% of design beam currents)
  Beam collision tuning
    Orbit feedback (fast feedback, dithering system)
    Collision tuning w/ “Nano-Beam” scheme
  Luminosity tuning
    Tuning knobs (x-y coupling at IP etc.)
    Target luminosity: 1 x 1034 cm-2 s-1 (design of KEKB)
Feb. ~ June

## Slide 65: Detuned Optics (4x8)
βx*: x4, βy*: x8, x-y coupling =2 %, ξy ~ 0.025, ILER = 1 A.
Example of machine parameters for 1034 cm-2s-1

## Slide 66: Commissioning phase 3 (2016 Oct. ~ )
Machine condition
  Full set of Belle II, Physics experiment will start.
    Maybe some TOP counters will be delayed.
Tuning items
  Optics tuning
    Toward design values of IP beta’s
      Maybe it will take several years.
    Low emittance tuning:
      Design values for vertical emittances are very small. Demonstration of feasibility of TLEP.
    Optics tuning w/ beam-beam effect
  Detector beam background
    Establishment of continuous injection (azimuthal VETO)
  Increase of beam currents
    Design values are as twice high as those of KEKB.
  Luminosity tuning
    Study on effects of lattice non-linearity and space-charge
    Stability of tuning will be an important issue. (continuous optics correction?)

## Slide 67: Difficulty of SuperKEKB
The commissioning phase 3 will be the most critical phase.
  The true difficulty of SupeKEKB will be recognized in this phase.
    Corrections of machine errors seem the key issue.
    Stability of machine condition seems important.
      Continuous optics correction?
  Some unknown difficulties will possibly appear.
  My personal impression: Important milestone of luminosity: 1 x 1035 cm-2 s-1.

## Slide 68: SuperKEKB luminosity projection
Goal of Belle II/SuperKEKB
9 months/year
20 days/month
Commissioning starts
in early 2015.
Shutdown
for upgrade
Integrated luminosity
(ab-1)
Peak luminosity
(cm-2s-1)
Calendar Year

## Slide 69: QC1P, QC2P
QC2RP
K1=0.865
QC2LP
K1 = 0.860
QC1LP
K1 =-1.72
QC1RP
K1 = -1.72

## Slide 70: QC1E, QC2E
QC2RE
K1=0.558
QC2LE
K1 = 0.653
QC1LE
K1 =-1.21
QC1RE
K1 = -1.14

## Slide 71: Facilities
Storage and staging areas needed for magnet and vacuum components.
Need increased cooling water for klystrons and magnets:
  24 klystrons for ARES cavities, 8 klystrons for SCC
  Magnet cooling water needs double (4 plants -> 8)
Electricity:
71
KEKB/KEK total
Electricity Consumption: June-09
(Design option) | KEKB:MW | ΔMW | KEK:MW | ΔMW
Present(Average) | 45 |  | 64 | 
Nano Beam: June-09 | 70.7 | 24.3 | 96 | 32
Upgrade: Feb.-09 | 94.8 | 49.8 | 120 | 56
Super: ‘07-July | 102.6 | 57.6 | 128 | 64
Recent Design(Feb.-10): Add 2 ARES units--> +(3~4)MW
M. Ono

## Slide 72: Overall budget (original)
JFY2010 | JFY2011 | JFY2012 | JFY2013 | JFY2014 | Total
75.0 | 10.5 | 14.5 | 0 | 0 | 100.0
0 | 41.6 | 40.2 | 61.6 | 46.7 | 190.0
0 | 4.5 | 12.4 | 7.2 | 0 | 24.1
75.0 | 56.6 | 67.1 | 68.8 | 46.7 | 314.1
Supplied | Supplied | Supplied |  |  | 
JFY2010
JFY2011
JFY2012
JFY2013
JFY2014
JFY2015
JFY2016
Very Advanced Research SP (100 Oku-Yen)
Other budgets for construction (214 Oku-Yen)
Operation budget (continues - - - )
SuperKEKB commissioning
We are here
Budget
  Total construction budget is 314 Oku-Yen for Rings, Injector, and Belle-II.
  Most of the budget comes year-by-year based.
  Operation budget is expected in FY2014 and later.
VARSP
Others
Buildings
Total
Status
Unit: Oku-Yen (~1.1M$)

## Slide 73: Effect of mis-alignment of SX and Q
HER(Quad rotation)
  Coupling term: .0010816287630558967
  Dispersion term: 3.748599954860665e-05
HER(Sextu vertical misalignment)
  Coupling term: .044995709319378976
  Dispersion term: .0045765442050508375
Notes: （３）南アークはPSの建物の下を通っている。他は開削して埋め戻しているがここは添付資料にあるようについたてをつくって埋め戻している（添付資料の１頁目：IWAA2012山岡さんの発表より）。
トンネルの下にちゃんと埋め戻し土が入って行かなかったのではないか。

## Slide 76: Improvement plan for HER Aperture
from A. Morita
No room for beam-beam kick.
Synchrotron injection scheme is inevitable
±0.65%
[II]-(2)
N. Iida
Notes: This graph shows the dynamic aperture of HER.
This red line shows the injected beam.
There is no room for beam-beam kick.
Synchrotron injection scheme is inevitable.

## Slide 77: Impact on detector
Assuming design luminosity, BG impact on detector performance(occupancy, tracking/PID performance etc..) is tolerable.
Assuming 10 years operation at design luminosity, most of our detector components are safe for radiation damage/neutron flux.
  except for TOP PMT photocathode lifetime, which needs further x2 reduction.
Gammas in BGshower reach TOP quartz bar and generate electrons by Compton scattering and etc.. Those electrons emit Cerenkov photons and those photons reach PMT photocathode.
TOP: Time-of-Propagation counter, detect ring image Cerenkov radiation for particle ID

## Slide 78: Preliminary results on dynamic aperture study with sextupoles for crab waist
We have considered that the crab waist scheme can not be used at SuperKEKB due to the degradation of dynamic aperture. Now, we have started to study this scheme more seriously.
0%
50%
100%
50%
100%
before optimization
before optimization
with optimization
with optimization
H. Koiso
We are collaborating with people in BINP.

## Slide 82: RF-Gun development strategy for SuperKEKB
Cavity : Strong electric field focusing structure
  Disk And Washer (DAW) => 3-2, A-1(test)
  Quasi Traveling Wave Side Couple => A-1
  => Reduce beam divergence and projected emittance dilution
Cathode : Long term stable cathode
  Middle QE (QE=10-4～10-3 @266nm)
  Solid material (no thin film) => Metal composite cathode
  => Started from LaB6 (short life time) => Ir5Ce has very long life time and QE>10-4 @266nm
Laser : Stable laser with temporal manipulation
  LD pumped laser medium => Nd / Yb doped
  Temporal manipulation => Yb doped => Minimum energy spread

## Slide 83
Normal side couple structure
Quasi traveling wave sidecouple structure
Design of a quasi traveling wave side couple RF gun
Quasi traveling wave side couple has stronger focusing and accelerated gradient than DAW.

## Slide 84: Ir5Ce Cathode
Chart: Energy density of cleaning laser(μJ/mm2)
| 0.0 | 100.0 | 200.0 | 350.0 | 450.0 | 650.0 | 1000.0
LaB6@266nm | 2.551e-06 | 1.212e-05 | 2.191e-05 | 8.25e-05 | 5.314e-05 | 5.314e-05 | 6.273e-05
LaB6@532nm | 2.2662e-06 | 2.115e-05 | 2.6172e-05 | 9.6194e-05 | 0.00017493 | 3.8669e-05
Ir5Ce@266nm | 3.507e-06 | 2.215e-05 | 5.51e-05 | 8.61e-05 | 0.0001019
Quantum efficiency improvement by Laser cleaning
[SUPER-KEKB e Linac]
Laser Power ; 233μJ/pulse
（λ=266nm）
Target value ; 5nC
HV = 16kV
Vacuum ; 5.8×10-6 Pa
Cleaning time ; 10 min
Condition
×２０
Max QE = 1.00×10-4
Laser cleaning
×20
Lower energy density is enough to activate Ir5Ce
QE = 5.00×10-6
Non activation
LaB6
Carbon
Oxigen
SEM-EDX
Ir5Ce
Carbon
SEM-EDX
No oxidization is observed

## Slide 85: Properties of laser medium
LD Pump
(808nm)
Nd:YVO4
Nd:YAG
SHG(532nm) 40%
FHG(266nm) 20%
5HG(213nm) 3%
τ～200μs, 40%
Nd-doped
Yb-doped
Ti-doped
LD Pump
(941/976nm)
Yb-glass
Yb:YAG
Yb:BOYS
1064nm
808nm
941/976nm
1040nm
τ～900μs, 40%
Pump
(808nm)
Nd:YAG
SHG
40%
1064nm
808nm
Ti:Sapphire
532nm
800nm
τ～3μs, 40%
τ=200μs, 40%
○ 4-state laser is easy to operate.
○ High power pump LD is available.
○ Large crystal is available
× Pulse width is determined by SESAM. (Gaussian)
○ Wide bandwidth => pulse shaping
○ Long fluorescent time => High power
○ Fiber laser oscillator => Stable
○ Small state difference
× ASE
× Absorption
○ Very wide bandwidth
○ High breakdown threshold
× Low cross section
× Short fluorescent time => Q-switched laser is required for pumping
Pump
TW laser is based on Ti-Sapphire
SHG(520nm) 40%
FHG(260nm) 20%
5HG(208nm) 3%
SHG(400nm) 40%
THG(266nm) 20%
FHG(200nm) 10%
Best for RF-Gun
Nd laser system for 3-2 RF-Gun
Ti:Sapphire laser system for beam monitor.

## Slide 86: Yb laser system (Present status)
Yb Fiber Laser
frep=52MHz→10MHz
frep=1MHz→50Hz E=1mJ
Amplitude modulator x 2
Fiber strecher
& wavelength selection
Yb:YAG
Multipass
Amplifier ×3
Pulse
Compression
Yb:YAG
Regenerative
Amplifier
Yb Fiber Amplifier
Yb Fiber
Oscillator
Yb Fiber
Amplifier x 2
(20W + 70W pump)
λ0→1030 - 1040nm
Rotating Yb:YAG
Yb:YAG laser
frep=52MHz
Yb Fiber
Amplifier
(70W pump)
Pulse picker
frep=10 MHz→50 Hz
Wavelength
conversion
A few mJ @ 25
A few 10 mJ @ 1035nm
Yb:YAG
Multipass
Amplifier

## Slide 87: IP orbit control
The IP orbit control to maintain an optimum beam collision is more difficult than the KEKB case.
IP orbit is very sensitive to the vibration of QCS (QC1, QC2) magnets.
 | KEKB | SuperKEKB
ey | 150pm | ~8.6pm (LER)
by* | 5.9mm | 0.27mm(LER)
sy* | 940nm | 48nm

## Slide 88: QCSL vertical position oscillation (measurement) and orbit change (tracking) : SuperKEKB HER
Vertical orbit at IP
(simulation)
QCSL vertical position
(measurement)
-> QC1L (HER)
200nm -> ~4sy*
If the QC1L magnets of SuperKEKB vibrates with the same amplitude of the QCSL of the KEKB, the orbit change at IP amounts to 4sy*.

## Slide 89: Countermeasures
Reinforcement of supports for QCS magnets
Rely on the coherency of the oscillation of QC1P and QC1E (QC2P and QC1E).
Fast orbit feedback

## Slide 90: Electron cloud issues
The single bunch instability is main concern.
  Leads to increase in emittance
  Coupled bunch instabilities will be cured by feedback system.
Simulation and calculation by Ohmi, et al.
E [GeV] | = 4.0 |  |  |  | 
g | = 7828 | Nb | = 6.25E+10 |  | 
ns | = 0.026 | Qb[C] | = 1.4E-08 | (1.4 mA/bunch) | 
 |  | Sb [m] | = 1.2 | (4ns) | 
sz [m] | = 6.E-03 | l [C/m] | = 5.2E+12 | (Qb/2/sz) | 
c [m/s] | = 3.E+08 | s y [m] | = 2.E-05 |  | 
K | = 11 | s x [m] | = 2.E-04 |  | 
Q | = 7 |  |  |  | 
re [m] | = 2.80E-15 | we | = 5.46E+11 | K = we sz/c | 
b y [m] | = 25 | we sz/c | = 10.9 | Q = Min(Qnl, we sz/c) | 
L [m] | = 3016 |  |  | Qnl ~7 | 
K. Ohmi , KEK Preprint 2005-100 (2006)
  Here,
Target: 1E11
ρth [e-/m3] =1.59E11
Threshold of density
Y. Suetsugu

## Slide 91: Latest simulation result on the threshold value of instability
Simulation with PEHTS2 by D. Zhou and K. Ohmi
  With uniform beta functions and uniform electron cloud density along the ring, the threshold for electron cloud density is about 5.0 x 1011 m-3.
  With realistic beta functions and uniform electron cloud density along the ring, the threshold reduces to about 1.6 x 1011 m-3.
  With realistic beta functions and estimated s-dependent electron cloud density along the ring, the threshold is about 5.0 x 1011 m-3.
Nov. 12 14:20
Beam-beam and e-cloud 20'
Speaker: Kazuhito Ohmi (KEK)

## Slide 92: Countermeasures
For the upgrade of the vacuum system for SuperKEKB, the electron cloud is a key issue.
Drift section | Antechamber +Solenoid +TiN Coating
Q and Sx mag. | Antechamber +Solenoid +TiN Coating
Bend section | Antechamber +Groove+ TiN Coating
Wiggler section | Antechamber +Electrode (Cu)
Countermeasures are carefully chosen based on the various studies.
Y. Suetsugu

## Slide 93: Countermeasures for electron clouds
Drift section: Antechamber + TiN coating
Groove
Inside view
Electrode
Wiggler section:
Antechamber + Clearing electrode
Y. Suetsugu

## Slide 94: Expected electron density
ne after applying countermeasures: estimated from experiments (Red)
Compared with results of CLOUDLAND (Blue)
  dmax=1.2, Solenoid field=50G (ne=0), Antechamber; photoelectron yield =0.01 (1/10)
ne of approx. 1/5 of the target value is expected.
Target value for ne: ~1x1011
Condition | ne [m-3]
Circular Cu chamber [KEKB beam pipe] | 5.2E12
+Solenoid at Drift (1/50) | 4.7E11
+Antechamber (1/5)+TiN (3/5) | 5.7e10
+Electrode in Wiggler (1/100) | 3.5e10
+Groove in Bend (1/4) | 2.0E10
KEKB~3x1011
If the latest simulation result on the threshold is true, there is a margin of a factor 25!
Y. Suetsugu

## Slide 95: Beam injection issues
Dynamic aperture with beam-beam effect in LER
  Estimated injection efficiency with beam-beam
    ~84% w/o machine errors
    Requirements to Linac beam (emittance etc.) will be considered after we finish the investigation on dynamic aperture with beam-beam effects.
HER injection
  Transverse ring acceptance is marginal with the design optics to keep enough injection efficiency.
  Maybe, we will need to switch to the “synchrotron injection” in the process of squeezing beta functions at IP.
Synchronization issue between Linac and SuperKEKB rings
  We will introduce a damping ring.

## Slide 96: Dynamic Aperture with beam-beam LER : w/ damping
sx@Injection = 0.55mm
-> 12sx ~ 6.6mm
DE / se
Dx / sx
sler_1686
Injection efficiency: ~ 84%
w/o machine errors
Linac beam:
gex ~117mm , gey ~2.5mm

## Slide 97: Continuous injection
At SuperKEKB, the continuous injection (top-up injection) is indispensable, since the beam lifetime is very short.
  Max. 50 Hz (e- + e+)
  Azimuthal VETO (at KEKB not azimuthal 3.5msec after injection)
Before continuous injection
After continuous injection
Gain in integrated luminosity at KEKB: ~30%
8 hours
8 hours

## Slide 98: Issues related to present ferrite HOM damper system
Ferrite material is sintered on a copper base pipe by hot isostatic press (HIP) method.
Ferrite
  Thickness: 4 mm
  Ferrite surface temperature ：190℃ @2.6 A
  Gas release from ferrite triggers high voltage breakdown
Cooling water
  Water temperature＜60℃
    To prevent air bubbles
    Deaeration system >60℃
Chiller unit
  Total heat load：46 kW per cavity
  Cooling capacity （with a safety margin）：60kW
  Cooling capacity of present chiller: 27 kW
HIPped ferrite （Thickness：4mm）
Cupper pipe (3/8”) for cooling channel
Flange: Stainless steel
Beam current | SBP load | LBP load
(A) | (kW) | (kW)
2 | 12 | 15
2.6 | 20 | 26