## Slide 1: Beam Polarization I. Koop BINP, 630090 Novosibirsk, Russia
Workshop on Physics at HIEPA, Hefei, China
13-17 January 2015

## Slide 2: Outline
General polarization scenario for HIEPA – tau-charm factory
Review of Polarized Electron Source issues
Longitudinal polarization schemes
Polarization estimates for HIEPA
Siberian Snake optics and parameters
Energy calibration issues
Concluding remarks

## Slide 3: Polarization scenario for HIEPA
Polarized electrons from a photo-emission gun with a full production rate: Ṅ≈ 1-5 · 1011 s-1 – regular or to refill
Damping Rings (E≈1 GeV) to store, cool and self-polarize positrons (for energy calibration purpose only?) and electrons as well (in separate ring!)
Odd (1 or 3) number of Siberian Snakes to provide the longitudinal polarization at IP in wide energy range
Continuous energy monitoring in both collider rings using the Compton backscattering technique, validated by the resonance depolarization (with Snakes switched off!)

## Slide 4: PES subsystems
Glove box for photocathode etching
Loading chamber
Preparation chamber
Magnetic manipulators
100-200 kV photo-gun (pulsed, 50 Hz)
Ultrahigh vacuum system (pumps, heaters, NEG, sensors): p<10^(-11) mbar
Ti-Sapphire drive laser + optics
Z-shape or Wien-type spin-manipulator
100-200 keV beam line
Mott-polarimeter
Sub-harmonic pre-buncher/accelerator (400 keV ?)
Alpha-magnet to match bunch length to main linac

## Slide 5: Pulsed Polarized Electron Source for AmPS. Built in 1995 by BINP in collaboration with NIKHEF (Amsterdam) and ISP, Novosibirsk.
AmPS energy range 440 – 720 MeV
Beam polarization 80 %
Cathode voltage (pulsed) -100 kV
Photocathode type Strained InGaAsP
Laser type Ti – Sapphire
Light wavelength 700 – 850 nm
Laser power in a pulse 200 W
Pulse duration 2.1 s
Repetition rate 1 Hz
Maximum current from a gun 150 mA
Operational current 15 – 20 mA
Photocathode recesiation time
(depends on laser power) 190 – 560 hours

## Slide 6
Polarized Electron Source
for AmPS stretcher ring
S – focusing solenoids
BM – bending magnets
EB – electrostatic deflectors
CM – beam current monitor
EM – beam profile monitor
C – RF buncher/acceleration
cavities
B.L.Militsyn et al.
“The pulsed polarized electron source
for nuclear physics experiments at AmPS”,
EPAC98,1415-1417, Stockholm 1998

## Slide 7
Pulsed 100 kV photocathode gun (AmPS)
2,3 – UHV pumping ports
4 – acceleration vacuum chamber
5 - anode
6,11 – gun insulators
7 - cathode
8 – high voltage cable
9 – polyethylene insulator
10 – guard vessel
12 – port of preparation chamber
13 – guard vessel pumping port

## Slide 8: 100 kV pulsed power supply (BINP for AmPS)
Dramatic increase of a cathode’s
lifetime: up to 560 hours! Before
in DC mode it was 4-5 hours, only.
Good enough pulse flat top uniformity
Reliable and safe in operation

## Slide 9: World’s best photocathodes (From PESP 2008: L.G.Gerchikov et al., SPTU & FTI, St.Petersburg, Russia)
Sample | Composition | Pmax | QE(max) | Team
SLSP16 | GaAs(3.2nm)/ GaAs0.68P0.34 (3.2nm) | 92% | 0.5% | Nagoya University, 2005
SL5-777 | GaAs(1.5nm)/ In0.2Al0.23Ga0.57As(3.6nm) | 91% | 0.14% | SPbSPU, 2005
SL7-307 | Al0.4Ga0.6As(2.1nm)/ In0.19Al0.2Ga0.57As(5.4nm) | 92% | 0.85% | SPbSPU, 2007
Eg = 1.536 eV, valence band splitting: Ehh1 - Elh1 = 87 meV,
Maximal polarization: Pmax= 92% at QE = 0.85%

## Slide 10
SL: Al0.19 In0.2 Ga0.61As(5.4nm)/Al0.4Ga0.6As(2.1nm)
(PESP 2008, L.G.Gerchikov et al., SPTU & FTI, St.Petersburg, Russia)
Pmax= 92%, QE = 0.85%
Notes: 10

## Slide 11
Ceramic
200 keV Polarized Electron Gun for ILC (Nagoya University, M.Yamamoto et al.)
Ultra high vacuum < 10-9Pa
High field gradient > MV/m
Photocathode preparation
with Load-Lock
(cleaning, NEA activation)
Photocathode puck
(f23mm)

## Slide 12
Mo Cathode
Ti Anode
Electrode Design & Fabrication (Nagoya U., M.Yamamoto et al.)
Mo cathode:
Material : pure Mo (>99.96%)
Size : f 162mm
Space Charge Limit: 30A
Maximum field gradient:
7.8 MV/m @electrode
Ti anode:
Material : pure Ti (JIS-grade 2)
Gap:22mm

## Slide 13
Gap 0.5mm results
Reducing field emission dark current
Electrode shape
F.Furuta et al., NIM-A 538 (2005) 33-44
Nagoya & KEK
Test sample

## Slide 14
ILC:5nC/bunch
Nano second bunch generation from superlattice
(M.Yamamoto et al., SPIN2006 @Kyoto)
Photocathode : GaAs-GaAsP strained SL
Bunch charge : 8nC
Laser spot size : f~20mm,
Bunch width(FWHM): 1.6ns
space-charge-limit was appeared clearly over 6nC/bunch under condition with -70kV.
Peak current density
~18 mA/mm2
No Charge Limit

## Slide 15: C-tau PES preliminary parameters
Beam polarization 90 %
Cathode voltage (pulsed mode) 100 kV
Photocathode type Super Lattice
Laser type Ti – Sapphire
Light wavelength 700 – 850 nm
Laser energy in a pulse 10 mkJ
Pulse duration 1 - 2 ns
Repetition rate 50 Hz
Number of electrons/pulse 2 · 1010
Photocathode quantum efficiency 1%
Photocathode re-cesiation time
(depends on laser power) 200 – 600 hours

## Slide 16: Spin orbit in presence of Siberian Snake
Snake
IP
Derbenev, Kondratenko, Skrinsky, 1977
Snake rotates spin
by 1800 around z-axis
In arcs spin lies
in the horizontal plane
At IP spin is directed
longitudinally (exactly!)
With partial snake at magic energy spin is directed also
longitudinally at IP and similarly at the snake’s location

## Slide 17: Polarization scheme with 3 snakes (arc=1200 + 2 damping wigglers in the arc’s middle points )
IP
snake1
snake2
snake3
damping
wiggler1
damping
wiggler2

## Slide 18: Transparent spin rotator (partial snake)
All quads don’t need to be skewed!
( Koop et al., SPIN2006)
(Litvinenko, Zholentz,1980)

## Slide 19: Depolarization time in presence of snakes Derbenev and Kondratenko, Zh. Eksp. Teor. Fiz. 64 1918, 1973; Sov. Phys. JETP 37 968, 1973
Placing damping wigglers
in minimum of |d| weakens
depolarizing effects of SR

## Slide 20: Longitudinal polarization estimates for HIEPA
Due to lower bending field compared to BINP’s c-tau project (B=1 T)
depolarization here is going much slower!
3 snakes instead of 5 - looks quite sufficient for r=15-20 m.

## Slide 21: Longitudinal Compton Polarimeter
Compton backscattering asymmetry is high at the edge of a spectrum! Could be utilized for the longitudinal polarization measurement. One shall detect scattered electrons instead of photons! Much better capability to select events with certain momentum transfer!
0.085

## Slide 22: Free precession of spin in the horizontal plane
Bunch is injected with polarization directed perpendicular to the bending field:

## Slide 23: Free spin precession in medium plane - 2
Spin ensemble de-coherence is rather small during 10000 turns !
The precise frequency analysis is straightforward!

## Slide 24: Fourier spectrum of free spin precession
Determination of the spin precession frequency with very high accuracy,
in the order of 10-6 is feasible! The first, second and the third order synchrotron
satellites are clealyr visible due to small initial energy offset of the injected beam.

## Slide 25: Concluding remarks
80% in average of longitudinal polarization at IP of HIEPA is feasible with 3 snakes for Ebeam=2.5 GeV - τp > 5000 s, if r > 16 m.
And even for Ebeam=3.0 GeV, the polarization reaches 50% in average (τp= 1300 s).
Compton backscattering polarimeter is a useful tool to control the longitudinal polarization. Scattering rate asymmetry relative to the sign of the circular polarization of the laser light may reach 10% or more!
It can be used also to measure the free precession spin frequency via seeing of turn by turn modulation of the laser light scattering rate, when beam is being injected with spins lying in horizontal plane. This is much faster technique to determine the energy than the famous resonant depolarization method! Then snakes, of course, should be switched off!
This fast and robust method of the spin precession frequency determination greatly facilitates making scans to study of proximal spin resonances - their contribution to spin precession frequency. That is of crucial importance for correct energy calibration!