## Slide 1
Weiwei Gao
Fujian University of technology
2020-8-6
STCF Lattice design

## Slide 2
1. STCF对lattice的要求及设计难点
2. 各模块lattice设计
3. 全环参数
Outline

## Slide 3
能够在优化能量点上获得10^35cm-2s-1 亮 度，要求低发射度，低beta；
实现Crab waist + Large Piwinski angle 对撞；
3. Local chromaticity correction；
4. 纵向极化束对撞，要求消色散长直线节，在对称的弯转角度上安装蛇装置；
5. MDI要求第一块散焦铁距离对撞点0.9m。
STCF lattice需求及设计难点

## Slide 4
Optics design
Interaction region
Arc section
Technical section-----injection、RF 、ring separation、snake、tune……
Final focus doublet
Final focus telescope
Vertical chromaticity correction section
Horizontal chromaticity correction section
Achromatic section
Crab sextupole section
Total telescope
8 long arc section（6 FODO cell）
2 short arc section（3 FODO cell）
Matching section

## Slide 5: Interaction section
ccy section:
ccx section:

## Slide 6: Interaction section
Local chromaticity correction
Crab waist

## Slide 7: Arc section
total ARC section composed of 8 super-periods
Each super-periods composed of 6 FODO cell
tune of each FODO cell is 0.25
(both planes), two FODO cell compose -I
Bending angle of each super-periods is 36°
2 pairs of horizontal sextupoles
2 pairs of vertical sextupoles
Phase advance of each pairs of
Is π

## Slide 8: Arc section
Used to connect interaction
region and long arc section
Composed of 3 FODO
adjust angle suitable for
Siberian Snake
Satisfy –I transformation
Right short arc
Match to interaction section
Match to long arc
section

## Slide 9: Technical section
45×2m
injection
RF cavity
ring separation
snake
tune

## Slide 10
Geometry
Circumference: 740.1753618 m，
Revolution frequency : 0.4050289481 MHz
8 dispersion free long straight section (10 m)
5 Siberian snakes, interval by 72°
snake
snake
snake
snake
snake
Interaction point

## Slide 11
Total ring

## Slide 12
Beam parameters of ring
Parameters | value
Circumference[m] | 740.1753618
Optimized energy[GeV] | 2.0
Horizontal beta @ IP[m] | 0.06
Vertical beta @ IP[m] | 0.0006
tunx/tuny | 30.64877157/33.83336655
Natual chromaticity | -93.61581055/ -482.0501874
Horizontal emittance[nmrad] | 2.977
Vertical emittance[nmrad] | 0.2977
Momentum compaction factor | 0.001214146667
Energy loss per turn[MeV] | 0.071734
Horizontal beam size @ IP[um] | 13.36
Vertical beam size @ IP[um] | 0.423
Horizontal damping times(x/y) | 0.13840184/0.13767343
Luminosity[cm-2 S-1] | 1.51×1035（@current=2A, ξy=0.1）

## Slide 13
Summary and outlook
根据STCF的要求设计了较完整的磁聚焦结构；
开发了一套lattice设计的方法；
进一步研究怎样的工作点可以获得更高的亮度；
进一步加入高频腔研究纵向动力学；
进一步MBA弧区设计；
进一步非线性动力学孔径的优化方面，采用与机器学习结合的方法进行优化。

## Slide 14
Thanks for your attention！