## Slide 1: GEM 读出电子学 ------ 一点个人理解
2015年 6月23日
中国科学技术大学 近代物理系
安 琪
核探测与核电子学国家重点实验室

## Slide 2
报告内容
 基本的读出方法
 系统平台框架
 ASIC芯片近期发展

## Slide 3
 基本的读出方法
 系统平台框架
 ASIC芯片近期发展

## Slide 4
 Pre_Amp + Shaper + 数字化
 延迟线 + Disc. + TDC
 波形数字化
 编码读出
基本的读出方法

## Slide 5
 传统技术路线:
Pre_Amp + Shaper + 数字化
 PreAmp
 Fast/Slow Shaper
 Comparator
 Peak Detect & Hold
 Digital FIFO/Buffer
 Analog FIFO/Buffer
 ADC/TDC
PreAmp
Slow
Shaper
Comparator
Peak Detect & Hold
Fast
Shaper
Analog FIFO/Buffer
Digital FIFO/Buffer
TDC
ADC
ASIC
ASIC
 技术路线的发展
PreAmp
Slow
Shaper
Fast
Shaper
N:1
NUX
TDC
 PreAmp
 Fast/Slow Shaper
 Comparators/FIFO
 Switched Capacitor Arrays
 N:1 MUX
 Output Buffer
 ADC/TDC
SCAs
N:1
NUX
ADC
Comparators
/FIFO
CSA为主

## Slide 6
Pre_Amp + Shaper + 数字化
ASIC
 技术路线的发展
PreAmp
Slow
Shaper
Fast
Shaper
N:1
NUX
TDC
 PreAmp
 Fast/Slow Shaper
 Comparators/FIFO
 Switched Capacitor Arrays
 N:1 MUX
 Output Buffer
 ADC/TDC
SCs Arrays
N:1
NUX
ADC
Comparators/FIFO`
SoC

## Slide 7
典型ASIC芯片: HELIX128-2
 128Ch. +1 (Test)
 129 CSA
 130 Shaper
 128 Comparators
 128 Pipeline SCA
Cell for each Ch.
 4 x 34 MUX.
 2 Current Buffer
 Rupertus Carola Univ. Germany
 Ulrich Trunk，博士论文， 2000
 Silicon Strip Detector，Microstrip Gaseous Chambers
 Originally developed for the HERA-B experiment
 2-D readout of a triple GEM detector （LHCb）

## Slide 8
典型ASIC芯片: APV25
 128Ch.
 0.25 m CMOS
 Low Noise CSA
 50ns CR-RC Shaper
 192 Pipeline(SCA)
 Pulse Shape Processor
Peak mode
Deconvolution mode
 128:1 MUX
 S/H
 Diff. Current Driver
 Rutherford Appleton Lab,
Instrumentation Dept, Oxfordshire , UK
 NIMA 466 (2001) 359–365
 Developed for silicon microstrip detectors
in the CMS tracker

## Slide 9
读出方法：延迟线读出
 大大减少了读出电子学通道数
 空间分辨高（100m）
 死时间大
 延迟线：分离元件或集成芯片
Delay Line
Amp
Amp
CFD
CFD
TDC

## Slide 10
读出方法：延迟线读出

## Slide 11
读出方法：波形数字化
高速采样直接获取GEM输出脉冲的波形
 优点：
 很方便同时获取时间与能量信息；
 消除了传统电荷积分放大带来的“堆积”
效应，死时间小，适应于高亮度、高事例
率的物理实验；
 此外，波形数字化还可以使物理学家采用
任何可能的数字处理方法来处理波形数字
化的信号数据。
 缺点：
 代价高：功耗、集成度、数据传输、成本，…….
Amp
Amp
ADC
ADC
GEM
Detectors
Data Processing

## Slide 12
读出方法：编码读出
 优点：减少读出电子学通道数
 两种实现方法：
  感应编码读出
  胡荣江等，原子核物理评论, V28, No.4 (2011) p459
  直接编码读出
  S. Procureur et al, Nucl. Instr. and Meth. A729 (2013) 888

## Slide 13
感应编码读出原理
增加感应读出条
电荷按比例分除到下面的相邻感应条上
对感应信号进行特定地编码合并，缩减信号路数
放大成形后，直接用ADC记录
幅度大小关系 | 位置
A>B | 1
B>C | 2
C>A | 3
A>C | 4
C>B | 5
B>A | 6
阳极条
感应条
通过鉴别两路信号的大小关系，用3路读出电子学能确定 Pn2 = 6 路位置，其位置解码如右表所示；
一般地，利用n路读出电子学，就可以唯一地确定Pn2 路位置。
任何相邻两个通道的排列方式最多出现一次，不能重复。
一维感应编码原理图
一维感应编码解码表
13

## Slide 14
直接编码读出原理
通常情况下，一个事例信号会被至少两个相邻条读取到；因此采用如右的组合方式编码,放大成形后，直接用ADC记录，根据读出各通道信号，则可以唯一地确定信号击中的相邻条位置。
若A,E通道有信号，则可以确定击中位置在5，6条
阳极读出条
如图，5路读出可编码11个读出条的位置；
n通道读出电子学，对应有Cn2 种无序组合，则可编码确定Cn2 +1个读出条的位置。
电荷重心法依然有效，可得到较小的分辨率
同理，此方法可扩展到二维。
一维直接编码原理图
一维直接编码读出解码表
A1 | B2 | C3 | D4 | E5 | A6 | C7 | E8 | B9 | D10 | A11

## Slide 15
 基本的读出方法
 系统平台框架
 ASIC芯片近期发展

## Slide 16
模块化、标准化的框架平台
 NIM；  VME；  cPCI/PXI；
 PCIe；  ATCA；

## Slide 17
SRS：Scalable Readout System
 SRS理念
 构建一个面向不同规模、不同类型、不同技术的MPGD探测器的通用多通道读出电子学的平台框架。
 CERN RD51 Collaboration
 2008年成立；
 全球大约80多个研究所、大学参加；
 成立了一个专门的读出电子学工作组:WG5，目标是建立“Portable
Multichannel Readout system for Multi Pattern Gas Detectors；
 2009年提出了SRS平台框架的理念和计划。

## Slide 18
SRS 单元（Cell）的基本概念
 三个基本组成部分
 Front-End（FE）
Front-End Hybrids: Front-End ASICs with all supporting Circuits，紧靠探测器
Chip Link (HDMI, Optical)
 Front-End Card（FEC）
Adapter Board
FPGA-based Card: Programmable logic，Memory，H-Speed Communication.
 Scalable Readout Unit（SRU）
Standard 6U
DTCC: Data, Trigger, Clock & Control

## Slide 19: SRS单元的进一步说明
Chip Carriers
Single
Master
Slave
On-detector front-end hybrids
APV25
VFAT
BEETLE
…
Front-end adapter
(FE-specific)
ADC card
digital FE card (VFAT)
GBT receiver
…
Front-end FPGA card (SRS standard)
modular firmware:
SRS control
application specific
GbE
to DAQ (small/ medium size system)
to SRU
(large-size system)
Chip-links
HDMI
- analog (APV/Beetle)
- digital (VFAT/Beetle)
optical (GBT. …)
…
DTCC
Max 40 FEC/ SRU
Max 16 chip carriers/FEC
Notes: DTC:Data-Trigger-Clock

## Slide 20
SRS星型结构
Star Topology
SRS employs a star topology with point-to-point connections between all components of the system, which enables the user to increase the number of DAQ cells when moving to a larger area detector.

## Slide 21
SRS_ATCA
 ATCA: Advanced Telecommunications Computing Architecture

## Slide 22
一个最简单的SRS例子：Timepix

## Slide 23
A Muon Tomography Station Using GEM Detectors
APV25
Chips

## Slide 24
 基本的读出方法
 系统平台框架
 ASIC芯片近期发展

## Slide 25
 VMM
 GEMROC
 N-XYTER
 VFAT
ASIC芯片近期发展
ASIC举例

## Slide 26
VMM：An ASIC for ATLAS Muon Spectrometer Upgrade
New Small Wheels
sTGC
Small Strip Thin Gap Chamber
MM
MicroMegas
(MICROMEsh GAseous Structure)
Front-end Electronics (ASIC)
more than 2.3 million channels total
operate in both polarities of charge
sensing element capacitance 10-200 pF
charge meas. up to 2 pC @ < 1 fC rms
time meas. ~ 100 ns @ < 1 ns rms
trigger primitives, neighbor meas.
low power (< 10mW/ch.), programmable
 可以用于各类 Micro-Pattern Gaseous
Detectors，包括：GEM。

## Slide 27
VMM Family ASICs
VMM1 (2012)
50 mm²
500k MOSFETs
(8k/ch.)
mixed-signal
2-phase readout
64-ch. ：Charge & Time Measurement
VMM2 (2014)
115 mm²
> 5M MOSFETs (>80k/ch.)
Deep re-design of VMM1
Higher functionality and
complexity
Continuous fully-digital readout
VMM3 (2015-16)
130 mm²
> 6M MOSFETs
includes L1 handling and SEU-tolerant logic
L1H

## Slide 28
VMM1

## Slide 29
VMM1 特征

## Slide 30
VMM2 Architecture
technology: IBM CMOS 130nm ；  size: 13.5 mm x 8.4 mm
power dissipation: 7-10 mV/ch.；  transistor count/ch.: > 80,000

## Slide 31
VMM2 特征: Analog Front-End

## Slide 32
VMM2 特征: Signal Processing
o amplitude discriminator capable of processing sub‐hysteresis signals；
o discrimination threshold adjustable with 10bit global DAC, ~1mV steps, & 4bit channel DAC,
~1mV steps；
o option of disabling discrimination once the first peak is detected；
o force‐neighbor signal processing for above threshold events: when an event exceeds the
threshold, the neighbor channels (in neighbor chips if desired) are forced to peak/time detection;
enabled with global register bit sng; first and last channels communicate with associated channels
in neighbor chips through bi‐directional pins sett, setb
o peak detector with peak‐found signal for accurate timing (multi‐phase: track, peakdetect,
hold&buffer)
o 10bit peak amplitude conversion available for each channel，providing offset adjust. in LSB units.
o time detector at peak‐found with time‐to‐amplitude conversion implementing voltage ramp
with adjustable duration: 0.125, 0.25, 0.5, 1 μs, ramp starts at peak‐found from peak detector
and stops either at falling edge of ena input or at next BC clock；
o 8bit timing conversion available for each channel and providing offset adjustment in LSB units.
o address in real time (ART) available at output art either at threshold crossing or at peak found
with flag indicator followed by serialized address；
o time‐over‐threshold, threshold‐to‐peak, peak‐to‐threshold, pulse‐at‐peak available for
each channel at dedicated outputs ttp；
o 6bit peak amplitude conversion available for each channel at dedicated outputs ttp

## Slide 33
Current Status
VMM2 dies received from foundry in May 2014
Packaged samples received on Sept. 18th (considerable delay in packaging process) and are being assembled on AZ PCB
Dies wire-bonded on Sept. 15th made possible preliminary tests

## Slide 34: ATLAS Phase 1 Muon谱仪端盖NSW 触发系统研究
 山东大学物理学院负责探测器
 核探测与核电子学国家重点实验室（USTC）负责电子学
 2015年国家自然科学基金重大国际合作项目
 前端读出电子学采用VMM

## Slide 35
抗辐照ASD/TDS
IBM 130nm
>15kHz/cm2
Pad L0 trigger
预触发
高速数据传输 >5Gbps/fiber
sTGC触发系统前端电子学
ASD：VMM2
TDS： Michigan
USTC
Notes: FE功能：1）前端读出+ASD；2）+PAD预触发；3）所有数据的集成送出
通道数：(#128-#512/FE-detector) * 2*912FE (strip+padwire) == 330k
LUT与BigWheel结合，形成L1MUON触发判断

## Slide 36
FEB系统
+ 512通道
+ 采样率40MHz Bx
+ Pad Trigger L0触发
+ 4.8Gbps Strip触发信息
+ 尺寸25×5cm
高度集成：
512 channels
8 VMM + 4 TDS
1 SCA + 2 ELink
512通道/25cm
VMM
VMM
VMM
VMM
VMM
VMM
VMM
VMM
TDS
TDS
TDS
TDS
sTGC触发系统前端电子学：FEB

## Slide 37
GEMROC: GEM Readout Chip
 32Ch.
 Transimpedance Preamp, Fast/Slow Shaper
 Comparator & TWC（Time-Walk Compensation）
 Peak Detect & Hold
 Time Stamp Generator
 两类FIFOs：电荷/时间信息缓存
 差分输出形式（analog，digital）
 0.35m CMOS
 2-D GEM（30cm x 30cm）读出, 事例率：106 /s
 2011 IEEE Nuclear Science Symposium Conference，AGH Univ. of Sci. & Tech.，Krakow
Time-Walk Compensation

## Slide 38
TWC: Time-Walk Compensation
 diffa， diffb：比较器输入
 comp_outa，comp_outb：比较器输出
 TWC_out， TWC输出
Vth
 Time Walk
 diffa输入信号幅度小，充电电流ICA就大，
加快CA充电，TWC_out前沿变快；
 反之亦然；
 IEEE JOURNAL OF SOLID-STATE CIRCUITS, VOL. 30, NO. 12, DECEMBER 1995，
A CMOS Multichannel IC for Pulse Timing Measurements with 1 -mV Sensitivity

## Slide 39
N-XYTER: Neutron-X-Y-Time-Energy
Read-out Chip
 0.35m CMOS
 Originally developed for the high rate imaging neutron detection, NIMA 568(2006) 301–308
 “2-dimensional GEM detector with FEE based on the nXYTER ASIC”, Jinst 9 C08026, 2014
 “Self triggered readout of GEM in CBM” （CBM-MUCH）, 14th RD51 Collaboration
Meeting, 2014
 128Ch.
 CSA Preamp,
 Fast/Slow Shaper （达峰时间：30ns/175ns）
 Comparato & TWC（Time-Walk Compensation）
 Peak Detector & Holder
 Signal rate  900K/ch
 ENC: 1000e@30pF

## Slide 40
N-XYTER
TWC

## Slide 41
nXYTER 的发展
 128Ch.
 CSA
 Fast/Slow Shaper
 Comparator/TWC
 Peak Detector & Holder
 SCA Array for Charge Inf.
 Time Stamp Generator
 FIFO for Time Inf.
 MUX for Output
 Token Manager
 增加部分
 原有部分

## Slide 42
STS-XYTER：nXYTER 的进一步发展
 CBM的STS组以N-XYTER为基础进行设计
、、
 片内集成Flash ADC
 第一版STS-XYTER已完成测试
第二版正在设计，并改为：MUCH-XYTER

## Slide 43: VFAT2
 “Trigger & tracking” Front-End ASIC
 128Ch.
 0.25m CMOS
 Designed for TOTEM of LHC
 Integrate A & D together
Originally developing for three detectors of TOTEM:
Silicon strips, Gas Electron Multipliers (GEM), Cathode Strip Chambers (CSC).
Two main functions:
 Trigger
Providing programmable “fast OR” information based on the region of the
sensor hit & it’s used for the creation of a trigger.
 Tracking
Providing precise spatial hit information for a given triggered event.

## Slide 44
VFAT2
 Transimpedance pre_Amp & Shaper.
 Calibration Unit
 Signal Discrimination with a Programmable
threshold (programmable dc level )
 Synchronization and monostable
 Fast OR  Hit Signal
128 ch. are grouped in sectors & assigned to 8 LVDS outputs
 SRAM1: circular memory, 128  256 (6.4s)
Trigger Latencies: 1- 256 clock periods
 SRAM2: Used for Triggered Event Data
only receiving the L1 (LV1A ) signal

## Slide 45: VFAT3
Developed for the CMS triple-GEM system. The features of the new ASIC are listed below:
 Operation at high particle rate using large GEM detectors;
 Provide trigger data at 40MHz as well as precise tracking data upon Level-1 Accept signal;
 Large detector capacitance 20–60 pF;
 Relatively long signal charge collection 80 ns;
 Programmable shaping time: 25, 50, 100, 250, 500 ns;
 Interface required: slvds elinks to GBT at 320 Mbps;
 Level-1 trigger latency up to 20 ms;
 Integrated calibration, bias and monitoring functions.
Using CFD to correct time walk

## Slide 46
Thanks！

## Slide 47
国内的进展