## Slide 1: 清华大学MRPC研究进展
Outline:
  Introduction of timing RPC (MRPC)
Application in physics experiments
MRPC intrinsic resolution
Application in industry and medical
Conclusions
王义
清华大学工程物理系
yiwang@mail.tsinghua.edu.cn

## Slide 2
Introduction of MRPC(多气隙电阻板室）
Application in nuclear physics experiments
Application in industry（Muon tomography)
Application in medicine（TOF-PET）
2
Standard parameters:
Resistivity of glass: ~1012 Ω.cm
Time resolution <100ps
Efficiency >95%
Dark current: a few nA
Noise <1Hz/cm2
MRPC is made of thin
glass, large area and cheap
The inner glasses are
floating, take and keep
correct voltage by
electrostatics. it is
transparent to fast signals
Thin gap->good timing
Multi-gap-> high efficiency
Read out
Read out
Insulator
Carbon
Insulator
Resistive plate

## Slide 3
SPARK Counter, 时间分辨~1ns
MRPC/RPC 的发展历史
Pestov Counter, 时间分辨可达30ps
0.1 mm
1 mm
1.5 mm
第1个RPC，1981, 效率达97％，时间分辨可达1ns
0.3 mm
第1个MRPC，效率达97％，时间分辨<100ps
1971
1978
1981
1996

## Slide 4
V=-Vo
'not so free'-charges
感应电荷的局部性
streamer takes energy only
from a local region
Q=2C*Vo, C*<<C
V=Vo
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
V=6Vo-ΔV1
V=4Vo-ΔV2
V=2Vo-ΔV3
V=ΔV4
V=6Vo
V=0
-
-
-
-
+
+
+
+
+
+
MRPC/RPC 的主要性能
内部场强的自我调节功能

## Slide 5
MRPC的工作气体
The standard gas mixture is:
C2H2F4 (90%) i-C4H10 (5%) SF6 (5%)
-C2H2F4 (tetrafluorethane): very electronegative, it is the main ionizing gas (easily 90% of the mixture).
-i-C4H10 (iso-butane): it quenches UV photons (0-10% in the mixture).
-SF6 (sulfur hexafluoride): the best practical electron scavenger in nature。 SF6吸附电子变成负离子，很容易与正离子结合，活动性变差。
SF6是很好的绝缘气体，有助于提高MRPC工作电压，提高时间分辨

## Slide 6
元素电负性递变规律
加入SF6气体的好处

## Slide 7
Applications in nuclear physics experiments
Industrial applications
Medicine application-TOF-PET
2
QCD临界点
RHIC, FAIR
3
3
QCD相变边界
FAIR, CSR
1
1
高温QCD
LHC, RHIC
2
Quarkyonic matter?
重子化学势μB (MeV)
温度 T (MeV)
部分子物质
(QGP)
早期宇宙
发展演化
强子物质
高能核核碰撞中的QCD相结构示意图

## Slide 8
RHIC
BRAHMS
PHOBOS
PHENIX
STAR
AGS
TANDEMS
1 km
通过核物质状态的相变来了解和说明夸克禁闭的本质和强子质量的起源。
2. 核子的内部结构—自旋物理。
3. 研究极高的胶子密度时强相互作用的性质和寻找奇异粒子。如双粒子，H粒子（6夸克）等。
RHIC 的主要物理目标

## Slide 9
应用TOF做粒子鉴别
TOF与TPC测得的粒子动量P相结合，
要求Start 和Stop探测器时间抖动小，即响应快，时间分辨好

## Slide 10
10
粒子鉴别能力与分辨时间的关系
对于相同动量，质量分别为mA, mB 的两种粒子，固定距离的飞行时间差为：
粒子分辨本领为：

## Slide 11
可选择的TOF探测器
闪烁探测器
响应速度快，信号上升时间只有几ns
时间分辨好<100ps
缺点是价格昂贵
多气隙电阻板室(MRPC)
响应快，时间分辨好
结构简单，价格便宜

## Slide 12
MRPC used in STAR barrel TOF
Long side view

## Slide 13
Glass: ～4×1012.cm
Carbon tape: 500k /
Gas gap: 6×0.22mm
Working gas: 95% F134a+5% iso-butane
Time resolution: 70ps
Efficiency >90%
Rates capability: <500Hz/cm2 !
3cm
6cm
Readout pad
Performance of STAR-TOF MRPC

## Slide 14
PID of STAR-TOF
Only TPC:
/k ~0.7 GeV/c,
(,k)/p ~1.1 GeV/c
TOF
e
π
K
p
Only TOF:
 /k ~1.6 GeV/c,
(,k)/p ~ 3.0 GeV/c
TPC

## Slide 15
15
MRPC 批量生产
通过产学研合作，建立了探测器批量生产基地，培养了批量生产及测试人员

## Slide 16
TOF－Trays在BNL调试，安装

## Slide 17
重大物理成果
TPC与TOF结合，加上先进的高级触发，在10亿次金核金核对撞实验中，成功捕获到18个反氦核。产生概率接近亿分之一！
“Observation of the Antimatter Helium-4 Nucleus”
by STAR Collaboration
Nature, 473, 353(2011).
April, 2011

## Slide 19
A large area of muon telescope detector (MTD) at mid-rapidity, allows for the detection of
di-muon pairs from QGP thermal radiation, quarkonia, light vector mesons, possible correlations of quarks and gluons
as resonances in QGP, and Drell-Yan production
single muons from the semi- leptonic decays of heavy flavor
hadrons
advantages over electrons: no  conversion, much less Dalitz decay contribution, less affected by radiative losses in the detector
materials, trigger capability in Au+Au
trigger capability for low to high pT J/ in central Au+Au collsions
excellent mass resolution, separate different upsilon states
e-muon correlation to distinguish heavy flavor production from initial lepton pair production
STAR Muon Telescope Detector

## Slide 20
Concept of Design of the STAR-MTD
A detector with long-MRPCs covers the
whole iron bars and leave the gaps in-
between uncovered. Acceptance: 45% at
||<0.5
117 modules, 1404 readout strips, 2808 readoutchannels
Long-MRPC detector technology, HPTDC
electronics (same as STAR-TOF)






















## Slide 21
Structure of LMRPC module
Time resolution ~ 70ps, efficiency> 95%
Strip readout :

## Slide 22
STAR-MTD已建成
整个MTD系统由122个LMRPC组成，2928个读出道。已安装到STAR上。相应的在线刻度软件及事例重建软件也已就绪，将在2014年度的运行中发挥重要作用。

## Slide 23
STAR-MTD的性能刻度
σ: 84.5ps
Xinjie Huang, Tsinghua
The time difference between TOF+MTD measured time and TPC measured time is
deltaT = (tTOF2 – tTPC + tTOF1)/2 – tMTD – tSteel

## Slide 24
UNILAC
SIS18
p-Linac
HESR
CR & RESR
NESR
100 m
初级束流
1012/s; 1.5 GeV/u; 238U28+
1010/s 238U73+ up to 35 GeV/u
3x1013/s 30 GeV protons
次级束流
冷却储存环
radioactive beams
1011 antiprotons 1.5 - 15 GeV/c,
stored and cooled
range of radioactive beams up to 1.5 - 2 GeV/u; up to factor 10 000 higher in intensity than presently
antiprotons 3 - 30 GeV
Facility for Antiproton and Ion Research: FAIR
APPA
(1)最新高科技加速器群
(2)强子物理；天体物理；
放射性束流物理；
高重子密度物理(CBM)
FAIR计划2018年出束流，耗资～€15亿

## Slide 25
CBM-TOF是研究各种物理的必备探测器，中心粒子计数率达到25kHz/cm2
CBM将采用中国组研制的高计数率和高时间精度飞行时间探测器（TOF）
飞行时间探测器
硅探测器
零度角量能器
电磁量能器
径迹探测器
超导二极磁铁
The Compressed Baryonic Matter Experiment: CBM

## Slide 26
26
A
B
C
D
CBM Experiment
CBM MRPC TOF
CBM科学问题:
高重子密度下QCD相结构
相边界
临界点
夸克素物质
CBM关键技术问题:
高计数率高精度探测器
计数率: R ≥ 25 kHz/cm2
分辨率:sT ≤ 50 ps
面积: A ~ 120m2
CBM 物理和飞行时间探测器 (TOF)

## Slide 27
How to increase rate of MRPC
27
Voltage drop changes with rate:
Two main ways to improve rate capability:
Reducing bulky resistivity of electrode glass (CBM)
Reducing the avalanche charge (ATLAS)
Other methods:
Reducing the thickness of glass
Warming the detector

## Slide 28
World map of MRPC’s rate capability

## Slide 29
Development of low resistivity glass
32cm x 30cm
29

## Slide 30
Performance test of glass
This glass was applied with 1000V for about 32days, integrated charge: 1 C/cm2
--roughly corresponding to the CBM life-time over 5 years operation at the maximum particle rate.
Resistivity decreases with temperature
Resistivity is very stable in DC measurement

## Slide 31
Rate scanning
Even though the rate is 70kHz/cm2, the efficiency is still higher than 90% and the time resolution is about 80ps.
31

## Slide 32
MRPC计数率世界分布图
Rate: 60-70kHz/cm2
Time resolution: 40 ps
Cosy 2011
HZDR 2011/2012
GSI Apr/Aug 2009
Test results in other Labs
32

## Slide 33
已被FAIR-CBM采用建造高计数率，高时间精度的时间飞行谱仪
Technical Design Report of CBM-TOF

## Slide 34
CBM－TOF墙结构
超级模块结构
CBM-TOF墙结构
TOF墙面积: 120平米
MRPC数目： 1376个
电子学道数：~10万
造价：~8百万欧元

## Slide 35
Glass: low resistive glass
0.7mm thick, 27cm x 25cm
Strip: 27cm x 0.7cm, 0.3cm interval, 24 strips
Gas gap: 8 x 0.25mm
Gas box: 600mm x 500mm x 72mm
Design of Real-size strip-MRPC
Differential strip: 7mm wide+3mm interval
h
w
t
ground
Feed trough: Micro-strip, 50Ω

## Slide 36
36
Beam test @GSI, Oct.2014
1.1 GeV/u 152Sm beam
On 0.3mm/4mm/xmm Pb target
Rate limit <5kHz/cm2
Tsinghua strip counter
Reference counter:
HDMRPC-P5
Diamond
Beam
Setup

## Slide 37
Counter type under test | HD-P2 | TSU-strip
HV （kV） | 11 | 5.5
Efficiency D4 | 0.975 | 0.967
Gaussian resolution s (ps) | 63 | 65
RMS (ps) | 123 | 137
Fraction of Hits outside 3 s (%) | 8 | 9
Average cluster size | 2.37 | 1.6
Mean Hit Multiplicity | 2.6 | 2.1
Performance of two strip MRPC (Heidelberg and Tsingha)
Performance of two MRPC

## Slide 38
10气隙MRPC本征时间分辨
HPTDC的时间抖动 30ps
NINOs ASIC+Interface card 24ps
测试得到MRPC时间分辨 40ps
则MRPC的本征时间分辨为，

## Slide 39
24 x140m气隙MRPC时间分辨
更快前沿波形采样TDC 30-> 5ps
更快FEE 24-> 5ps
MRPC本征时间分辨 11-> 8ps
则测得MRPC时间分辨为，

## Slide 40
TOF PID at the EIC
TOF Positives
Compact (10-15 cm of space needed), allowing more room for, e.g., RICH
More clean PID
Can contribute to e/h identification using TPC dE/dx
TOF Negatives
Start counter?
40
@ 1m distance | Distance | Pion-Kaon Separation | Kaon-Proton Separation
σtot=100 ps | 1m |  | 
σtot=10 ps | 1m |  | 
σtot=10 ps | 3m |  | 
Momentum reach of TOF PID reaches interesting levels if one can achieve ~ 10 ps

## Slide 41
 | MRPC ( C. Williams et al. ) | MRPC ( UIUC & BNL)
Gas Gap Width | 160um (fishing line) | 105um (fishing line, and 165, 125, 75um)
# of Gas Gaps | 4 stack x 6 layers = 24 | 4 stack x 9 layers = 36
# of thin glass layers | 4 stacks x 5 layers = 20 (250um thick glass) | 4 stack x 8 layers = 32 (210um thick glass)
Preamplifier | Differential type, NINO chip | LMH6881 2.8-GHz + Evaluation Board
TDC and DAQ | Oscilloscope (10Gs) | DRS4-V5(5Gs) + PC
Time resolution | 20 ps published (16 ps private comm) | 18ps
Configuration of eRD10 Prototype mRPC
Gas gap width : 160um
(16ps timing resolution)
Gas gap width : 105um
Crispin Williams
BNL&UIUC Prototype
4 x
4 x
PCB
glass
Gas gap
41

## Slide 42
Time Resolution Measurement at UIUC
MRPC-A
MRPC-B
DRS4-V5
(Wave form digitizer)
PC
(DAQ)
DC0,1,2
SC1
SC4
preamp
preamp
Gas Cylinder
USB
50 Ohm cable (<1m)
ch2
ch2
Muon trigger
Gas Mixture : “Freon” (R134a) 90% : Iso 5% : SF6 5%
42
SC2
SC3
DC3,4
Pb Block

## Slide 43
Difference between time of top and bottom mRPC, Δt = t2 – t1= 25 ps
  σt = Δt/√2 = 18 ps
  Used a “Leading Edge Discriminator technique” in software from waveform, slew corrected
  Difference in pathlength taken into account
  Wings possibly due to noise, cross-talk, streamers, or something else?
We believe best published result is 20 ps
  Nucl.Instrum.Meth. A594 (2008) 39-43
  Nucl.Instrum.Meth. A629 (2011) 106-110
时间分辨

## Slide 44
15G 波形采样TDC

## Slide 45
在无损检测中的应用-宇宙线µ子成像
宇宙线主要粒子
在不同海拔高度的通量
宇宙线µ子天然存在
  能量极高，穿透力强
  自然存在，处处遍布
µ子与物质相互作用
能量损失
完全吸收
多次库仑散射

## Slide 46
Muon Tomography
Active area
concrete
Fe
Pb
U
diffuse density (mrad*mrad/cm)

## Slide 47
国外研究进展
K. N. BOROZDIN, et al., “Radiographic Imaging
with Cosmic Ray Muons,” Nature, 422, 277 (2003).
洛斯·阿拉莫斯国家实验室(LANL)
  29分钟-2.5cm宽铅”LANL”
Nicolas Hengartner et al., Information Extraction for Muon Radiography, 2005 IEEE NSS Conference Record, N1-5 (2005)

## Slide 48
国际动态 @ 2012~2013
 | 组织 | 探测器
美 | 洛斯·阿拉莫斯/LANL | 漂移管
 | 佛罗里达理工/FIT | GEM
俄 | 高能物理研究所/IHEP | 漂移室
意 | 国家核物理研究院/INFN | 漂移室 & 塑料闪烁体+波长位移光纤
加 | 原子能有限公司/AECL (CRIPT) | 漂移室 & 闪烁体+波长位移光纤
英 | 原子武器机构/AWE | RPC & 漂移室
LANL
FIT
INFN
AECL

## Slide 49
49
MRPC detector
The “TUMUTY” (Tsinghua University Muon Tomography)
height: 3m
6 groups of MRPC detectors
each group includes 2 MRPC, can realize the x-y 2D readout.
detector area: 736mm×736mm
framework figure
Muon Tomography @Tsinghua

## Slide 50
Advantage of MRPC
Good spatial resolution: 120μm
Excellent time precision: 75ps
Can get the momentum of muons

## Slide 51
缪子断层成像结果

## Slide 52
52
e-
e+
The converter-plate principle
Use the electrode plates as a g converter, taking advantage of the natural layered construction of the RPCs.
Time resolution for 511 keV photons: (our routine lab-test tool)
90 ps s for 1 photon
300 ps FWHM for the photon pair
e
-
e
-
e
-
..........
S
tacked
RPCs
A previous work on PET with gaseous detectors (21 lead plates + 20 MWPCs = 7% efficiency)
“The Rutherford Appleton Laboratory´s Mark I Multiwire Proportional Counter Positron Camera” J.E. Bateman et al. NIM 225 (1984) 209-231
Glass
Gas
在医学上的应用 RPC-PET

## Slide 53
53
在医学上的应用RPC-PET
Full body PET Scanner
  Full body image obtained in a single bed position, hence, a single acquisition
    Saves time (money)
    Reduced injected activity (patient dose)
    Continuous uptake signal (image quality improved without loss of biological significance)
    Inexistence of adequate image reconstruction algorithms, yet

## Slide 54
54
54
RPC-PET is a Falloff of HEP into Nuclear Medicine (Blanco et al. NIMA 2003)
Advantages
  Inexpensive
  Suitable for large area detectors, covering a large solid angle
    Increased system sensitivity (Couceiro et al. NIMA 2007, Crespo et al. MIC 2009)
  Increased position accuracy, allowing full 3D detection, minimizing gross parallax errors;
  Excellent timing resolution of 60 ps FWHM for 511 keV photon pair, allowing TOF-PET (~1.8cm)
Disadvantages
  Much smaller detection efficiency: 20% to 50%.
  No energy resolution, although energy sensitivity.
Introduction to RPC-PET

## Slide 55
55
-HV
+HV
闪烁体
超薄玻璃
光电阴极
石墨电极
绝缘层
信号读出
工作气体
新型气体倍增探测器
优点：
效率：>90%
时间分辨：60ps
定位精度：~1.8cm
高空间分辨
价格便宜
关键技术难点：
新型光电阴极研究，
倍增型探测器研制，
工作气体研究，
高灵敏ASIC电子学研制.

## Slide 56
Conclusions
MRPC以其优越的时间性能和低廉的造价，在高能核物理实验领域已经得到了广泛应用。
随着加速器亮度的提高，提高探测器计数率和时间分辨成为研究热点。
MRPC/RPC在工业领域及医学研究领域的应用又成为下一个研究热点！

## Slide 57
Thanks for your attention!