## Slide 1
STCF PID detector design and R&D progress
Qian LIU
On be half of STCF PID group
University of Chinese Academy of Sciences
2020 Joint Workshop on Future charm-tau Factory
2020.11.17

## Slide 2
2
PID requirements @ STCF

## Slide 3: Barrel Conceptual design
Polar coverage: 35° < θ < 145°
Radial position: 0.85 < r < 1.05 m
Module size: 2.4 m*0.45 m
Segmentation in φ: 24-fold
Segmentation in r: 1
Detector thickness radially: ~17%
Radiator: C6F14 in Quartz box / Quartz
Typical pad: 5X5 mm2
Number of readout channel: 1.03 * 106
Detector gas: Argon based mixture
Gas volume: 2.6 m3
3

## Slide 4
4
RICH Radiator

## Slide 5
5

## Slide 6
μ PID
π/μ
π/Κ
Κ/p
The K/p ability can reach to 5.7 GeV/c with 3σ separation.
π/Κ goes up to 3.5 GeV/c. Fulfill the requirements of STCF.
The low momentum π/μ separation is also possible.
p PID
Proton efficiency
Kaon efficiency
Pi efficiency
Misidentified to muon
高动量的pi/mu无法有效鉴别
6
PID Capability from fast simulation

## Slide 7
Reconstruction: Maximum Likelihood
Scan from 0.8 to 2.5 GeV/c, shows a consistent result with the fast simulation.
The large incident angle (>45°) needs to be considered carefully.
pion
kaon
proton
7
PID Capability from G4 simulation

## Slide 8
 | RBB e± |  |  | RBB γ | Two photon e± | Touschek | Coulomb Scattering | Brems
 | [20°, 90°] | [1°, 20°] | [0.256°, 1°] |  |  |  |  | 
Cross section | 399.2 nb | 0.195 mb | 2.796 mb | 2.99 mb, n=0.3573 | 5.15 mb | 32 times than BES III | 4 times than BES III | 4 times than BES III
Luminosity | 1035 /cm2/s |  |  |  |  |  |  | 
Particle rate | 7.98×104 Hz | 3.90×107 Hz | 5.6×108 Hz | 2×107 Hz | 2×107 Hz | 1.07×108 Hz | 1.03×109 Hz | 1.6×108 Hz
RICH rate | 9.37×106 Hz | 4.68×107 Hz | 8.16×106 Hz | 1×106 Hz | 5.04×108 Hz | 1.10×108 Hz | 5.45×106 Hz | 9.97×106 Hz
In total the counting rate on RICH：～7.×108 Hz (~4.5 kHz/cm2)
The second particles, Cherenkov photon and quantum efficiency have been considered.
The counting rate for micro-pattern detector is ~MHz/cm2.
Preliminary
8
Beam related background simulation

## Slide 9
Effective area: 160 X 160 mm2
Quartz/MgF2 as radiator (10mm), will be replaced by C6F14
THGEM + CsI (700nm, <9% uniformity inside the effective area)
Anode pad (5x5mm2) and readout by 1024 AGET FEE.
9
RICH Prototype development

## Slide 10
10
Beam Test setup @ DESY

## Slide 11
Tracker Gas: Ar(93%)+CO2(7%), VMM=550 V
RICH Gas: Ar(93%)+CO2(7%), Ar/CF4=50:50.
(H2O & O2 are monitored, ~90ppm, will be approved)
Radiator: MgF2 / Quartz.
Rotate: 30, 35, 40, 45, 50 degrees
E_Field: varies
11
Event display & hitmap

## Slide 12
T02 X
T02 Y
T03 X
T03 Y
T06 X
T06 Y
Tracker Gas: Ar(93%)+CO2(7%), VMM=550 V
12

## Slide 13
Rotate RICH so the Cherenkov light can reach the CsI+THGEM plate
The ionization signal is used to check the spatial resolution.
σx~1.2mm
σy~1.0mm
RICH: Ar(93%)+CO2(7%)
Quartz
Rotate: 30 degrees
reversed ~6V/cm drift Field.
1990V/1995V/920V/570V
13
RICH event

## Slide 14
single photon
σθ~32mrad
nph~1.699
H2O/O2
contamination ～90ppm
14
nPh vs. Efield
Gain~1E5
RICH performance (preliminary)

## Slide 15
15
ASIC design for RICH
up to 1.6M channels.
Need: high density, low noise, low power consumption.
Currently used: AGET/VMM
~5fC
~40fC

## Slide 16
协调人：
刘倩/张志永
Purification system
Compact RICH prototype
ASIC/FEE
Radiator, Detector, FEE modular design.
Connect to purification system
FEE on the back of anode
Radiator purification
Gas purification
Large size 600mm×300mm
Micromegas detector
Finished design & emulation.
Charge Sensitive Amplifier
CSA + Switched Capacitor Array
ALICE
16
Next Plan

## Slide 17
Polar coverage: 21° < θ < 35°
Position: 1.2 < Z < 1.4 m
Segmentation in φ: 12-fold
Segmentation in Z: 1
Detector thickness: ~15%
Radiator: Quartz
Two options: DIRC/FTOF
17
Endcap Conceptual design

## Slide 18
PID separation vs. time resolution
40ps @ 1.2m is needed for 3σ 2GeV/c π/K separation.

## Slide 19
Chromatic error
19
DIRC/FTOF Timing

## Slide 20
Thickness：15mm
DIRC coverage：21-35°
Focusing part coverage：35-38°
MCP-PMT number：20
MCP-PMT size：45mm×45mm
Anode number：8×64
Anode size：0.7mm×5.6mm
~30 photons
20
Focusing design
DIRC design

## Slide 21
DIRC PID Capability from fast simulation
π/Κ 5σ separation @ 2GeV/c, 3 σ separation @ 5GeV/c
21

## Slide 22
FTOF design
Thickness：15mm
DIRC coverage：21-35°
MCP-PMT number：3x18
MCP-PMT size： 27.5×27.5×16.6 mm3
Anode number：4×4
Anode size：5.5mm×5.5mm
Z = 1400 mm - 1600 mm
R = 560 mm – 1050 mm
No focusing component
22

## Slide 23
Time resolution from single photon (calculation)
Time resolution (simulation)
FTOF time resolution
23

## Slide 24
Time resolution from G4 simulation
 16
From G4 simulation <12ps， Total timer resolution <50ps。

## Slide 25
2GeV π reconstruction
Number of P.E. ~ 30
σLOP~3.3 mm
Single p.e. ~100 ps
2GeV π/K 4σ separation
PID capability from simulation
PDF
π/Κ @ 2GeV/c, 4.36σ separation achieved.
25

## Slide 26
26
Background simulation
Physics background & Beam related backgrounds
Background sampled accordingly, within 50ns time window.
Considering the background contribution, 4.21σ separation can be achieved for 2GeV/c π/Κ.

## Slide 27
FEE
HV Board
HV Board
Cooling : Air Circulation
HVBoard
BackPlane
SwitchBoard
— Signal
— Crosstalk
crosstalk ratio~2%
27
533mm
295mm
15mm
454mm
  Preparing quartz: 454mm*533mm*15mm
  MCP-PMT *8
  128 channel readout
Prototype

## Slide 28
28
Cosmic ray telescope for FTOF
Trigger2 scintillator
Tracker 6 MicroMegas (X+Y)
  Strip：384×0.4 mm
  AGET Readout
Resolution: ~140 um
Efficiency > 90%
Tracker
Tracker
Tracker
Tracker
Tracker

## Slide 29
Light absorption & reflectivity
Laser：405, 515,640 nm photonics
29
Quartz optical parameters measurement

## Slide 30
Summary
STCF PID requires 2GeV/c π/K/p separation.
Baseline design: RICH for Barrel & FTOF/DIRC for Endcap.
RICH: C6F14 radiator + hybrid MPGD detector.
FTOF: fused silica + MCP-PMT.

## Slide 31
Thanks for your attention!