## Slide 1: Super Tau-Charm @ Hefei: Concept, Status and Prospects
Qing Luo
National Synchrotron Radiation Laboratory
University of Science and Technology of China
中国科学技术大学，国家同步辐射实验室
罗箐

## Slide 2: Outline
Goal and Preliminary Concept of the Accelerators
  Design Goal
  How to achieve high polarization beams
Key Technologies
  General Description
  Examples: Impedance & Vertical Emittance Measurement, etc.
Prospects
  Hefei Integrated National Science Center
  A Test Facility for Future Super Tau-Charm
  What’s next?

## Slide 3: What’s HIEPA?
A High Luminosity e-e+ Collider @ 2-7GeV
  Luminosity: ×1035cm-2s-1 @ 4GeV (center of mass)
  Beam Energy Range: 1-3.5GeV
  Polarization: >80% longitudinal e- @ IP
    With possibility to upgrade to polarized e+ e- collision
  May provide 3rd generation synchrotron
Symmetric Dual-ring, with Linac injection
  Full energy linac, no booster, easy to alter beam energy
  Also provide possible X-FEL and other test facility
Notes: N1，N2 are the number of particles in the two colliding bunches.
Σ，respectively, the convoluted horizontal and vertical bunch size at the IP. 卷积尺寸，两束团分别尺寸的平方和的平方根
[1]The hourglass effect and the measurement of the transverse size of colliding beams by luminosity scans, M. Venturini and W. Kozanecki , Stanford Linear Accelerator Center, Stanford University, Stanford, CA 94309
[2]Concept of luminosity, Werner Herr and Bruno Muratori∗ CERN, Geneva, Switzerland ∗ now at Daresbury Laboratory, United Kingdom
  优化在特定能量下的对称环形对撞机 ℒ^∗=(γ𝑛_𝑏 𝐼_𝑏)/(2𝑒𝑟_𝑒 𝛽_𝑦^∗ ) 𝜉_𝑦 𝐻

## Slide 4: Parameters and Plans
Accelerator Parameters
Parameters | 1 | 2
Circumference/m | ~600 | ~600
Beam Energy/GeV | 2 | 2
Current/A | 1.5 | 2
E/nm·rad | 5/0.05 | 5/0.05
β Function @ IP /mm | 100/0.9 | 67/0.6
Collision Angle(full θ)/mrad | 60 | 60
Tune Shift | 0.06 | 0.08
Hour-glass Factor | 0.8 | 0.8
Luminosity/×1035cm-2s-1 | ~0.5 | ~1.0
Parameters | 1 | 2
Circumference/m | ~600 | ~600
Beam Energy/GeV | 2 | 2
Current/A | 1.5 | 2
 | 5/0.05 | 5/0.05
 | 100/0.9 | 67/0.6
Collision Angle(full θ)/mrad | 60 | 60
 | 0.06 | 0.08
Hour-glass Factor | 0.8 | 0.8
Luminosity/×1035cm-2s-1 | ~0.5 | ~1.0
Steps:
Pilot: 0.5×1035
Nominal: 1.0×1035
Final: Polarized e-
Upgrade: Polarized e+

## Slide 5: Layout
Detector
Interaction Region: Large Piwinski Angle Collision
+Crabbed Waist
Snakes
Crab Sextupole
Wigglers
Injector
Linac
0.5-3.5
GeV
About injector:
  For e+ and e-, no booster, 0.5GeV->1~3.5GeV
  e+, a convertor, a linac and a damping ring, 0.5GeV
  e-, a polarized e- source, accelerated to 0.5GeV
e+0.5GeV
e- 0.5GeV

## Slide 6: Accelerator Design
Design Method
  Design the ring & IR respectively
  Match the lattice function at both sides
  30 DBA cells are enough for a 5nm·rad emittance
    (SSRF, 20 cells, 4 nm, 432 m)
  Iterative Method
Further Discussion
  What if we increase the energy?
  What about the higher order components and tolerance of the magnets? ×0.1‰？
Notes: thousandth

## Slide 7: Accelerator Design
Is MBA Lattice Useful? 1-3.5GeV
  While designing a diffraction limit synchrotron ring ‘HALS’
    Good: smaller emittance and beam size
    Bad: more severe collective effects and smaller dynamic aperture
  Balances all requirements
Could definitely use some help when design the IR
6BA，~600m
Natural ε 50pm·rad
Full Current 400pm·rad
ε∝E2C-3

## Slide 8: To achieve high polarization
Siberia Snakes
  Mini-rotator
    Very large trace bending angle, increases emittance
    Spin resonance
  How many snakes?
  For Energy of 3.5 GeV in future, 7 snakes
Courtesy of Prof. Dong Wang, SINAP
Courtesy of Dr. Anashin, Dr. Aulchenko, et al., BINP Tau Charm Report
Notes: A.W. Chao, Problems in obtaining polarized e+ and e- beams and perspectives for PEP, High-Energy Physics with Polarized Beams and Polarized Targets Volume 38 of the series EXS 38: Experientia Supplementum, p. 15-26, 1981
V. V. Anashin, V.M. Aulchenko, et al., A project of super c-τ factory in Novosibirsk, 2011
https://ctd.inp.nsk.su/c-tau/Project/CDR_en_ScTau.pdf
N1，N2 are the number of particles in the two colliding bunches.
Σ，respectively, the convoluted horizontal and vertical bunch size at the IP. 卷积尺寸，两束团分别尺寸的平方和的平方根
[1]The hourglass effect and the measurement of the transverse size of colliding beams by luminosity scans, M. Venturini and W. Kozanecki , Stanford Linear Accelerator Center, Stanford University, Stanford, CA 94309
[2]Concept of luminosity, Werner Herr and Bruno Muratori∗ CERN, Geneva, Switzerland ∗ now at Daresbury Laboratory, United Kingdom
  优化在特定能量下的对称环形对撞机 ℒ^∗=(γ𝑛_𝑏 𝐼_𝑏)/(2𝑒𝑟_𝑒 𝛽_𝑦^∗ ) 𝜉_𝑦 𝐻

## Slide 9: Polarized e- e+ Source
Polarized Beam Injection
    P0 injection beam polarization
    beam life, equilibrium time
    equilibrium beam polarization
Polarized e- beam
  NEA Photocathode Electron Gun
    Quantum Efficiency vs Polarization
    High Current vs High Quantity of Electric Charge
    QE>1%, P>90%
Notes: Negative electron affinity
N1，N2 are the number of particles in the two colliding bunches.
Σ，respectively, the convoluted horizontal and vertical bunch size at the IP. 卷积尺寸，两束团分别尺寸的平方和的平方根
[1]The hourglass effect and the measurement of the transverse size of colliding beams by luminosity scans, M. Venturini and W. Kozanecki , Stanford Linear Accelerator Center, Stanford University, Stanford, CA 94309
[2]Concept of luminosity, Werner Herr and Bruno Muratori∗ CERN, Geneva, Switzerland ∗ now at Daresbury Laboratory, United Kingdom
  优化在特定能量下的对称环形对撞机 ℒ^∗=(γ𝑛_𝑏 𝐼_𝑏)/(2𝑒𝑟_𝑒 𝛽_𝑦^∗ ) 𝜉_𝑦 𝐻

## Slide 10: Polarized e+ Source
Methods of Polarized e+ Source: from γ ray
  1 Linac & Helical Undulator to Circular Polarized γ
    2008, SLAC, test, 46.6GeV e- 》80%+ polarized 6MeV e+
    2016, DESY, design, 150GeV e- 》 60%+ polarized e+, e->1.5e+
    High energy, long linac, long undulator
    Best yield, but not appropriate for super τ-C, only use for ILC
  2 Compton Backscattering to Circular Polarized γ
    2014, LAL(France), 2GeV e- 》20% γ 》5.1‰ e+/e-，18.9MeV, 35.6% Polarization
Notes: 1979年，前苏联科学家Balakin和Mikhailichenko提出，可以由非极化的电子束通过螺旋型波荡器辐射来获得圆极化γ光，并打靶产生极化束流[25]。这种办法可以充分利用光源领域不断发展的前沿技术，能够获得高亮度的极化束流，因此很快为大家接受。2008年，国际科学家合作在SLAC直线加速器和FFTB验证装置上利用46.6±0.1GeV的电子束获得了纵向极化度达到80%以上的6MeV正电子（以及电子）[26]，证明这种方法完全适用于ILC计划，2016年，DESY为ILC考虑的150GeV驱动极化电子束配置就采用了这一方案，将ILC baseline设计中的147m超导螺旋波荡器再延长73.5m，可以将极化度提高到60%，且满足平均每个驱动电子可以产生1.5个正电子的需求；另外，其正电子产额随能量下降而降低，且能量降低到120GeV时极化度也下降到30-40%[27]。
上述方法要求电子束的能量达到几十乃至上百GeV，建设这样的巨型直线加速器成本很高。对TeV级的巨型对撞机，这个做法有其合理性；但对于几个GeV、周长几百米级别的对撞机就不适宜了。1996年，日本的东京都立大学的Okugi和KEK的Kurihara等提出可以利用非极化的电子束与圆极化激光进行逆康普顿散射（inverse Compton scattering，又称康普顿背散射或反散射，Compton backscattering）来获得圆极化的γ光，从而在KEK的ATF验证装置上打靶获得极化正电子[28]，这对电子束能量的要求大为降低，为紧凑型的正电子源指出了一个重要方向。KEK之后又提出，为了进一步提高产额，可以将逆康普顿散射腔安装在储存环中，并进行多次碰撞[29]。2008年，法国LPNL和俄罗斯BINP合作，为ILC和SuperB按照这一原理设计了（极化）正电子源，其超导直线加速器可使用ERL，用于产生γ光的Radiator既可以是晶体，也可以是康普顿腔；当利用ERL为逆康普顿散射提供1.3GeV电子束，可以获得平均纵向极化度47%、平均能量12MeV的正电子[30]。2014年，法国LAL利用2GeV的电子束获得了20%的γ光子->正电子产额和总计5.1‰的e+/e-产额，正电子平均能量18.9MeV，平均极化度35.6%[31]。
G. Alexander, J. Barley, Observation of polarized positrons from an undulator-based source, Physical Review Letters, Vol 100, 210801, May 2008
A. Vauth, J. List, Beam polarization at the ILC: physics case and realization, Spin Physics (SPIN2014) International Journal of Modern Physics: Conference Series Vol. 40 (2016) 1660003, DOI: 10.1142/S201019451660003X
T. Okugi, Y. Kurihara, et al. Proposed method to produce a highly polarized e+ beam for future linear colliders. Jpn. J. Appl. Phys. Vol 35 Part 1, No.6A, Jun 1996, p.3677-3680康普顿背散射产生γ，再产生纵向极化正电子
S. Araki, Y. Higashi, et al. Conceptual design of a polarised positron source based on laser Compton scattering— a proposal submitted to Snowmass 2005
https://arxiv.org/pdf/physics/0509016.pdf
X. Artrua, R. Chehab, et al., Polarized and unpolarized positron sources for electron–positron colliders, Nuclear Instruments and Methods in Physics Research Section B: Beam Interactions with Materials and Atoms, Vol 266, Issue7, Sept 2008, p. 3868–3875
N1，N2 are the number of particles in the two colliding bunches.
Σ，respectively, the convoluted horizontal and vertical bunch size at the IP. 卷积尺寸，两束团分别尺寸的平方和的平方根
[1]The hourglass effect and the measurement of the transverse size of colliding beams by luminosity scans, M. Venturini and W. Kozanecki , Stanford Linear Accelerator Center, Stanford University, Stanford, CA 94309
[2]Concept of luminosity, Werner Herr and Bruno Muratori∗ CERN, Geneva, Switzerland ∗ now at Daresbury Laboratory, United Kingdom
  优化在特定能量下的对称环形对撞机 ℒ^∗=(γ𝑛_𝑏 𝐼_𝑏)/(2𝑒𝑟_𝑒 𝛽_𝑦^∗ ) 𝜉_𝑦 𝐻

## Slide 11: Polarized e+ Source
Methods of Polarized e+ Source
  3 Polarized e- 》Bremsstrahlung
  Comparison
    Method 1, highest yield and cost, for huge colliders
    Method 3, lowest yield and cost, for small facilities
    2016, Jlab, PEPPo
    8.19 MeV, 85.2% Polarized e-
    6.25 MeV, 82% Polarized e+
    100 MeV-> 75% Polarization Transfer, 10-4 e+/e-
Notes: 第三种产生圆极化γ光子的途径是极化电子束打高Z材料靶产生的轫致辐射（bremsstrahlung）。1997年，俄国的Potylitsin结合1959年Olsen等人的研究结果，指出纵向极化的电子束打薄非晶体靶的轫致辐射中包含圆极化的γ光子，而圆极化的γ光子在同一靶上可以产生正负电子对，这些正负电子对中的高能成分拥有与光子圆极化度接近的纵向极化度，因此可以直接利用极化电子束[32]。2011年，JLab提出根据这种办法在CEBAF注入器上进行验证工作[33]，随后发起了称为PEPPo（The Polarized Electrons for Polarized Positrons）的合作计划，该合作计划涉及美、法多个研究单位，到2016年，报道了由8.19MeV、85.2%极化度的电子束打1mm钨靶，产生6.25MeV、82%极化度的正电子的实验结果，并推测可以用100MeV的电子束获得75%的极化传递效果和10-4e+/e-的产额[34]。显然，这个方法需要的电子束能量更低，装置更紧凑，是一个非常有潜力的选项。
D. Abbott, P. Adderley, et al., Production of highly polarized positrons using polarized electrons at MeV energies, Physical Review Letter, Vol116, 214801, 27 May 2016
N1，N2 are the number of particles in the two colliding bunches.
Σ，respectively, the convoluted horizontal and vertical bunch size at the IP. 卷积尺寸，两束团分别尺寸的平方和的平方根
[1]The hourglass effect and the measurement of the transverse size of colliding beams by luminosity scans, M. Venturini and W. Kozanecki , Stanford Linear Accelerator Center, Stanford University, Stanford, CA 94309
[2]Concept of luminosity, Werner Herr and Bruno Muratori∗ CERN, Geneva, Switzerland ∗ now at Daresbury Laboratory, United Kingdom
  优化在特定能量下的对称环形对撞机 ℒ^∗=(γ𝑛_𝑏 𝐼_𝑏)/(2𝑒𝑟_𝑒 𝛽_𝑦^∗ ) 𝜉_𝑦 𝐻

## Slide 12: Concept Design for a Plasma Injector W. Lu et al., CEPC Workshop, April 17-20, 2017
Linac3
~300MeV
RF gun
Linac1
~200MeV
Linac2
2-4GeV
BC1
FC
PWFA
DB
LPA/photo-gun linac
>100MeV
20nC
e+ Target
Damping ring
BC2
TR=6-12

## Slide 13: Polarized e+ Source
Plasma Wakefield Accelerator (PWFA) as a Booster
  2~3.5GeV -> 40~50GeV, Helical Undulator
  Polarized γ -> Polarized e+
A PWFA-based Polarized e+ Injector
3.5GeV Linac
PWFA
TR=10-20
40~50GeV
  Good:
    High yield for high energy beam
    Relatively low cost
  Weakness
    Low repetition beam
PRL 100, 210801 (2008)
Notes: N1，N2 are the number of particles in the two colliding bunches.
Σ，respectively, the convoluted horizontal and vertical bunch size at the IP. 卷积尺寸，两束团分别尺寸的平方和的平方根
[1]The hourglass effect and the measurement of the transverse size of colliding beams by luminosity scans, M. Venturini and W. Kozanecki , Stanford Linear Accelerator Center, Stanford University, Stanford, CA 94309
[2]Concept of luminosity, Werner Herr and Bruno Muratori∗ CERN, Geneva, Switzerland ∗ now at Daresbury Laboratory, United Kingdom
  优化在特定能量下的对称环形对撞机 ℒ^∗=(γ𝑛_𝑏 𝐼_𝑏)/(2𝑒𝑟_𝑒 𝛽_𝑦^∗ ) 𝜉_𝑦 𝐻

## Slide 14: Collective Effects
For Super Tau-Charm Factory
  High Current; Many Small Bunches
  Low Energy (compared to B factory, FCC-ee/CEPC…)
Collective Effects for Low Emittance Rings
  For Storage Ring: Like 3rd Generation Light Source
  For Collider: Beam-beam Effects
  Single Bunch:
    Microwave instability, Bunch Lengthening, TMCI, IBS, etc.
  Multi-bunch:
    Coupled-Bunch Instability, HOM, Electron Cloud, etc.

## Slide 15: Impedance Study
Purpose
  Estimate and Control the Collective Effects
Methods
  Simulation (CST Studio, etc.)
  Bench Measurement of Coupling Impedance
    Coaxial-wire method measure S-parameters
    For devices with complex structure and NEG-coated chamber
    Junctions and transition sections excite noise; wire thickness; spectrum of higher frequency is hard to measure
  On-line Measurement?
    Tune measurement, use tune vs current to estimate the impedance of the whole ring

## Slide 16: Vertical Size Measurement
Very Small Vertical Bunch Size
  ~1% Coupling, @IP: σx~20μm; σy~0.2μm
  Other point, βx≈1m @BM，σy~1μm
Traditional Method as X-ray Pinhole or FZP
  SR X-ray Image: Diffraction Limit(Fundamental Theory)
  Interferometer: Short SR Wavelength, higher resolution
Method | Detail | Resolution | Price
Image | X-ray Image | ~μm | High
 | X-ray Pinhole | ~10μm | Low
Interferometer | Visible to X-ray | 0.01-1μm | Medium

## Slide 17: Vertical Size Measurement
SR X-ray Interferometer
  Resolution:
  ;
For a X-ray Interferometer of Vertical Beam Size
  ，
  ,

## Slide 18: Vertical Size Measurement
SR X-ray Interferometer
  Picture below shows a UV system for horizontal size system of 1μm resolution
  X-ray needs more optimization and better optical devices
    X-ray multi-layer reflector ;
    X-ray monochrometer (instead of bandpass filter);
    X-ray CCD;
    X-ray polarizing prism;
    etc.

## Slide 19: Other Key Technologies
New injection method
  Top-up injection
  Minimizing injection-induced detector background
Superconducting
Ultrahigh vacuum
Other high precision beam diagnostics
Beam control and feedback system
Power supply, Stability Technology such as Bracing, etc.

## Slide 20: Prospects
Hefei Integrated National Science Center
  A national science center which will play an important part in ‘Megascience’ of China in near future
    Pay a lot of attention to accelerator facilities
    Hefei Advanced Light Source is already under design
    HIEPA is listed in future plan
    10M RMB start fund proved by USTC

## Slide 21: Prospects
National Synchrotron Radiation Laboratory: HLS II
800MeV,
38nm·rad,
4 DBA Cells
Notes: 注入器
  由直线加速器和输运线组成
  加速结构：等梯度
  能量为800MeV
储存环
  能量为800MeV
  发射度38nm·rad
  八个直线段，现安装5台插入件

## Slide 22: Prospects
Hefei Advanced Light Source
  A diffraction limit ring based SR light source
Parameters
Beam Energy | ~2.0 GeV
Circumference | ~600 m
Lattice | 6BA
Natural Emittance | < 50 pm.rad
Current | 500±0.5 mA

## Slide 23: Test Facility for HIEPA?
What kind of facility it should be?
  What to do: Bench Test or Online Test?
    Technique develop and test with beam
  What kind of accelerator: Ring or Linac?
    Mainly linac; tests based on small ring is not that useful for large ring collider; built a ring is more expensive
    Can also provide FEL or other utilities
  What kind of technology should be tested?
    Online: Superconducting, Photocathode Guns, Magnets, etc.
    Bench test: Magnets, Impedance Measurements, Interferometers, etc.

## Slide 24: Test Facility for HIEPA?
How can we achieve that?
  Linac with NEA photoinjector
  Polarized electron directly for polarized positron
    Also can be used in Positron Annihilation Technique
  Compton Backscattering in test facility (or HLS II)
100MeV~2 GeV Linac
Radiator or
Target
NEA Photocathode Gun
e- Test
e+ Test
ERL Loop
Future addition
Notes: LEPD low energy positron diffraction
RHEPD Reflection High Energy Positron Diffraction

## Slide 25: Collaboration Needed
Accelerator Physics
  IR Design
  Polarization: Spin Rotation and Maintenance
  Collective Effects: Simulation and Bench Measurements
  Advanced Computational Accelerator Physics
Accelerator Technologies
  Superconducting Cavities and Magnets
  Polarized Beam Sources
  Ultrahigh Vacuum Chamber with Small Aperture, Optimized Impedance and Low SEE

## Slide 26: Conclusion
Conditions for a super tau-charm factory to be approaching
  Time Window: 2020-2025
  Budget: RMB ~4 Billion
    Apply for support from Central Government of China and local authority
  Short of Faculties and Staffs
  Technologies Readiness: need to be invested
Still a lot of work to do

## Slide 27: Thanks for Attention! 感谢各位！

## Slide 28: Large Piwinski Angle
考虑beam-beam tune shift，有交叉角θ
  ; ;
交叉角θ数值较小（即使“大交叉角”，仍很小）
Piwinski Angle
怎
亮度在某点取次于0点的极大值（1995，平田光司，PRL）
在这种情况下，
“能够达到的”亮度最大值增加了！
Notes: [1]Analysis of Beam-Beam Interactions with a Large Crossing Angle, Kohji Hirata 平田光司* Stanford Linear Accelerator Center, Stanford University, Stanford, California 94309, Volume 74, Number 12 Physical Review Letters 20 March 1995
[2]Test of ‘‘Crab-Waist’’ Collisions at the DAФNE Ф Factory, lots of authors, PRL 104, 174801 (2010) PHYSICAL REVIEW LETTERS

## Slide 29: Crabbed Waist
交叉角对撞引入新的束-束共振，限制tune shift
  synchro-betatron共振（SBR），整数共振
  有交叉角时的束-束相互作用对束-束共振有重要贡献
DAФNE Ф Factory的Crab Waist INFN-LNF, 2010 PRL
  在对撞点两侧合适的相位引入一对Crab六极铁
  抑制共振，提高峰值亮度；增加工作点空间上高亮度区域范围
束-束效应的研究
Notes: 高能所张源：正负电子储存环对撞机中的束束效应研究

## Slide 30: 采用新对撞机制的同类加速器设计
俄罗斯BINP，Super Charm-Tau，2008-2011
Notes: V. V. Anashin, V.M. Aulchenko, et al., A project of super c-τ factory in Novosibirsk, 2011
https://ctd.inp.nsk.su/c-tau/Project/CDR_en_ScTau.pdf
M.E. Biagini, R. Boni, et al., Tau/Charm Factory Accelerator Report, INFN Report INFN-REPORT-INFN-13-13-LNF (INFN, 2013) arXiv:1310.6944 [physics.acc-ph]. 2013

## Slide 31: 采用新对撞机制的同类加速器设计
意大利INFN，Tau-Charm Factory，2013
区别：
意大利的设计仅优化一个指定能量；
俄罗斯的设计需求更长的周长，2倍以上；
意大利的参数，束流品质要求更高，束团长度更短
etc.
类似的还有SuperB/SuperKEKB…
Notes: V. V. Anashin, V.M. Aulchenko, et al., A project of super c-τ factory in Novosibirsk, 2011
https://ctd.inp.nsk.su/c-tau/Project/CDR_en_ScTau.pdf
M.E. Biagini, R. Boni, et al., Tau/Charm Factory Accelerator Report, INFN Report INFN-REPORT-INFN-13-13-LNF (INFN, 2013) arXiv:1310.6944 [physics.acc-ph]. 2013

## Slide 34: 结论
τ-Charm能区高亮度对撞机的可行性
国内外环境与发展现状来看，现实的可能性
  时间
  预算
  人
  技术储备
加速器领域，关键的、有意思的问题非常多
  也包括与其他装置，譬如巨型对撞机/光源等的共性问题