## Slide 1
Preliminary Considerations on Tracking for HIEPA
Yifei Zhang and Jianbei Liu
University of Science and Technology of China
Workshop on Physics at Future High Intensity Colliders @ 2-7GeV in China
USTC, China
January 16, 2015

## Slide 2: HIEPA
Circumference ~ 1000m
Ecm = 2-7 GeV; L = (0.5-1)x1035 cm-2s-1 at 4 GeV, single polarized beam.
A 3rd/4th generation SRF (synchrotron radiation facility).
Potential for FEL( free electron laser) with the long LINAC.
A High Intensity Electron Positron Accelerator
Primary physics requirement on detectors for HIEPA: highly efficient and precise reconstruction of exclusive final states in electron-positron collisions.
Tracking detectors at HIEPA play a central role in the final state reconstruction.
( From Prof. Zhengguo Zhao )

## Slide 3: A glimpse of final states in -c regime
The momenta of charged final-state particles are mostly below 1GeV/c.
Designs of tracking detectors for HIEPA have to match this important feature of final states.
’s from inclusive J/psi decays
Kaon’s from inclusive D0 decays

## Slide 4: Requirements for Tracking System
Large acceptance (close to 4*pi)
High efficiency at momentum down to <~100MeV
Good momentum resolution at momentum <~1GeV
High rate capability
  Fast response
  Radiation hard
Fast and efficient triggering on charged particles
Good transparency to downstream measurements (PID and Ecal)
PID for low-momentum (<600-700MeV) particles
Vertexing (less critical, more on background rejection)
`

## Slide 5: Detector Design Considerations
Dominant factor in tracking performance in tau-charm regime
  multiple scattering
So the driving force in tracking design
  low mass (to be also transparent to downstream measurements)
Special design required for inner tracking
  to cope with the very hostile radiation environment expected at HIEPA
So an inner-outer separate design would be the optimal choice
An outer-tracker option: a drift chamber
  High momentum resolution from low mass plus good spatial resolution
  PID via dE/dx
Inner-tracker options
  Silicon detectors: Pixel/Strip
  MPGD: Cylindrical GEM, Cylindrical MicroMegas, (pixel/strip readout)
  …

## Slide 6: Outer Tracker: Drift Chamber Option
Low mass
  Helium-based working gas
  Aluminum wires
  Carbon-fiber support structure
Small cells
  Fast response
  Small electron diffusion → good spatial resolution
Super-layer arrangement
  Facilitates triggering and reconstruction
Stereo layers
  Z measurement

## Slide 7: Continued
Chamber dimensions
  Rin: beam background
  Rout : cost of EM calorimeter
  Length: acceptance and cost of EM calorimeter
Number of wire layers
  Sufficient enough for both momentum and dE/dx measurements
  Must also balance with material budget
B field
  Balance between momentum resolution and low-pT tracking efficiency

## Slide 8: Low-Mass Drift Chambers
KLOE
Belle
Babar
CLEO-C
• Low mass design
• helium-based working gas
• Al ﬁeld wires (less tension needed -> lighter chamber structure)
• Carbon ﬁber structure (for cylinders or even endplates)
• Typical performance
• spatial resolution: 100-130 um
• momentum resolution: 0.5%@1GeV (1T)
• dE/dx resolution: 5-6% (MIP)

## Slide 9: BESIII Drift Chamber
Could serve as a starting point
Cell size
  1.2cm (inner), 1.6 cm (outer)
# of layers = 43
L~70cm
B = 1 T
He/C3H8 (60/40)
Performance
  Momentum resolution: ~ 0.5% @1GeV
  dE/dx resolution: ~ 6% (MIP)
Square drift cells

## Slide 10: Adapting to HIEPA ?
Enlarge Rin to avoid the very high beam background near IR expected at HIEPA.
Reduce cell size for inner layers to accommodate generally high counting rates in the region at HIEPA.
To further reduce material ?
  No Au coating on Al wires
  Thinner W wires
  A lighter working gas
  Sharing field wires at axial-stereo boundaries

## Slide 11: A Drift Chamber for HIEPA ?
Rin = 15 cm
Rout = 85 cm
L = 2.4 m
B = 1 T
He/C2H6 (60/40)
Cell size =1.0cm(inner),1.6cm(outer)
Sense wire: 20 um W
Field wire: 110 um Al
# of layers = 44
Layer configuration: 8A-6U-6V-6A-6U-6V-6A
Carbon fiber for both inner and outer walls
Expected spatial resolution: ~130 um
Expected dE/dx resolution: 6%

## Slide 12: Standalone Tracking Performance
Outer tracker (the drift chamber) alone
Momentum resolution estimated using empirical formula
σx | 130um
L | 70cm
B | 1T
N | 44
X0 | cm
Inner region | 19209.0
Outer region | 36522.0
Overall | 34942.8
momentum resolution | position measurement | multiple scattering | total
(%) | 0.335 | 0.364 | 0.495

## Slide 13: Inner Tracker Options
Silicon detectors
  Prerequisite for use at HIEPA: low material
  Examples
    STAR heavy flavor tracker
    BELLE2 pixel detector
Cylindrical GEM
  a gaseous detector, low mass intrinsically
  An example
    KLOE2 inner tracker
…

## Slide 14: STAR Heavy Flavor Tracker
MAPS technology
A prototype pixel ladder
SSD: single-layer double-side strips
IST: one layer of strips
PIXEL
  MAPS technique : sensor and signal processing integrated → low material, low power consumption
  pixel pitch: 20 μm *20μm
  2cm*20cm ladder, 10 ladder in total
  double layers

## Slide 15: BELLE2 Pixel Detector
DEPFET Technology
Two layers of PXD: 1.8 cm and 2.2 cm in radius, consisting of 8 and 12 modules for innermost layer and the second, respectively.

## Slide 16: KLOE2 Inner Tracker
X pitch 650μm → X res 190 μm
V pitch 650μm → Y res 350 μm
Material Budget | 
Total 1 layer | 0.49%
Total 4 layers | 1.95%
Pixel readout would be required for the innermost layers at HIEPA
2-d strip readout

## Slide 17: Combining inner and outer trackers

## Slide 18: Combined Tracking Performance
Option1
Option2
Caveat: very rough modeling used on material effect

## Slide 19: Summary
Tracking system for HIEPA
  Outer tracker (main tracker)
    a small-cell drift chamber with helium-based gas and Al wires.
  Inner tracker
    Silicon or GEM? Material still a concern? cost for pixels? …
    Others?
More concrete and serious work needs to be done.

## Slide 20: Backup

## Slide 24: KLOE CGEM