## Slide 1: Potential Options on the PID Detector at HIEPA
Xin Li
Dept. of Modern Physics , USTC
Key State Key Laboratory of Particle Detection and Electronics (USTC-IHEP)
2018/03

## Slide 2: Requirements of PID Detector at HIEPA
Enable /K/p separation up to 2.0GeV/c(3-4)
Suitable for high luminosity run – fast timing
High radiation resistance, especially in the endcap
Compact – reduce costs of the outer detectors
Modest material budget(<0.5X0)
dE/dx in the gaseous tracking detector
example: ~6% at BESIII MDC (track length ~0.7m), clean /K ID for p<0.8GeV/c
/K separation at 0.8~2.0GeV/c, Cherenkov detector and TOF .

## Slide 3: Cherenkov Detector
Cherenkov radiation
Radiation if particle velocity larger than speed of light in medium
Fast timing at high luminosity, two catalogs:
  Threshold Cherenkov
  Imaging Cherenkov: Ring Imaging Cherenkov detector (RICH) or Detection of Internally Reflected Cherenkov light(DIRC)

## Slide 4: BELLE Aerogel Cherenkov Counter (ACC)
A threshold Cherenkov detector (/K) with a TOF
TOF resolution ~90ps, for k/p separation 0.8-2.5GeV/c
n = 1.030, /K separation 0.8-2.5GeV/c
n = 1.010,  /K separation 1.0-3.5GeV/c
Structure simple
Require large space to install
Threshold Cherenkov detector module

## Slide 5: ALICE HMPID
PID by RICH only
Liquid C6F14 radiator n~1.3 @ 175nm
Proximity gap = 80mm
Readout pad size 8mmX8.4mm
>3 σ  /K separation at 3 GeV/c
Already proven:
Large momentum range
Same structure at both the endcap and the barrel
System complicated
HMPID: The High Momentum PID

## Slide 6: LHCb TORCH Project
The TORCH (Time Of internally Reflected Cherenkov light) detector is an innovative high-precision TOF system for -K PID incorporating DIRC methods(DIRC-like TOF) .
Endcap PID detector for high luminosity CERN/LHCb upgrade
Composed of large-area quartz radiator, light reflecting and focusing mirror, and MCP-PMT as readout unit
LHCb simulation: efficiency vs. p
Compact structure
Target resolution is 70 ps per photon to give 10–15 ps per track and provide clear K- separation up to 10 GeV

## Slide 7: TOP for BELLE-II
Time of Propagation (TOP) detector: measuring 3D (x, y, time)
Good single photon detection efficiency
Excellent time reslution (<50 ps)
Pixel size of ~5.3 x 5.3 mm with MCP-PMT readout units
Efficiency >99% at 0.5% pion fake prob. For B->k decay
Compacted structure,
More expensive with a large number of MCP_PMT readout

## Slide 8: DIRC Detector for the PANDA Experiment at FAIR
Photon detectors and electronics
CFRP enclosures
Flat mirror
Radiator bar
Focusing optics
Expansion volume
The PANDA DIRC is a key component of the PANDA PID system: silicon radiator with MCP-PMTs
Two DIRC detectors for hadronic PID
Barrel DIRC:3  π/K separation up to 3.5 GeV/c
Endcap Disc DIRC：4  π/K separation up to 4 GeV/c
Under R&D, successfully validated PID performance in CERN beam tests
Large range of momentum
Focusing optics, structure complicated
~3.6  π/K @ 3.5 GeV/c
~3.4  π/K @ 3.5 GeV/c
Time imaging:
Geometrical reconstruction:

## Slide 9
Dirc-like TOF in Froward Region (FTOF) is an imaging Cherenkov counter which uses to identify charged particles for R@D of SuperB factory
Detector made of 12 quartz sectors at the endcap
The quartz used as Cherenkov radiator and a light guide (DIRC technique)
readout by 14 MCP-PMT SL10 (TTS~40 ps) base line or SiPM candidates
Simple and compact structure
Total time resolution per track between 30 – 40 ps
FTOF at SuperB

## Slide 10: Time of Flight Detector
For K/p at p=2GeV/c, T ~ 0.27ns*X(m) = 270ps at X~1m.
3 K/p separation for overall TOF time resolution is 90ps
For /K at p=2GeV/c, T ~ 0.1ns*X(m) = 100ps at X~1m.
3 /K separation for overall TOF time resolution is ~30ps. This is a
challenge for TOF technology
Fast Timing TOF(<30ps) base on new pico-second timing technology, TOF combined with DIRC method
The 3 separation of TOF :

## Slide 11: Simulation on Fast Timing TOF
Photon
Hit time
Pulse signal
Photon Hit Time
MC(Geant4) Simulation model:
Fused quartz + MCP-MPT readout
Scinitillator(BC420,two layer)with SiPM (or MCP)readout
Threshold: 1pe
Intrinsic time resolution can reach to ~30ps(preliminary results)
Fused quartz
BC420,two layer
Two layer sum-up
One single layer

## Slide 12
Readout: PDA(programmable Differential Amp) LMH6881/2 + DDD(Dual threshold Differential Discriminator) :Low threshold: 28.7mV, High threshold: 390.6mV
Rise time for 3100V readout by PDA
Time resolution: 17.03ps
Rise time for 3100V
readout by oscilloscope
Time resolution:
8.74ps
Fused silica crystal for ultra- violet Cherenkov lights
Hamamastu MCP-PMT（R3089U)
Picosecond Timing TOF Development in USTC
Beam test at CERN H4 Thanks for RD51 group!

## Slide 13: Some New Developments on Double-mesh Micromegas
Single photoelectron detection: A double-mesh Micromegas (DMM) was developed to achieve >106 high gas gain and ~ 0.05% excellently low ion backflow ratio;
2D high spatial resolution measurement: A four-corner resistive array anode readout was verified to be fulfilled with very small amount of electronics channels;
Photoelectron convertor: A Diamond-like Carbon (DLC) photocathode was being studied to replace the fragile CsI.
Schematic of DMM
Four-corner readout
DLC coating on a KAPTON foil
Principle
Resistive pads array
From Dr Z.Y.Zhang

## Slide 14: A DMM prototype and its performance
A 5.9keV x-ray spectrum
Typical pulse height spectrum of single electron
~0.0005 IBF ratio
3 ×106 high gain for single photoelectron
Published on NIM-A：A high-gain, low ion-backflow double micro-mesh gaseous structure for single electron detection，889 (2018) 78–82.
Design diagram for the fabrication of prototype；
Fabricated with a thermal bonding technique, which is originally developed by USTC MPGD group.
From Dr Z.Y.Zhang

## Slide 15: The Four-corner Readout Method
  A 100 × 100mm2 active area prototype;
  Consisting of ~100 10×10mm2 resistive pad array, thus ~ 100 readout nodes；
  Comparing with the typical pixel scheme (2 ×2mm2), the readout channels are significantly reduced with a factor of ~20;
  Better than 250μm good spatial resolution was obtained！
Test with ~8 keV x-ray gun
Total signal
Four corner signals
σ=235um
From Dr Z.Y.Zhang

## Slide 16: Summary
The potential options on the /k/P detector for HIEPA
Experiment | Detector | Material | Technical | Structure
BELLE/ACC | Thres. Cheren. +TOF | Aerogel/PMT | proved | simple/ large space
ALICE/HMPID | RICH(X,Y,θ) | C6F10/MWPC | proved | complex/ larger space
BELLE-II/TOP | DIRC(X,Y,T) | Quartz/MCP | improved | compact/ larger cost
LHCb/TROCH | DIRC-Like TOF | Quartz/MCP | improved | compact larger cost
HIEPA/Opt.1 | RICH/HMPID | C6F10/GEM | Relatively mature | complex/ larger momentum
HIEPA/Opt.2 | DIRC-Like TOF(or TOF <30ps) | Quartz/SiPM | Pico-second Timing R&D | compact lower cost

## Slide 18: Option1 (backup) The baseline design uses the same technique of HMPID in both the barrel and the endcap region. This reduces the complexity of combining different detection methods and the risk to maintain the PID system.
The liquid radiator C6F14 must be kept at high purity. The impurity, especially Oxygen, must be less than 10ppm . This imposes the major technical challenge of the baseline design.
Another important issue is to develop a dedicated CsI doping and testing technique for the GEM foil. Long term stability and aging effect should be thoroughly investigated.
The basic structure is similar to that of the ALICE HMPID, but with MWPC in the photon detection part replaced by triple gaseous electron multiplier (GEM) layers.