## Slide 1
Ingo Deppner
Physikalisches Institut der Uni. Heidelberg
CBM TOF prototypes
STAR Regional Meeting Workshop on STAR upgrades
Daniel CEBRA

## Slide 2
Outline
Test beam time at GSI in Oct. 2014
- Test beam results
Test beam time at CERN in Nov. 2015
- Design consideration for the various prototypes
Test beam time at BNL in Feb. 2017
- Synchronization proposal
Design proposal for eTOF
Summary

## Slide 3
Test beam time @ GSI
Test beam time in October 2014 at GSI (Hades cave)
Sm beam with 1.2A GeV kin. energy
5 mm thick lead target
„Uniform“ illumination of the counter surface
Flux on the lower part of the setup was about few hundred Hz/cm2
Delivered flux does not meet the CBM requirements
THU-Strip
Setup

## Slide 4
MRPC-P2 prototype
Full size demonstrator for high rates (1 - 10kHz/cm2)
Low resistive glass
Spacers (fishing line)
HV electrode (Licron)
Pickup electrode
27 x 32 cm2

## Slide 5
Full size demonstrator and reference MRPC used for the performance analysis MRPC-P2 (HD) THU-strip (Beijing) MRPC-P5 (HD) MRPC differential differential differential glass stack single double single active area 32 x 27 cm2 24 x 27 cm2 15 x 4 cm2
strips 32 24 16
strip / gap 7/ 3 7/ 3 7.6 / 1.8 mm
glass type low resistive glass low resistive glass low resistive glass
glass thickness 0.7 mm 0.7 mm 1.0 mm
number of gaps 8 2 x 4 6
gap width 220 mm 250 mm 220 mm
Test beam time @ GSI
MRPC-P2 THU-strip MRPC-P5

## Slide 6
Results
Efficiency > 98 %
Resolution  62 ps
Efficiency > 96 %
Resolution  65 ps
Differential singel stack MRPC with 8 gaps
Differential double stack MRPC with 2 x 5 gaps
vs.
Data points at 11 kV in the left plot can be compared with 5.5 kV in the right plot.
Single stack MRPC shows slightly better efficiency and time resolution.
Single counter resolution is in the order of 45 ps including all electronic components.

## Slide 7
Results
Differential single stack MRPC with 8 gas gaps
Differential double stack MRPC with 2 x 5 gas gaps
vs.
In a triggered setup there is no major difference in the performance between both counter types.
However, in a free running mode an impedance matched MRPC should give a better performance due to minimized signal reflections.

## Slide 8
Test beam time @ CERN
Cave specially build for our test beam time

## Slide 9
Test beam time @ CERN
Test beam time in Nov. 2015 at CERN
Lead beam with 30A GeV kin. Energy
Beam intensity about 108 / spill
Spill length of about 15 s
2 mm thick lead target
Estimated flux of about few kHz/cm2
Delivered flux probably still does not meet the CBM requirements
Setup in Feb. 2015
Beam
Upper setup
Lower setup

## Slide 10
Channel count
Group | Counter | # MRPCs | Channels
Bucharest | Strip counter Buc2012 | 4 | 256
Bucharest | Strip counter Buc2015a/b | 2 | 128
Bucharest | Strip counter Buc2010 (reference) | 1 | 128
Tsinghua | PAD counter | 3 | 48
Tsinghua | Strip counter | 4 | 256
USTC | Strip counter | 4 | 256
Heidelberg | Strip counter P2 | 1 | 64
Heidelberg | Strip counter P5 (reference) | 1 | 32
GSI | Diamond strip 2x16 | 2 | 32
 | Total # | 20 | 1200
About 17% of eTOF and about 1% of CBM

## Slide 11
Possible setup
1. Buc. 2012, 4 MRPC (same) 2. Buc. 2015, 1 MRPC single stack 1 MRPC double stack 3. Tsinghua Pad, 3 MRPC (same) 4. Buc. Reference, 1 MRPC nar. Strip 5. Tsg. strip, 3 MRPC, double stack 6. Tsg. strip, 1 MRPC single stack USTC strip, 2 MRPC, single stack 7. USTC strip, 2 MRPC, double stack 8. HD strip, 1 MRPC single stack 9. HD Ref, 1 MRPC, single stack
1
2
3
4
6
7
8
9
5
Beam

## Slide 12
MRPC design of Bucharest
Prototype | 2015a | 2015b
# strips | 40 | 40
Strip length / cm | 9.6 | 9.6
Pitch / mm | 7.2 | 10.1
# Gaps | 2 x 5 | 8
Gap size / m | 140 | 140
Impedance /  |  100 |  100
Glass | low res. | low res.
HV | Metal | Metal
What is new? - 1 Prototype (2015a) with a double stack matched to 100  impedance and a changed strip width - 1 Prototype (2015b) with a single stack matched to 100  impedance and a changed strip width
2015a
2015b

## Slide 13
MRPC design of Tsinghua
Prototype | A | B | C | D
# strips | 32 | 32 | 32 | 32
Strip length / cm | 27 | 27 | 27 | 27
Pitch / mm | 10 | 10 | 10 | 10
# Gaps | 2 x 4 | 2 x 4 | 2 x 4 | 8
Gap size / m | 250 | 250 | 220 | 220
Impedance /  |  50 |  50 |  50 |  100
Glass | low res. | low res. | low res. | low res.
HV | Col. carbon | Col. carbon | Col. carbon | Col. carbon
What is new? - All 4 prototypes with fully new designed readout electrode (number of strips, signal routing - prototype B equal to prototype A but with gas sealing - the readout electrode of prototype C is designed in HD however with the counter design from Tsinghua - single stack has the design of the Heidelberg prototype but with HV supply method of Tsinghua

## Slide 14
MRPC design of Tsinghua
Single stack
double stack
double stack (Heidelberg prot.)
- single stack MRPC has by construction a fully equal signal path length - signal path length is in one of the double stack prototypes not equal - strips due to HV supply not symmetric (two prototypes)

## Slide 15
2 MRPC concepts
Differential singel stack MRPC with 8 gaps
Differential double stack MRPC with 2 x 4 gaps
Advantages - lower High Voltage (< 6 kV) - smaller cluster size
Disadvantages - more complex construction - merging of signals leads to reflections in the counter - more glass plates (#10) - impedance matching hardly possible (100)
Advantages - simpler construction - symmetric signal path - fewer glass plates (#9) - lower weight - impedance matching easy possible (100)
Disadvantages - higher High Voltage (> 10 kV) - bigger cluster size
vs.

## Slide 16
MRPC design of USTC
Prototype | A | B | C | D
# strips | 32 | 32 | 32 | 32
Pitch / mm | 10 | 10 | 10 | 10
# Gaps | 2 x 6 | 2 x 6 | 12 | 12
Gap size / m | 140 | 140 | 140 | 140
Impedance /  |  50 |  50 |  100 |  100
Glass | float | float | float | float
HV | Col. carbon | Metal | Col. carbon | Metal
What is new?  more details in Yongjie’s talk - All 4 prototypes with fully new designed readout electrode (number of strips, signal with, signal routing - prototype B equal to prototype A but different HV connection (Bucharest design) - the same for prototype C and D, they are additionally sealed

## Slide 17
MRPC design of Heidelberg
 | P2 | P5
# strips | 32 | 16
Strip length / cm | 27 | 4
Pitch / mm | 10 | 9.7
# Gaps | 8 | 8
Gap size / m | 220 | 220
Impedance /  | 100 | 100
Glass | low res. | low res.
HV | Col. carbon | Res. Kapton
What is new? - HV electrodes in both prototypes - Prototype P2 has colloidal carbon painted on Kapton foil (instead of Licron) - Prototype P5 has a new low resistive Kapton foil, with surface resistivity of 5 M/

## Slide 18
HV electrode
Bucharest design: Metal strips connected with resistors superimposing the readout strips on an additional PCB
Tsinghua design: Colloidal graphite painted on the glass facing to the readout strips. Resistive layer and readout strips are separated via isolating foil.
USTC design: Colloidal graphite painted on the glass. Readout strips are facing to the honey comb. Resistive layer and readout strips are separated via PCB material.
Heidelberg design 1: Colloidal graphite painted on a Kapton foil facing to the glass. Kapton foil acts also as insulator between resistive layer and readout strips.
Heidelberg design 2: Resistive Kapton foil (5 M/) on top of the glass. Resistive layer and readout strips are separated via isolating foil.
Currently 5 methods to apply HV exist

## Slide 19
Goals
Efficiency, time resolution, rate capability of the new prototypes
Single stack vs. double stack: Which is the best solution?
Impedance matching: is it so important? Can we solve this issue in a triggered system?
HV electrode: 5 solution on the market! Which is the most optimal?
Gas diffusion problem: Is sealing the way to go?
What we expect to learn from this beam time?

## Slide 20
Module design for STAR
Design is the same as in the CBM TOF TDR
Box size 102 x 49 x 11 cm3
Module is suppose to be a full size demonstrator for STAR
During the CERN beam time in Nov. 2015, 3 of this chambers housing 3 MRPCs each will be tested
One of the modules will be tested in Feb. 2017 at BNL
a
b
c
a: MRPC (MRPC3a/b) b: PADI (Preamplifier) c: Crate with GET4 (TDC) d: HV, gas and ground feed-though e: gas tight chamber
d
e

## Slide 21
CBM TOF electronic chain
Free running DAQ
MRPC Module connect to PADI with crate for TDC
cupper
optic
ROB = first concentration stage
GBTx = second concentration stage
DPB = third concentration stage
max 4 x ROB
next ROB (max 4x)
TOF-ROB
optic
direct connection to DPB
without GBTx
optic
PC
FLIB
Clock
240 MHz
160 MHz
120 MHz from CBM
cupper
Sync

## Slide 22
Electronic chain in Feb 2017
optic
PC
FLIB
TOF-ROB
cupper
optic
Free running DAQ
Clock
160 MHz
40 MHz from STAR HPTDC
Sync
240 MHz
Trigger signal from STAR
FPGA board
Sync
Trigger number
How to synchronize the TDCs?
(proposal from Heidelberg/GSI)

## Slide 23
Electronic chain in Feb 2017
optic
PC
FLIB
TOF-ROB
cupper
optic
Free running DAQ
Clock
160 MHz
inject 9.4 MHz from STAR to both TDC systems
Sync
240 MHz
FPGA board
Sync
Trigger number
How to synchronize the TDCs?
(proposal from Geary)
Trigger signal from STAR
HPTDC

## Slide 24
Goals
Get to know the STAR environment
Space constrains at the east pole side: Is there enough space for 3 module layers? Do the electronic crates have enough space or do we have to find other solutions?
How to synchronize the TDCs?
How to merge the data?
How to calibrate the data?
Can we do already now PID?
What we expect to learn from this beam time?

## Slide 25
STAR
Space for additional Time-of-Flight detectors

## Slide 26
End-cap design
Interaction point in collider mode
Interaction point in fix target mode
3 layers
36 CBM-TOF modules
108 MRPC3a/b
6912 readout channels
About 10 m2 active area
CBM-TOF module

## Slide 27
Summary
Summary
The design of the differential single stack MRPC from Heidelberg is driven by the free- streaming readout  impedance matching is realized.
The single stack MRPC shows slightly better efficiency and time resolution in comparison to a double stack MRPC.
Single counter resolution is in the order of 45 ps including all electronic contributions. However this value was achieved in a low rate environment.
Both types of MRPC detectors fulfill the CBM ToF requirements. However, in a free running mode an impedance matched MRPC might show a better performance due to minimized signal reflections.
In the next beam time 20 MRPCs with about 1200 channels will be tested. Based on these results a decision on the design will be taken.
A full size module for STAR will be built and installed in STAR in summer 2016
The main goal of the Feb. 2017 test run is the synchronization and merging the data of both subsystems.
Thank you for your attention

## Slide 28
Backup
80 W
1 ns
Backup Slides

## Slide 29
Backup Slides
CBM Physics topics
Deconfinement / phase transition at high ρB
QCD critical endpoint
The equation-of-state at high ρB
chiral symmetry restoration at high ρB
Observables
excitation function and flow of strangeness and charm
collective flow of hadrons
particle production at threshold energies
excitation function of event-by-event fluctuations
excitation function of low-mass lepton pairs
in-medium modifications of hadrons (ρ,ω,φ → e+e-(µ+µ-), D)
non twisted part
connector
p
p
K
D. Kresan Au + Au @ 25GeV
Kaon acceptance depends critically on TOF resolution

## Slide 30
Incident particle flux
URQMD simulated charged particle flux for Au + Au (minimum bias) events at 25 AGeV assuming an interaction rate of 10 MHz
kHz/cm2
Flux ranging from 0.1 to 100 kHz/cm2
At different regions MRPC counters with different rate capabilities are needed

## Slide 31
Engineering design of the CBM experiment
TOF
TRD
RICH
Magnet
Nominal ToF position is between 6 m and 10 m from the target
Movable design allows for optimization of the detection efficiency of weakly decaying particles (Kaons)
Backup Slides

## Slide 32
Counter occupation
80 W
1 ns
Active area of overlain counters
D.u.t. MRPC-P2: 32 x 27 cm2
Reference MRPC-P5: 15 x 4 cm2
Plastic: 8 x 2 cm2

## Slide 33
Backup
80 W
1 ns
Cut 1
Cut 3
HV = 11 kV, Uthr = 200 mV